## Slide 1: JVET-O0551 AHG13: Tool-off tests on Open Images dataset images.
J. Ström, D. Saffar, P. Wennersten and R. Sjöberg
VISTA
ER DRI
2019-01-31

## Slide 2: CTC test sequences not very varied
18 sequences, every 8th image used
Many images similar
This contribution is about what happens when the test data is more varied
first frame
last frame

## Slide 3: Open Images dataset
A dataset of ~9 million still images
Used for training neural networks
We had downloaded parts of it already so we thought we could try it on VVC.

## Slide 4: Pros and cons
Disadvantages:
  Compressed images, not raw
  Images, not frames from video
    Different characteristics; less motion blur, more “artistic” background blur etc.
  No manual scrubbing of data
    May contain text-overlay
    May be almost monochrome
Advantage
  Varied, good for stress-testing

## Slide 5: Selection of images
The Open Images dataset consists of a long list of URLs to jpeg images
Some of these have heavy compression artifacts and are not good for testing
We downloaded them and tested the quality setting value (between 0 and 100)
  We only used images of quality setting 99 (second highest)
Some images only have one channel -> discard
Some images are 4-channel CMYK images -> discard
Some images are larger than 4k-resolution -> discard
Some images are smaller than 1920*1080 pixels -> discard
We cropped the center 1920x1080 section of the remaining images.

## Slide 6: Test set parts
We created 5 parts of the test set
  Part0: 235 images: used for all tools
  Part1: 242 images: used for backup
  Part2: 218 images: used for backup
  Part3: 271 images: used for backup
  Part4: 243 images: used for backup

## Slide 7: Tool-off results (positive number means tool gives loss when turning off)
Test | Description | Acronym | BDR-Y 235 images | CTC BDR-Y
1 | Chroma separate tree | CST | 0.61% | 0.41%
2 | Dependent quantization/sign data hiding | DQ | 2.14% | 1.90%
3 | Cross-component linear model | CCLM | 1.70% | 1.85%
4 | Multiple transform set | MTS | 0.99% | 0.84%
5 | Adaptive loop filter | ALF | 2.19% | 2.42%
6 | Multi-line reference prediction | MLRP | 0.18% | 0.36%
7 | Intra sub-partitioning | ISP | 0.24% | 0.31%
8 | Matrix based intra prediction | MIP | 0.41% | 0.36%
9 | Low frequency non-separable transform | LFNST | 0.88% | 1.26%
10 | Sample adaptive offset | SAO | 0.41% | -
11 | Luma mapping with chroma scaling | LMCS | -0.22% | 0.81%

## Slide 8: Backup test on luma mapping
Test part | Number of images in test set part | BDR-Y change when LMCS is turned off | CTC tool off test
0 | 235 | -0.22% | 
1 | 242 | -0.24% | 
2 | 218 | -0.15% | 
3 | 271 | -0.19% | 
4 | 243 | -0.22% | 
summary: | 1209 (sum) | -0.21% (average) | +0.81% (average)

## Slide 9: New software from Dolby JVET-O0432
Test part | BDR-Y change when LMCS is turned off, compared to an anchor using JVET-O0432
0 | 0.06%
1 | 0.04%
2 | 0.01%
3 | 0.03%
4 | 0.01%
summary: | 0.03% (average)

## Slide 10: New software from Dolby JVET-O0432 (cont.)
In the new test, the tool is turned off 93% of the time.
When talking to the proponents, they mentioned that it is turned off for full range, since it is not possible to get gains for full range data.
We converted our test set from full range to video range and re-ran our test.
Test part | BDR-Y change when LMCS is turned off, compared to an anchor using JVET-O0432
0 | 0.65%

## Slide 11: Tool off chroma
Test | Description | Acronym | BDR-U no BW | BDR-V no BW | AHG13 BDR-U | AHG13 BDR-V
1 | Chroma separate tree | CST | 18.10% | 18.63% | 12.73% | 13.50%
2 | Dependent quantization | DQ | 0.64% | 0.38% | -0.94% | -0.95%
3 | Cross-component linear model | CCLM | 25.91% | 23.27% | 17.20% | 17.54%
4 | Multiple transform set | MTS | 0.55% | 0.40% | 0.37% | 0.42%
5 | Adaptive loop filter | ALF | 3.55% | 4.09% | 2.73% | 3.06%
6 | Multi-line reference prediction | MLRP | 0.11% | -0.08% | 0.16% | 0.18%
7 | Intra sub-partitioning | ISP | 0.21% | 0.02% | 0.25% | 0.25%
8 | Matrix based intra prediction | MIP | 0.22% | 0.08% | 0.10% | 0.14%
9 | Low frequency non-separable transform | LFNST | 0.22% | -0.03% | 0.39% | 0.55%
10 | Sample adaptive offset | SAO | 0.18% | 0.24% | - | -
11 | Luma mapping with chroma scaling | LMCS | -0.58% | -0.65% | -1.20% | -0.98%
old LMCS code