## Slide 1
JVET-O0575:CE7-related: Reduction for Context Coded Bins in Transform Skip Mode
Weijia Zhu, Li Zhang, Jizheng Xu, Kai Zhang, Hongbin Liu

## Slide 2: Motivation
The maximum number context coded bins per block/per sample is set for TS blocks
To maintain a high CABAC throughput, It is desired to further reduce the number of context coded bins for TS blocks.

## Slide 3: Proposed method
Propose to further limit the number of context coded bins for TS blocks based on block size and coded mode.
  The number of context coded bins is limited to 1.5 bins per sample of IBC and BDPCM blocks with block size larger than 16.
  The number of context coded bins is limited to 1.75 bins per sample for other blocks.

## Slide 4: Simulation Results
The simulation is conducted followed the CE7 test condition
VTM5 is employed as the benchmark
CTC QPs = {22,27,32,37} and Low QPs = {2,7,12,17} are tested

## Slide 5: Simulation Results-Cont.
AI | Y | U | V | EncT | DecT
Class TGM | 0.53% | 0.45% | 0.45% | 100% | 115%
Class F | 0.25% | 0.26% | 0.07% | 101% | 129%
RA | Y | U | V | EncT | DecT
Class TGM | 0.31% | 0.34% | 0.23% | 101% | 121%
Class F | 0.18% | 0.14% | 0.25% | 101% | 140%
AI | Y | U | V | EncT | DecT
Class TGM | 0.92% | 0.77% | 0.76% | 99% | 108%
Class F | 0.29% | 0.21% | 0.26% | 100% | 115%
RA | Y | U | V | EncT | DecT
Class TGM | -2.67% | 0.54% | 0.58% | 100% | 118%
Class F | 0.75% | 0.22% | 0.15% | 99% | 124%
CTC QPs
Low QPs

## Slide 6: Simulation Results-Cont.
CTC QPs
Low QPs
 |  | Max – Bin2Bit Ratio | TRF of Max – Bin2Bit Ratio | Avg TRF – Bin2Bit Ratio | Avg – Bin2Bit Ratio
AI | TGM | -2.20% | -1.27% | -0.91% | -2.09%
 | Class F | -0.81% | -0.28% | -0.38% | -1.03%
RA | TGM | -2.40% | -0.45% | -0.57% | -1.43%
 | Class F | -1.11% | -0.88% | -0.52% | -0.96%
 |  | Max – Bin2Bit Ratio | TRF of Max – Bin2Bit Ratio | Avg TRF – Bin2Bit Ratio | Avg – Bin2Bit Ratio
AI | TGM | -3.06% | -0.97% | -0.94% | -2.98%
 | Class F | -1.36% | -0.38% | -0.47% | -1.37%
RA | TGM | -2.96% | -0.75% | -0.64% | -2.41%
 | Class F | -1.98% | -0.32% | -0.38% | -1.32%

## Slide 7: Conclusions
Proposed to further limit number of context coded bins for TS blocks based on block size and coded mode to enhance the throughput.
We recommend adopting the proposed method into next version of VVC draft.