## Slide 1
CE9-related:
Complexity Reduction
for BDOF Parameters Calculation
JVET-O0612

## Slide 2: BDOF (Bi-Direction Optical Flow)
BDOF adds correction to bi-direction MC
  Base MV derived from bitstream and DMVR (if applicable)
  Only apply to luma channel
4-step process to compute BDOF predictor
  SAD based early termination
  Gradient and BDOF parameters calculations
  4x4 level MV calculation used to compute pixel level offset
  Pixel level offset for bi-direction MC to obtain BDOF predictor

## Slide 3: Extended CU Region in BDOF
Horizontal and Vertical gradients of every pixel in a padded CU, 10x10 for a 8x8 CU, is computed
MV for each 4x4 subblock (red square) in a CU is computed using gradients in 6x6 surrounding region (green dashed square)

## Slide 4: Block BDOF Parameters Calculation in VTM-5.0
5 parameters for auto- and cross- correlation of pixel gradients needed to compute 4x4 level MV
Block parameters are sum of the 5 parameters for all pixels in 6x6 surrounding region

## Slide 5: Proposed Method
Compute BDOF parameter for each 4x4 block using gradients from pixels within 4x4 block
Block parameters are sum of the 5 parameters for all pixels in 4x4 block

## Slide 6: Simulation Results

## Slide 7: Conclusions
Compute BDOF parameters from gradients and pixel differences within 4x4 block
Reduce 5 additions (one per each BDOF parameter) per number of removed pixel
Reduce number of additions from 36x5 (6x6 gradients in current design) to 16x5 (4x4 gradients in proposed method)
Total number of reductions is 100 (20x5) for every 4x4 block in a CU
Padding step to store gradient information at CU level is not needed