## Slide 1: Non-CE3: On signalling of intra coded blocks
L. Pham Van, G. Van der Auwera, A. K. Ramasubramonian, V. Seregin, H. Huang, M. Karczewicz
@qualcomm
07/2019
AV

## Slide 2: Introduction to VTM5.0 intra mode signaling
To detect a regular intra coded block, MIP, MRL and ISP flags are decoded with possibly 16 conditional checks.
Prob. if an intra block is regular is high (72.8%).
 Many redundant checks
mpm_flag
mpm_idx
mrl_idx
mip_mode
isp_flag
0
>0
1
mip_flag
1
isp_mode
PL_flag
mpm_idx
PL
remainder
0
PL
PL_flag
mpm_idx
1
Regular mode at very end of the syntax
0
0
0
1
Flag | Conditional check
MIP | if(sps_mip_enabled_flag&&(Abs(Log2(width)−Log2(height))<=2)&&width<= MaxTbSizeY && height<=MaxTbSizeY )
MRL | sps_mrl_enabled_flag && ( ( y0 % CtbSizeY ) > 0)
ISP | if(sps_isp_enabled_flag&&intra_luma_ref_idx[x0][y0] == 0 && (width <= MaxTbSizeY &&height<=MaxTbSizeY )&&(width*height > MinTbSizeY * MinTbSizeY ) )
MPM | if( intra_luma_ref_idx[x0][y0] == 0 && intra_subpartitions_mode_flag[x0][y0] = = 0)

## Slide 3: Test 1: MPM flag before MRL
isp_flag
remainder
mpm_flag
mip_mode
mrl_index
1
0
1
mip_flag
>0
mpm_idx
PL
1
PL
PL_flag
mpm_idx
1
0
0
0
mpm_idx
isp_mode
PL_flag
0
0
1
+ Pros: No need signal ISP and MRL for Remainder mode
- Cons: Need to signal MPM flag for ISP and MRL

## Slide 4: Test 2: regular MPM flag before MIP
Regular MPM mode = regular intra + prediction mode in MPM
mpm_idx
reg_mpm_flag
remainder
mrl_idx
mip_mode
0
1
isp_flag
0
>0
1
0
mip_flag
1
mpm_idx
PL_flag
PL
1
0
0
PL
mpm_idx
0
1
isp_mode
PL_flag
+ Pros: No need signal ISP, MRL, MIP for regular MPM blocks
- Cons: Need to signal regular MPM flag for MIP, ISP, MRL blocks.

## Slide 5: Test 3: regular intra flag
mpm_idx
mpm_idx
reg_intra_flag
PL
remainder
mrl_idx
mip_mode
0
1
PL_flag
0
>0
1
0
mip_flag
0
PL_flag
mpm_idx
mpm_flag
PL
0
1
1
0
1
isp_mode
+ Pros: No need signal ISP, MRL, MIP for regular blocks
Many redundant checks are removed
Clean and logical design
4 contexts to encode reg_intra_flag:
ctxIdx = min(3, (Log2(w) + Log2(height) – 4) / 2 )
ISP flag is removed

## Slide 6: Test 4: Regular intra flag + MPM mode signalling change
Regular intra flag as in Test 3 with 2 contexts:
ctxIdx = (Log2(w) + Log2(height) – 4) / 5
MPM mode signalling modification
  Planar and first bin of MPM index are encoded using 2 contexts:
    ctxIdx = top is Planar || left is Planar
    Planar check unifies with Planar check in MPM list derivation: not Intra || (is Intra and Planar) ||is MIP

## Slide 7: Test 5: Combination of Test 4 and JVET-O0925

## Slide 8: Conclusions
Several signalling designs for intra mode coding.
Performance can be improved further by CABAC retraining
Regular intra flag at the beginning of the syntax:
Clean design
Remove redundant checking
 It is recommended to adopt regular intra flag to the next version of VTM.