## Slide 1: JVETO0671: Simplified intra chroma mode coding
Bappaditya Ray, Geert Van Der Auwera, Marta Karczewicz
JVET

## Slide 2: Proposal 1
Motivation: VTM-5 draft associates DM_CHROMA with pred_mode = 4 for sps_cclm_enabled_flag=0, and pred_mode=7 for sps_cclm_disabled_flag=1.
Proposal:
Keep DM_CHROMA=4 for both cases (a single table is sufficient).

## Slide 3: Proposal 2
VTM-5 uses different binarization table for sps_cclm_enabled_flag 0 and 1.
Value of intra_chroma_pred_mode | Bin string
4 | 0
0 | 100
1 | 101
2 | 110
3 | 111
Value of intra_chroma_pred_mode | Bin string
7 (DM_CHROMA) | 0
4 (LM_CHROMA) | 10
5 (LM_L) | 1110
6 (LM_T) | 1111
0 (PLANAR) | 11000
1 (VERTICAL) | 11001
2 (HORIZONTAL) | 11010
3 (DC) | 11011
Value of intra_chroma_pred_mode | Bin string
4 (DM_CHROMA) | 00
0 (PLANAR) | 0100
1 (VERTICAL) | 0101
2 (HORIZONTAL) | 0110
3 (DC) | 0111
5 (LM_CHROMA) | 10
6 (LM_L) | 110
7 (LM_T) | 111
Proposing single binarization table:
For sps_cclm_enabled_case=0, the first bin should be inferred to be zero (not to be coded).

## Slide 4: Comparison of number of bins
Value of intra_chroma_pred_mode | Original Bins | Proposed Bins | deltaBins
4 (DM_CHROMA) | 0 | 00 | +1
0 (PLANAR) | 11000 | 0100 | -1
1 (VERTICAL) | 11001 | 0101 | -1
2 (HORIZONTAL) | 11010 | 0110 | -1
3 (DC) | 11011 | 0111 | -1
5 (LM_CHROMA) | 10 | 10 | 0
6 (LM_L) | 1110 | 110 | -1
7 (LM_T) | 1111 | 111 | -1
1 extra bin for DM_CHROMA, same bins for LM_CHROMA, and 1 reduced bin for 6 other modes

## Slide 5: Context design for binarization
Value of intra_chroma_pred_mode | Bin string
4 (DM_CHROMA) | 00
0 (PLANAR) | 0100
1 (VERTICAL) | 0101
2 (HORIZONTAL) | 0110
3 (DC) | 0111
5 (LM_CHROMA) | 10
6 (LM_L) | 110
7 (LM_T) | 111
Context 1: regular or LM, Context 2: DM_CHROMA or not. Context 3: LM_CHROMA or not.
Uses 3 contexts like the original chroma coding
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 0 | na | 1 | bypass | bypass | na | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 1 = = 0 | 0 | 1 | bypass | bypass | na | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 1 = = 1 | 0 | 2 | bypass | na | na | na

## Slide 6: Results
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.13% | -0.28% | 100% | 100%
Class A2 | 0.00% | -0.09% | -0.03% | 100% | 102%
Class B | 0.00% | -0.12% | -0.11% | 100% | 101%
Class C | 0.00% | -0.13% | -0.03% | 100% | 96%
Class E | 0.00% | 0.04% | -0.12% | 101% | 98%
Overall | 0.00% | -0.09% | -0.11% | 100% | 99%
Class D | -0.01% | 0.04% | -0.05% | 99% | 101%
Class F | -0.01% | -0.05% | -0.12% | 99% | 96%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.47% | -0.31% | 98% | 100%
Class A2 | 0.01% | 0.14% | 0.04% | 101% | 103%
Class B | 0.03% | -0.27% | -0.50% | 97% | 97%
Class C | -0.04% | -0.33% | -0.29% | 102% | 102%
Class E |  |  |  |  | 
Overall | 0.00% | -0.24% | -0.30% | 99% | 100%
Class D | 0.06% | -0.50% | 0.08% | 102% | 103%
Class F | -0.02% | -0.03% | 0.03% | 100% | 101%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.16% | -0.29% | 101% | 101%
Class C | -0.01% | -0.16% | -0.41% | 100% | 107%
Class E | 0.10% | -0.05% | -0.35% | 100% | 103%
Overall | 0.02% | 0.00% | -0.35% | 100% | 103%
Class D | 0.00% | -0.69% | 0.39% | 101% | 93%
Class F | 0.02% | -0.19% | -0.30% | 97% | 93%

## Slide 7
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.13% | -0.28% | 100% | 100%
Class A2 | 0.00% | -0.09% | -0.03% | 100% | 102%
Class B | 0.00% | -0.12% | -0.11% | 100% | 101%
Class C | 0.00% | -0.13% | -0.03% | 100% | 96%
Class E | 0.00% | 0.04% | -0.12% | 101% | 98%
Overall | 0.00% | -0.09% | -0.11% | 100% | 99%
Class D | -0.01% | 0.04% | -0.05% | 99% | 101%
Class F | -0.01% | -0.05% | -0.12% | 99% | 96%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.47% | -0.31% | 98% | 100%
Class A2 | 0.01% | 0.14% | 0.04% | 101% | 103%
Class B | 0.03% | -0.27% | -0.50% | 97% | 97%
Class C | -0.04% | -0.33% | -0.29% | 102% | 102%
Class E |  |  |  |  | 
Overall | 0.00% | -0.24% | -0.30% | 99% | 100%
Class D | 0.06% | -0.50% | 0.08% | 102% | 103%
Class F | -0.02% | -0.03% | 0.03% | 100% | 101%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.16% | -0.29% | 101% | 101%
Class C | -0.01% | -0.16% | -0.41% | 100% | 107%
Class E | 0.10% | -0.05% | -0.35% | 100% | 103%
Overall | 0.02% | 0.00% | -0.35% | 100% | 103%
Class D | 0.00% | -0.69% | 0.39% | 101% | 93%
Class F | 0.02% | -0.19% | -0.30% | 97% | 93%
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.15% | -0.22% | 100% | 99%
Class A2 | 0.00% | -0.04% | -0.04% | 101% | 101%
Class B | 0.00% | -0.09% | -0.13% | 100% | 101%
Class C | 0.01% | -0.04% | -0.02% | 101% | 96%
Class E | -0.01% | -0.07% | 0.01% | 100% | 99%
Overall | 0.00% | -0.08% | -0.08% | 100% | 99%
Class D | -0.01% | 0.08% | -0.02% | 101% | 102%
Class F | -0.01% | 0.00% | -0.06% | 101% | 102%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.41% | -0.24% | 88% | 95%
Class A2 | 0.04% | 0.02% | 0.10% | 100% | 98%
Class B | 0.01% | -0.06% | -0.25% | 100% | 98%
Class C | -0.01% | -0.13% | -0.16% | 98% | 102%
Class E |  |  |  |  | 
Overall | 0.00% | -0.13% | -0.15% | 97% | 99%
Class D | 0.03% | -0.10% | 0.34% | 101% | 101%
Class F | -0.01% | -0.07% | 0.06% | 95% | 81%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.53% | -0.18% | 112% | 78%
Class C | 0.04% | -0.07% | -0.23% | 100% | 96%
Class E | 0.08% | 0.63% | 0.88% | 99% | 95%
Overall | 0.03% | 0.35% | 0.07% | 104% | 88%
Class D | 0.08% | 0.65% | 0.64% | 100% | 96%
Class F | 0.00% | -0.35% | 0.00% | 100% | 96%
O0671
O0416

## Slide 8: Conclusion
Simplification of intra chroma mode coding and VVC draft.
  The proposal uses a single binarization for cclm enabled and disabled case.
  Same intra_chroma_pred_mode=4 for cclm enabled and disabled.
Minor chroma gain is achieved.