## Slide 1: O0673: Harmonized MIP/CCLM boundary downsampling
T. Biatek, G. Van der Auwera and M. Karczewicz
JVET 15th

## Slide 2: Motivation
Current VVC specification includes downsampling of luma neighboring samples for:
  MIP : as vectorized input for matrix-vector multiplication
    Use simple averaging on samples
  CCLM : to estimate linear model parameters
    Use up to 6-tap filter
This proposal:
  Harmonize MIP/CCLM downsampling of luma neighboring samples
  Simplify downsampling of luma neighboring samples in CCLM

## Slide 3: Proposed harmonization
Invoked down-sampling process for CCLM is replaced by MIP’s one for luma boundaries
Rest of CCLM process remains unchanged:
  (W’,H’) derivation for LM / LM-A / LM-L
  (α,β) parameters derivation
  Inner luma sample interpolation with filtering selection for type-0 and type-2 contents

## Slide 4: Performance overview (1)
Over VTM5, SDR CTC
 | All Intra Main10 |  |  |  | 
 | Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.11% | 0.85% | 0.94% | 101% | 98%
Class A2 | 0.04% | 0.21% | 0.04% | 100% | 101%
Class B | 0.02% | 0.21% | 0.33% | 100% | 102%
Class C | 0.06% | 0.48% | 0.49% | 100% | 101%
Class E | 0.00% | 0.01% | 0.00% | 100% | 102%
Overall | 0.04% | 0.34% | 0.36% | 100% | 101%
Class D | 0.03% | 0.23% | 0.15% | 99% | 101%
Class F (optional) | 0.13% | 0.73% | 0.83% | 102% | 102%
 | Random Access Main 10 |  |  |  | 
 | Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.15% | 0.43% | 0.89% | 102% | 99%
Class A2 | 0.04% | 0.40% | 0.15% | 101% | 101%
Class B | 0.02% | 0.54% | 0.43% | 100% | 98%
Class C | 0.01% | 0.47% | 0.30% | 101% | 103%
Class E |  |  |  |  | 
Overall | 0.05% | 0.47% | 0.43% | 101% | 100%
Class D | 0.05% | 0.56% | 0.31% | 99% | 99%
Class F (optional) | 0.09% | 0.67% | 0.70% | 103% | 95%
 | Low delay B Main10 |  |  |  | 
 | Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | 0.19% | 0.51% | 101% | 95%
Class C | 0.02% | 0.31% | -0.02% | 103% | 104%
Class E | -0.01% | -0.28% | 0.77% | 102% | 102%
Overall | 0.01% | 0.11% | 0.40% | 102% | 100%
Class D | 0.03% | -0.07% | 0.94% | 101% | 105%
Class F (optional) | 0.00% | 0.14% | 0.10% | 103% | 96%
 | Low delay P Main10 |  |  |  | 
 | Over VTM5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | -0.01% | 0.62% | 101% | 102%
Class C | 0.00% | 0.04% | 0.28% | 103% | 105%
Class E | -0.02% | 0.24% | 0.11% | 102% | 103%
Overall | 0.00% | 0.07% | 0.38% | 102% | 103%
Class D | 0.07% | 0.09% | 0.09% | 100% | 102%
Class F (optional) | 0.09% | 0.53% | 0.76% | 104% | 96%

## Slide 5: Performance overview (2)
Over VTM5, HDR for type-2 content (see M0142)
  sps_cclm_colocated_chroma_flag = 1
 | All Intra |  |  |  |  |  |  |  |  | 
 | Over VTM-5.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | #VALUE! | #VALUE! | 0.12% | 1.60% | 3.40% | 0.12% | 1.43% | 2.96% | 100% | 101%
Class H2 |  |  |  |  |  | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Overall | #VALUE! | #VALUE! | 0.12% | 1.60% | 3.40% | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-5.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | #VALUE! | #VALUE! | 0.07% | 1.99% | 2.75% | 0.08% | 1.93% | 2.37% | 99% | 103%
Class H2 |  |  |  |  |  | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Overall | #VALUE! | #VALUE! | 0.07% | 1.99% | 2.75% | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 6: Conclusion
We propose unified MIP/CCLM downsampling of luma neighboring samples
Performance shows evidence that unification is possible at a reasonable cost:
  AI: .04% / .34% / .36%
  RA: .05% / .47% / .43%
  LDB: .01% / .11% / .40%
  LDP: .00% / .07% / .38%
We recommend to conduct a CE on that topic.
Thanks to InterDigital for crosschecking our contribution.