## Slide 1: JVET-O0888 AHG10: Adaptive Coding Sub-set for encoder optimization
Madhukar Bhat
Jean-Marc Thiesse
Didier Nicholson
David Gommelet

## Slide 2
JVET-O0888
To bring an additional flexibility to the encoder side for handling underuse of the full standard capacity: Adaptive Coding Subset (ACS)
Why:
  Underuse of specific tools is common in the implementation of hardware and software encoders, in order to meet a given speed/power consumption target/processing capabilities…..
  It has an impact on the coding efficiency but this impact can be reduced by adapting syntax
  Coding efficiency gains are also expected in CTC by adapting to content/bit-rates.
Introduction

## Slide 3: Proposal: overview
Add signalization of sub-set at PPS and slice (or APS) level:
pps_adaptive_coding_subset_enabled_flag
Two subset construction modes are proposed:
  Decimation: PARAM_acs_decimation_factor_minus1.
  Explicit: PARAM_acs_explicit_num, PARAM_acs_explicit_subset.
Can be applied to coding parameters with multiple choice: SAO offsets, intra modes, merge candidates, SAO EO class…
JVET-O0888

## Slide 4: Proposal: overview
Benefits:
  Limits the signalization overhead when an encoder doesn’t implement all the choices of a tool.
  Picture level optimization to adapt to content (2-pass, histogram).
  Reduce corner-case situation.
Design principle:
  No impact on decoding process: candidate generation for the max number, then use mapping table.
  Small impact on parsing.
JVET-O0888

## Slide 5: Application to SAO offsets: syntax
adaptive_coding_subset_data() { | Descriptor
if( sps_sao_enabled_flag ) { | 
sao_acs_mode | u(1)
if(sao_acs_mode = = 0) { | 
sao_luma_acs_decimation_factor_minus1 | u(2)
if( ChromaArrayType != 0 ) | 
sao_chroma_acs_decimation_factor_minus1 | u(2)
} | 
else if (sao_acs_mode = = 1) { | 
sao_luma_acs_explicit_num | ue(v)
sao_luma_acs_explicit_subset | ue(v)
if( ChromaArrayType ! = 0 ) { | 
sao_chroma_acs_explicit_num | ue(v)
sao_chroma_acs_explicit_subset | ue(v)
} | 
} | 
} | 
} | 
JVET-O0888

## Slide 6: Application to SAO offsets: decoding process
JVET-O0888
If pps_adaptive_coding_subset_enabled_flag is equal to 0:
SaoOffsetVal[ cIdx ][ rx ][ ry ][ 0 ] = 0 for( i = 0; i < 4; i++ ) SaoOffsetVal[ cIdx ][ rx ][ ry ][ i + 1 ] = ( 1 − 2 * sao_offset_sign[ cIdx ][ rx ][ ry ][ i ] ) * (7‑126) sao_offset_abs[ cIdx ][ rx ][ ry ][ i ]
Else if pps_adaptive_coding_subset_enabled_flag is equal to 1 and sao_acs_mode is equal to 0:
SaoOffsetVal[ cIdx ][ rx ][ ry ][ 0 ] = 0 for( i = 0; i < 4; i++ ) SaoOffsetVal[ cIdx ][ rx ][ ry ][ i + 1 ] = ( 1 − 2 * sao_offset_sign[ cIdx ][ rx ][ ry ][ i ] ) * (7‑126) (sao_offset_abs[ cIdx ][ rx ][ ry ][ i ] << (cIdx = = 0 ? (sao_luma_acs_decimation_factor_minus1 + 1) : (sao_chroma_acs_decimation_factor_minus1 + 1))
Otherwise if pps_adaptive_coding_subset_enabled_flag is equal to 1 and sao_acs_mode is equal to 1:
SaoOffsetVal[ cIdx ][ rx ][ ry ][ 0 ] = 0 for( i = 0; i < 4; i++ ) SaoOffsetVal[ cIdx ][ rx ][ ry ][ i + 1 ] = ( 1 − 2 * sao_offset_sign[ cIdx ][ rx ][ ry ][ i ] ) * (7‑126) (cIdx = = 0 ? sao_luma_acs_explicit_subset[ sao_offset_abs[ cIdx ][ rx ][ ry ][ i ] ] : sao_chroma_acs_explicit_subset[ sao_offset_abs[ cIdx ][ rx ][ ry ][ i ] ])

## Slide 7: Application to intra mode
else{ | 
for(sizeId = 0; sizeId < 6; sizeId++) { | 
intra_acs_mode[ sizeId ] | u(1)
if(intra_acs_mode[ sizeId ] = = 0) { | 
intra_luma_acs_decimation_factor_minus1[ sizeId ] | u(2)
if( ChromaArrayType != 0 ) | 
intra_chroma_acs_decimation_factor_minus1[ sizeId ] | u(2)
} | 
else if (intra_acs_mode[ sizeId ] = = 1) { | 
intra_luma_acs_explicit_num[ sizeId ] | ue(v)
intra_luma_acs_explicit_subset[ sizeId ] | ue(v)
if( ChromaArrayType ! = 0 ) { | 
intra_chroma_acs_explicit_num[ sizeId ] | ue(v)
intra_chroma_acs_explicit_subset[ sizeId ] | ue(v)
} | 
} | 
} | 
} | 
} | 
Decimation mode for intra
JVET-O0888

## Slide 8: Results: SAO ACS decimation
JVET-O0888
 | All Intra |  |  |  | 
 | Over EncoderApp_SAO_decimation.exe |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,02% | -0,04% | -0,14% | 103% | #DIV/0!
Class A2 | 0,01% | -0,12% | -0,11% | 100% | #DIV/0!
Class B | 0,00% | -0,06% | -0,08% | 99% | #DIV/0!
Class C | 0,03% | -0,19% | -0,24% | 95% | #DIV/0!
Class E | 0,01% | -0,08% | -0,09% | 101% | #DIV/0!
Overall | 0,01% | -0,10% | -0,13% | 99% | #DIV/0!
Class D | 0,02% | -0,09% | -0,09% | 103% | #DIV/0!
Class F (optional) | -0,02% | -0,26% | -0,29% | 104% | #DIV/0!
 | Random Access |  |  |  | 
 | Over EncoderApp_SAO_decimation.exe |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
Class A2 | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
Class B | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
Class C | 0,02% | -0,09% | -0,05% | 106% | #DIV/0!
Class E |  |  |  |  | 
Overall | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
Class D | 0,16% | 0,19% | 0,37% | 100% | #DIV/0!
Class F (optional) | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
 | Low delay B |  |  |  | 
 | Over EncoderApp_SAO_decimation.exe |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,03% | 0,30% | -0,09% | 110% | #DIV/0!
Class C | 0,06% | -0,47% | -0,81% | 102% | #DIV/0!
Class E | 0,23% | 0,13% | -0,59% | 102% | #DIV/0!
Overall | 0,09% | 0,00% | -0,46% | 105% | #DIV/0!
Class D | 0,15% | -0,34% | 0,56% | 99% | #DIV/0!
Class F (optional) | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
Decimation factor | getTLayer()=0 |  | getTLayer()=1 | getTLayer()=2 | getTLayer()>2
 | I_SLICE | B_SLICE |  |  | 
0 | QP <= 24 |  |  |  | 
2 for chroma |  |  | QP < 35 | QP < 38 | 
2 for luma and chroma | QP > 24 | All QP | QP >= 35 | QP >= 38 | All QP

## Slide 9: Results: SAO ACS explicit
 | All Intra |  |  |  | 
 | Over EncoderApp_explicit_offsets_optimized.exe |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,00% | -0,04% | -0,09% | 100% | #DIV/0!
Class A2 | 0,00% | -0,05% | -0,04% | 100% | #DIV/0!
Class B | 0,00% | -0,03% | -0,04% | 100% | #DIV/0!
Class C | 0,01% | -0,09% | -0,11% | 94% | #DIV/0!
Class E | 0,02% | -0,03% | -0,02% | 101% | #DIV/0!
Overall | 0,01% | -0,05% | -0,06% | 99% | #DIV/0!
Class D | 0,02% | -0,03% | -0,02% | 111% | #DIV/0!
Class F (optional) | -0,03% | -0,22% | -0,24% | 102% | #DIV/0!
 | Low delay B |  |  |  | 
 | Over EncoderApp_explicit_offsets_optimized.exe |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,03% | 0,12% | -0,14% | 103% | #DIV/0!
Class C | 0,07% | -0,10% | -0,44% | 101% | #DIV/0!
Class E | 0,35% | 0,37% | -0,71% | 101% | #DIV/0!
Overall | 0,12% | 0,11% | -0,38% | 102% | #DIV/0!
Class D | 0,19% | -0,17% | 0,47% | 100% | #DIV/0!
Class F (optional) | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
 | Random Access |  |  |  | 
 | Over EncoderApp_explicit_offsets_optimized.exe |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
Class A2 | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
Class B | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
Class C | 0,05% | -0,02% | 0,07% | 104% | #DIV/0!
Class E |  |  |  |  | 
Overall | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
Class D | 0,19% | 0,14% | 0,27% | 99% | #DIV/0!
Class F (optional) | #VALEUR! | #VALEUR! | #VALEUR! | #DIV/0! | #DIV/0!
JVET-O0888
SAO offset subset = {0,1,4,8,16,31}.
Anchor = VTM5.0
Small chroma gain with complexity reduction (6 offsets instead of 32)

## Slide 10: Results: intra modes
 | Random Access |  |  |  | 
 | Over VTM_3.0_Intra67_19_all.exe |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.40% | 0.09% | -0.49% |  | 
Class A2 | -0.27% | -0.43% | -0.22% |  | 
Class B | -0.48% | -0.63% | -1.04% |  | 
Class C | -0.44% | -0.41% | -0.44% |  | 
Class E |  |  |  |  | 
Overall | -0.41% | -0.39% | -0.60% |  | 
Class D | -0.44% | -0.79% | -0.93% |  | 
Class F (optional) | -0.57% | -0.89% | -1.78% |  | 
Implemented in VTM 3.0.
Tested: ACS decimation mode with factor 2 (19 intra modes).
Anchor: Reference using 19 modes.
Same number of intra RD tests.
Two sequences gain vs CTC anchor (SlideEditing and SlideShow with -0.83% and -0.32% in luma)
JVET-O0888

## Slide 11: Thank you
The research leading to this work has been supported by the FUI23 EFIGI project, BPIFrance and Region Ile de France.

## Slide 12: Intra modes selection statistics
JVET-O0888

## Slide 13: Results: intra modes ACS vs CTC anchor
JVET-O0888
 | Random Access Main 10 |  |  |  | 
 | Over VTM3_intra67mpm6.exe |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 1.16% | 0.71% | 1.84% |  | 
Class A2 | 1.35% | 1.75% | 2.01% |  | 
Class B | 1.69% | 1.50% | 1.20% |  | 
Class C | 1.71% | 1.82% | 1.55% |  | 
Class E |  |  |  |  | 
Overall | 1.52% | 1.48% | 1.58% |  | 
Class D | 0.84% | 2.35% | 0.52% |  | 
Class F (optional) | 0.66% | 1.21% | 0.25% |  |