## Slide 1
Non-CE7: Context reduction in residual coding
JVET-O1098
Y. Chen, F. Le Léannec, T. Poirier

## Slide 2: JVET-O1098: Context reduction in residual coding
VTM-5.0 transform coefficient coding:
  Context index for parity and gtx flags of Chroma components:
    ctxId (Chroma) =
Current position
Neighboring positions for sumAbsLevel and numSig

## Slide 3: JVET-O1098: Context reduction in residual coding
Context index for parity and gtx flags of Chroma components:
  ctxId (Chroma) =
  Reduces complexity
    no more local template for parity and gtx flags in Chroma TUs
  Saves 24 contexts
CtxId=2
CtxId=1
CtxId=0
For last non-zero

## Slide 4: JVET-O1098: Context reduction in residual coding
 | Random Access Main 10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.07% | 0.34% | 101% | 101%
Class A2 | 0.03% | 0.07% | 0.36% | 101% | 102%
Class B | 0.01% | 0.12% | 0.04% | 100% | 103%
Class C | -0.03% | 0.08% | 0.22% | 100% | 98%
Class E |  |  |  |  | 
Overall | 0.00% | 0.09% | 0.21% | 100% | 101%
Class D | 0.04% | 0.33% | 0.66% | 100% | 100%
Class F (optional) | 0.04% | 0.34% | 0.34% | 100% | 100%
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.29% | 0.33% | 100% | 100%
Class A2 | 0.01% | 0.31% | 0.31% | 101% | 101%
Class B | 0.00% | 0.17% | 0.16% | 101% | 104%
Class C | 0.01% | 0.19% | 0.14% | 101% | 103%
Class E | 0.00% | 0.12% | 0.04% | 100% | 100%
Overall | 0.00% | 0.21% | 0.19% | 101% | 102%
Class D | 0.01% | 0.25% | 0.21% | 101% | 102%
Class F (optional) | 0.00% | 0.31% | 0.31% | 100% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.44% | -0.14% | 102% | 106%
Class C | 0.00% | 0.02% | 0.18% | 102% | 110%
Class E | 0.02% | -0.47% | 1.89% | 101% | 107%
Overall | 0.00% | 0.07% | 0.47% | 102% | 107%
Class D | 0.03% | 0.40% | 0.44% | 101% | 102%
Class F (optional) | 0.01% | 0.48% | -0.26% | 102% | 107%

## Slide 5: Conclusion
It is proposed to reduce the contexts in residual coding
  Reduces 24 contexts in transform coefficient coding
Reduces complexity:
  No more local template for parity and gtx flags in Chroma TUs
Performance:
  Acceptable losses for Chroma components
  No change for Luma component