## Slide 1: Non-CE2: unification of chroma residual scaling design

## Slide 2: Problem
Chroma residual scaling (CRS) is a component of LMCS.
CRS scales chroma residual values by a factor derived from the average value of the corresponding luma prediction block
VTM5.0 design of CRS results in a pipeline latency.
Several non-CE2 contributions intend to address this issue

## Slide 3: CE2-related proposals
Category 1: explicit signalling of the CRS values
  various levels of spatial granularity:
    Slice (O0232 method 2.2)
    NxN CTU (O0429 option1)
Category 2: implicit derivation of the CRS values
  various levels of spatial granularity:
    Slice (O0232 method 1, O0618)
    CTU (O0627)
    VPDU (O0429 option2)
  CTU/VPDU level: use neighboring luma samples of the CTU/VPDU

## Slide 4: Properties of each design
Explicit signalling
  Solves the latency problem
  Removes the chroma-to-luma dependency
  Signalling overhead (at maximum CTU granularity seems to be needed)
    using one single CRS value per slice observed to perform well for SDR CTC (some penalty observed for HDR PQ)
Implicit derivation
  Solves the latency problem
  Does not remove the chroma-to-luma dependency
  No signalling overhead enabling better localization of the CRS process
    beneficial for content with large luma variations, such as HDR PQ content

## Slide 5: Proposed solution
SPS-level flag : explicit/implicit CRS
16-pieces LM model signalled in APS, as in VTM5.0
At slice level, the following signalling applies:
  If explicit signalling is used
    CRS values signalled per n×m CTUs
    n, m signalled in slice header
  If implicit derivation is used
    CRS values inferred at VPDU level
    Using 16 top & 16 left VPDU neighboring luma samples
Applies for both Dual Tree and Single Tree

## Slide 6: Experiments - SDR
explicit signalling (nxm > #CTUs in one slice) is used

## Slide 7: Experiments – HDR PQ
implicit derivation on VPDU level is used
LQP off / LMCS on versus LQP off/LMCS on
proposal

## Slide 8: Conclusions
The proposed unified design for Chroma Residual Scaling eliminates pipeline dependency
Explicit signalling and implicit derivation of CRS values are supported
Applies both for Dual Tree and Single Tree cases
Allows taking benefits from the 2 options depending on the content
Significant chroma performance improvement compared to VTM5.0 anchor