## Slide 1: Non-CE3：Fixed downshifting for 8-bit MIP
Junyan Huo, Yanzhuo Ma, Fuzheng Yang (Xidian Univ.) Kenji Kondo, Masaru Ikeda, Teruhiko Suzuki (Sony) Shuai Wan (NPU) Yuanfang Yu (OPPO)

## Slide 2: Downshifting in MIP
predMip[ x ][ y ] =
( () + oW ) >> sW ) + pTemp[ 0 ]
(8‑69)
Proposed:
predMip[ x ][ y ] =
( () + oW ) >> 6 ) + pTemp[ 0 ]
(8‑69)

## Slide 3: Results over JVET-O0084
 |  |  | All Intra |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | 0.09% | 100% | 100%
Class A2 | 0.00% | -0.02% | -0.01% | 100% | 100%
Class B | 0.01% | -0.04% | 0.01% | 100% | 100%
Class C | 0.01% | 0.02% | -0.01% | 100% | 100%
Class E | -0.01% | 0.00% | -0.06% | 100% | 100%
Overall | 0.00% | -0.01% | 0.00% | 100% | 100%
Class D | 0.00% | 0.18% | -0.01% | 100% | 100%
Class F | 0.02% | -0.05% | 0.04% | 100% | 100%
 |  |  | Random Access |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.05% | -0.10% | 100% | 100%
Class A2 | 0.02% | 0.06% | -0.07% | 100% | 100%
Class B | 0.00% | 0.01% | 0.10% | 100% | 100%
Class C | -0.01% | 0.00% | -0.31% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.01% | -0.08% | 100% | 100%
Class D | 0.02% | 0.21% | -0.17% | 100% | 100%
Class F | 0.04% | 0.15% | 0.19% | 100% | 100%

## Slide 4: Results over JVET-O0925
 |  |  | All Intra |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | -0.04% | 0.01% |  | 100%
Class C | 0.00% | -0.02% | 0.07% |  | 100%
Class E | 0.00% | 0.00% | -0.07% |  | 100%
Overall |  |  |  |  | 
Class D | 0.00% | 0.07% | -0.08% |  | 100%
Class F | 0.02% | -0.10% | -0.03% |  | 100%
 |  |  | Random Access |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | 0.01% | 0.14% | -0.01% |  | 100%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0.04% | -0.17% | 0.12% |  | 100%
Class F |  |  |  |  | 

## Slide 5: Conclusion
Fix downshifting to 6
Coding performance is maintained
The table of sW can be deleted
Suggest to adopt this proposed method into VVC
Thanks for HHI to plan to cross check

## Slide 6
Thank you