## Slide 1: JVETO1153: Revised simplified intra chroma mode coding
JVET

## Slide 2: Proposal 1
Motivation: VTM-5 draft associates DM_CHROMA with pred_mode = 4 for sps_cclm_enabled_flag=0, and pred_mode=7 for sps_cclm_disabled_flag=1.
Proposal:
Keep DM_CHROMA=4 for both cases (a single table is sufficient).

## Slide 3: Proposal 2
VTM-5 uses different binarization table for sps_cclm_enabled_flag 0 and 1.
Value of intra_chroma_pred_mode | Bin string
4 | 0
0 | 100
1 | 101
2 | 110
3 | 111
Value of intra_chroma_pred_mode | Bin string
7 (DM_CHROMA) | 0
4 (LM_CHROMA) | 10
5 (LM_L) | 1110
6 (LM_T) | 1111
0 (PLANAR) | 11000
1 (VERTICAL) | 11001
2 (HORIZONTAL) | 11010
3 (DC) | 11011
Value of intra_chroma_pred_mode | Bin string
4 (DM_CHROMA) | 00
0 (PLANAR) | 0100
1 (VERTICAL) | 0101
2 (HORIZONTAL) | 0110
3 (DC) | 0111
5 (LM_CHROMA) | 10
6 (LM_L) | 110
7 (LM_T) | 111
Proposing single binarization table:
For sps_cclm_enabled_case=0, the first bin should be inferred to be zero (not to be coded).

## Slide 4: Comparison of number of bins
Value of intra_chroma_pred_mode | Original Bins | Proposed Bins | deltaBins
4 (DM_CHROMA) | 0 | 00 | +1
0 (PLANAR) | 11000 | 0100 | -1
1 (VERTICAL) | 11001 | 0101 | -1
2 (HORIZONTAL) | 11010 | 0110 | -1
3 (DC) | 11011 | 0111 | -1
5 (LM_CHROMA) | 10 | 10 | 0
6 (LM_L) | 1110 | 110 | -1
7 (LM_T) | 1111 | 111 | -1
1 extra bin for DM_CHROMA, same bins for LM_CHROMA, and 1 reduced bin for 6 other modes

## Slide 5: Context selection dependency in VVC draft
For binIdx=3, whether to use bypass or context coding depends on binIdx=2 value.
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 0 | 0 | bypass | bypassss | na | na | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 2 = = 0 | 0 | 1 | 2 | bypass | bypass | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 2 = = 1 | 0 | 1 | 2 | 2 | na | na

## Slide 6: Context design for binarization
Value of intra_chroma_pred_mode | Bin string
4 (DM_CHROMA) | 00
0 (PLANAR) | 0100
1 (VERTICAL) | 0101
2 (HORIZONTAL) | 0110
3 (DC) | 0111
5 (LM_CHROMA) | 10
6 (LM_L) | 110
7 (LM_T) | 111
Uses 2 contexts (original chroma coding has 3 contexts).
Removing context selection dependency
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 0 | na | 1 | bypass | bypass | na | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 0 = = 0 | 0 | 1 | bypass | bypass | na | na
intra_chroma_pred_mode[ ][ ] sps_cclm_enabled_flag = = 1 && bin at binIdx equal to 0 = = 1 | 0 | 1 | bypass | na | na | na

## Slide 7: Results
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.15% | -0.19% | 100% | 100%
Class A2 | 0.01% | 0.06% | -0.02% | 99% | 99%
Class B | 0.01% | -0.03% | -0.09% | 100% | 102%
Class C | 0.00% | -0.09% | 0.11% | 99% | 90%
Class E | 0.01% | 0.05% | 0.07% | 99% | 84%
Overall | 0.00% | -0.04% | -0.02% | 99% | 96%
Class D | 0.00% | -0.04% | -0.14% | 100% | 103%
Class F | 0.00% | -0.03% | 0.03% | 100% | 101%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.19% | -0.16% | 99% | 99%
Class A2 | 0.03% | 0.31% | 0.16% | 97% | 97%
Class B | 0.04% | -0.06% | -0.38% | 99% | 98%
Class C | -0.02% | -0.29% | -0.22% | 99% | 90%
Class E |  |  |  |  | 
Overall | 0.01% | -0.08% | -0.19% | 99% | 96%
Class D | 0.06% | -0.31% | 0.02% | 100% | 102%
Class F | 0.01% | 0.02% | 0.07% | 101% | 100%

## Slide 8: Conclusion
Simplification of intra chroma mode coding and VVC draft.
  Same intra_chroma_pred_mode=4 for cclm enabled and disabled.
  The proposal uses a single binarization for cclm enabled and disabled case.
  Uses same context for binIdx=1, independent of binIdx=0 value  removes context selection dependency.
Similar coding performance to VTM-5.0