## Slide 1: JVET-Q0389 Non-CE4: SbTMVP harmonization
Du Liu, Christopher Hollmann, Ruoyang Yu
Ericsson
2020-01-08

## Slide 2: Subblock-based temporal motion vector prediction (SbTMVP)
SbTMVP uses the motion information of a neighboring candidate block to derive the motion information of sub-CUs
Candidate block A1 is used to derive the motion information
The order of candidates in the spatial candidate derivation is B1, A1, B0, A0 and B2
Propose:
Use B1 as the spatial neighbor to derive the motion information for sub-CUs in SbTMVP to align with the spatial neighboring candidate list.
Suggest:
Algorithm description JVET-P2002 assigns different names to neighboring blocks.
Update the algorithm description using the same names for the same blocks as the specification.

## Slide 3: Results
 | Random Access |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.06% | 0.04% | 99% | 98%
Class A2 | 0.00% | 0.00% | 0.02% | 99% | 101%
Class B | 0.00% | 0.05% | 0.02% | 99% | 101%
Class C | 0.01% | 0.02% | 0.06% | 99% | 102%
Class E |  |  |  |  | 
Overall | 0.01% | 0.03% | 0.03% | 99% | 100%
Class D | -0.02% | -0.03% | -0.04% | 99% | 101%
Class F | 0.01% | -0.04% | 0.00% | 103% | 100%
 | Low delay B |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.15% | 0.10% | 97% | 98%
Class C | -0.03% | -0.14% | -0.06% | 98% | 99%
Class E | 0.01% | 0.16% | -0.72% | 98% | 100%
Overall | -0.01% | -0.07% | -0.16% | 98% | 99%
Class D | -0.07% | 0.78% | 0.25% | 99% | 100%
Class F | 0.04% | -0.37% | -0.12% | 97% | 100%

## Slide 4: Conclusions
Propose to use B1 as the spatial neighbor to derive the motion information for sub-CUs in SbTMVP
Align with the spatial neighboring candidate list,
Negligible impact on BD-rate performance 0.01% for RA and -0.01% for LDB
Recommend adopting the proposed method into the next VTM software and VVC working draft.
Thanks to Hikvision for cross-check.