## Slide 1: JVET-Q0390 Non-CE4: SbTMVP simplification
Du Liu, Christopher Hollmann, Ruoyang Yu
Ericsson
2020-01-08

## Slide 2: Subblock-based temporal motion vector prediction (SbTMVP)
Currently
SbTMVP divides a current CU into sub-CUs of size 8x8
8-tap interpolation filter is used for 8x8 subblocks of SbTMVP
6-tap interpolation filter is used for 4x4 subblocks of affine CUs
Propose
Use 6-tap interpolation filter for SbTMVP
Reduce the number of samples to be fetched during interpolation
Align all the subblocks to use the 6-tap interpolation filter
2

## Slide 3: SbTMVP memory bandwidth
Number of samples to be fetched per sample is
8-tap: (8 + 8 – 1) * (8 + 8 – 1) / (8 * 8) ≈ 3.52
6-tap: (8 + 6 – 1) * (8 + 6 – 1) / (8 * 8) ≈ 2.64
Reduction of 1 – 2.64/3.53 = 25%
Filter & prediction | Memory bandwith per sample | Memory bandwidth per CU
8-tap uni | 3.52 | 57,600
6-tap uni | 2.64 | 43,264
8-tap bi | 7.03 | 115,200
6-tap bi | 5.28 | 86,528
The memory bandwidth for a 128x128 CU

## Slide 4: Results
 | Random Access |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.02% | -0.01% | 102% | 100%
Class A2 | -0.01% | -0.02% | 0.04% | 100% | 97%
Class B | 0.02% | 0.03% | 0.01% | 100% | 100%
Class C | 0.05% | 0.01% | 0.06% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | 0.01% | 0.02% | 100% | 99%
Class D | 0.05% | 0.00% | 0.12% | 99% | 100%
Class F | 0.00% | 0.00% | -0.01% | 101% | 100%
 | Low Delay B |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | -0.17% | -0.09% | 100% | 101%
Class C | 0.02% | -0.15% | 0.00% | 103% | 99%
Class E | 0.10% | 0.48% | -0.29% | 101% | 100%
Overall | 0.04% | 0.00% | -0.11% | 101% | 100%
Class D | 0.02% | 0.84% | 0.17% | 102% | 101%
Class F | 0.09% | -0.51% | 0.06% | 97% | 101%

## Slide 5: Conclusions
Propose to use 6-tap interpolation filter for SbTMVP
Reduce the memory bandwidth by 25%
Align all the subblocks to use the 6-tap interpolation filter
Thanks to Nokia for cross-checking.