## Slide 1: JVET-AC0120 Non-EE2: CIIP with more combination candidates

## Slide 2: Introduction
In CIIP mode, the prediction samples are generated by weighting an inter prediction signal and an intra prediction signal;
Two different weighted method are supported:
  The current block is horizontally or vertically divided and the weights of sub-block are assigned according to sub-block index.
  The weight derived by neighboring modes is applied to the entire block.
Inter | intra
regular merge mode (10) CIIP-TM merge mode (2) | planar mode TIMD derived intra prediction mode PDPC method

## Slide 3: Proposed Method
Intra prediction modes list construction
  MPM with sorting
Mapping relationship
  a pair of merge candidate and the intra prediction mode in the list obtained in the first step
Linear model-based weighted method
  The derivation of model parameters is based on the LDL decomposition method same as CCCM.

## Slide 4
Results
 | Random Access Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.05% | 0.00% | #NUM! | #NUM!
Class A2 | -0.03% | 0.03% | 0.15% | #NUM! | #NUM!
Class B | -0.01% | 0.09% | -0.02% | #NUM! | #NUM!
Class C | -0.09% | 0.01% | -0.02% | 102% | 100%
Class E |  |  |  |  | 
Overall | -0.04% | 0.03% | 0.02% | #NUM! | #NUM!
Class D | -0.06% | 0.22% | 0.04% | 102% | 101%
Class F | -0.06% | -0.03% | -0.09% | 103% | 103%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.05% | -0.29% | -0.40% | #NUM! | #NUM!
Class C | -0.14% | 0.12% | -0.36% | 102% | 100%
Class E | -0.12% | 0.69% | -0.13% | 85% | 93%
Overall | -0.10% | 0.09% | -0.32% | #NUM! | #NUM!
Class D | -0.12% | -0.74% | -0.42% | 104% | 100%
Class F | -0.48% | -0.35% | -0.24% | 85% | 93%

## Slide 5: Conclusion
It is proposed to provide more combination candidates for CIIP mode.
On top of ECM-8.0, it achieves
LB {-0.10%, 0.09%, -0.32%}
RA {-0.04%, 0.03%, 0.02%}
It is suggested to investigate in the next round of EE2.
Thanks Bytedance and OPPO for cross-checking!

## Slide 6
THANK
YOU