## Slide 1: JVET-AD0238 On Film Grain Synthesis Subjective Evaluation and Further Work
Xuewei Meng (Disney Streaming)
Wenhao Zhang (Disney Streaming)
Andrey Norkin (Netflix)
Joel Sole (Netflix)
Alberto Duenas (Warner Bros. Discovery)

## Slide 2: Introduction
Film Grain is a type of noise and as such is hard to compress content due to lack of spatial and temporal correlation
Film Grain Synthesis has been an interesting topic since AVC added its support
Film Grain Synthesis importance is currently higher:
  Recent compression formats like VVC can remove redundancy more effectively than AVC, but noise and Film Grain are still as challenging to deal with as it was for AVC needing proportionally greater bit rates
    Leading to limited compression efficiency gains compared to AVC
  The production of content is now mostly done digitally, and the Film Grain is added during the post-production process or synthetically at the camera for artistic purposes
  The adaptive bit rate streaming use case is needing to support much lower bit rates and the Film Grain “preservation” is harder to achieve at low bit rates
    Leading to high artifacts or its removal

## Slide 3: Two use cases for the technology
Artifact masking
  The goal is to help to minimize the compression artifacts introduce but the compression system
Artistic Intent
  The goal is to preserve the subjective characteristics of the Film Grain Noise as designed for the title by the artists
    this is an artistic tool that has extensively been used in the past and still popular on the current creative process
    preserving the look and feel of film grain

## Slide 4: Potential Opportunity
All these items combined present the opportunity to use Film Grain Synthesis for the Artistic Intent use case
  Increase the value of HEVC and VVC based systems
    as they could achieve the expected bit rate reduction when processing content that contain Film-Grain
  Allow for greater quality and resolutions being delivered when using limiting bandwidth systems like internet streaming
    as the available bit rate is not spend to transmit the Film Grain Noise
  Perform synthesis closer to the viewers, allowing additional flexibility

## Slide 5: Understanding from current testing results
It is the understanding of the the authors of this contributions that:
  The current testing and software tools are providing some evidence that FGS can be used for artifact reduction and can deliver satisfactory results for that use case
  The current testing and software tools are offering limited evidence of the value of FGS to support the artistic intend use case
    Without strong evidence the availability of devices that use this technology could be limited
      Greatly influencing the usage of this technique
    Without strong evidence alternatives may appear leading to a greater fragmentation

## Slide 6: Recommendations
This contribution would like to encourage the group to prioritize the use case that tries to preserve the artistic intent at typical streaming bit-rates
  this is considered of great potential
  and it is also a harder goal to achieve
This contribution would like to encourage JVET to further develop the tools that facilitate the usage of the Film Grain Synthesis

## Slide 7: Further Requirements
The following could be some of the steps that could be considered by JVET in this activity:
  Continue development of subjective and objective testing methodologies to evaluate these technologies
    with stronger focus on the artistic intent use case
  Continue development and optimization of the current software tools to be able to utilize the available technologies for Film Grain Synthesis
    With the goal of providing strong evidence of the value of using FGS at the low bit rates used in internet streaming
  Full integration of the available software on https://vcgit.hhi.fraunhofer.de/jvet-ahg-fgt/vfgs into the VTM

## Slide 8: Further Requirements (2)
 | Current VTM | Requirements
Questions for Subjective tests | Focus on Artifact Masking | Careful design of the subjective tests that verifies the techniques preserve the artistic intent. Relevance of the question being asked. Results might differ if we ask for: 1) quality, 2) fidelity to the original 3) preservation of the artistic intent, etc.
Candidates for Subjective tests | Focus on video coding experts or naive viewers | Results might differ depending on to whom the question is being asked : 1) naive viewers 2) video coding experts 3) the artist/director
Input | YUV content file with embedded grain | Either a YUV content file with embedded grain Or/And a YUV clean content file + a YUV grain file
Denoiser | MCTF-based denoiser | An integrated denoiser, with feasibility to turn on and off, and/or change the denoising strengths Or interfaces for 3rd party denoiser

## Slide 9: Further Requirements (3)
 | Current VTM | Requirements
Film grain modeling | Frequency-based film grain modeling | Further increase the adaptability to the content and coding structure Possibly support both the Frequency-based modeling and AR-based modeling Capability to switch between the two types of modeling at least at sequence level. Frame level switching may be a stretching request
Film grain synthesis | Frequency-based film grain synthesis | Possibly support both Frequency-based synthesis and AR-based synthesis Interfaces to test different synthesis settings, such as different pattern sizes, different pattern shapes, and so on