## Slide 1: JVET-AE0047 On GPM-MMVD
Ruoyang Yu
Ericsson
2023-07

## Slide 2: Introduction
In VVC and ECM, the regular merge-MMVD applies MVD on top of merged MV
  The MVD is within a set { ¼-pel, ½-pel, 1-pel, 2-pel, 4-pel, 8-pel, 16-pel, 32-pel }
  The fractional MVDs can be disabled for certain pictures (indicated by a picture header flag)
    In CTC, the fractional MVDs are disabled for 4K sequences
GPM-MMVD applies MVD to merged MV of GPM
  The MVD is within set 0 { ¼-pel, ½-pel, 1-pel, 2-pel, 3-pel, 4-pel, 8-pel, 16-pel }
  or set 1 { ¼-pel, ½-pel, 1-pel, 2-pel, 4-pel, 8-pel, 16-pel, 32-pel }
  The fractional MVDs are always included in the sets

## Slide 3: Proposal
Propose to let GPM-MMVD to follow the regular merge-MMVD to have possibilities of disabling fractional MVDs for certain pictures
  When fractional MVDs are disabled, the magnitude of MVDs within the sets are all multiplied by 4, as done in the regular merge-MMVD

## Slide 4: Results for ECM
CTC (only the 4K sequences in ClassA1 and ClassA2 are affected )
Additional results for screen content
  Disable fractional MVD for regular merge-MMVD based on block hash value matching percentage (i.e., hashBlkHitPerc)
  Further disable fractional MVD for GPM-MMVD
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,01% | -0,18% | -0,02% |  | 
Class A2 | 0,01% | -0,15% | 0,03% |  | 
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0,01% | 0,04% | 0,04% |  | 
Class TGM | -0,03% | -0,04% | -0,04% |  | 
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0,01% | 0,03% | 0,01% |  | 
Class TGM | -0,08% | -0,10% | -0,08% |  | 

## Slide 5: Conclusion
It is proposed to let GPM-MMVD to follow the regular merge-MMVD to have possibilities of disabling fractional MVDs for certain pictures
Thanks to Bytedance for the cross-check

## Slide 7: Results for VTM
Additional results for screen content
  Disable fractional MVD for the regular merge-MMVD based on block hash value matching percentage
 | Random Access Main 10 |  |  |  | 
 | Over VTM-20.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | 0,00% | 0,00% | -0,01% |  | 
Class TGM | -0,09% | -0,12% | -0,09% |  |