## Slide 1: JVET-AE0057 AHG12 MTT split modes early termination
Waqas Ahmad, Per Wennersten, Kenneth Andersson
Ericsson

## Slide 2: Background
ECM encoding runtime is increasing with the progression of each meeting cycle.
Several proposals have been presented to reduce the encoding runtime for ECM.
  Such as JVET-AA0098, JVET-AD0197 , JVET –AD0128, and JVET-AD0105.
This contribution presents an early termination method that is claimed to reduce encoding runtime for ECM with some performance penalty.

## Slide 3
ECM support quadtree with nested multi-type tree partitioning structure.
We propose that a condition is applied on the no-split cost of 64x64 luma CUs.
If the no-split cost is greater than a threshold, MTT splitting will not be investigated.
An exception is made if MTT split has already been selected in parents to the 64x64 CU.
The threshold is set based on QP value as follows:
We present two tests,
  Test1: The proposed condition is applied on all the QPs.
  Test2: The proposed condition is applied to only QP 22.
The scope of this contribution is for camera captured contents.
Proposal
QT
BTH
BTV
TTH
TTV
Nosplit

## Slide 4: Results (Test1)
 | Random access |  |  |  | 
 | BD-rate Over ECM-9.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.03% | -0.04% | 0.07% | 99.7% | 99.8%
Class A2 | 0.04% | 0.01% | -0.02% | 97.0% | 99.6%
Class B | 0.04% | 0.16% | 0.18% | 96.5% | 100.3%
Class C | 0.02% | 0.06% | 0.15% | 95.8% | 99.8%
Class E |  |  |  |  | 
Overall | 0.03% | 0.06% | 0.11% | 97.0% | 99.9%
Class D | -0.04% | -0.01% | 0.06% | 97.3% | 99.9%
Table 1: ECM-RA
 | Low delay B Main 10 |  |  |  | 
 | BD-rate Over ECM-9.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.08% | -0.01% | 0.06% | 96.0% | 100.1%
Class C | 0.04% | -0.16% | -0.19% | 96.3% | 99.6%
Class E | 0.04% | -0.03% | -0.60% | 98.7% | 100.2%
Overall | 0.05% | -0.06% | -0.20% | 96.8% | 100.0%
Class D | -0.14% | 0.11% | 0.61% | 98.1% | 99.9%
Table 2: ECM-LDB
For BQTerrace QP22 anchor data is copied for the Test data

## Slide 5: Results (Test2) Applied to only QP 22
 | Random access |  |  |  | 
 | BD-rate Over ECM-9.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.00% | 0.02% | 0.03% | 99.8% | 99.9%
Class A2 | 0.01% | 0.02% | 0.01% | 98.5% | 100.0%
Class B | 0.00% | -0.02% | 0.02% | 98.6% | 99.8%
Class C | 0.00% | 0.00% | 0.02% | 98.6% | 100.0%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.02% | 98.8% | 99.9%
Class D | 0.00% | 0.02% | -0.03% | 99.5% | 99.6%
Table 1: ECM-RA
Overall EncT & DecT for QP22 are 95.5% , 99.7% respectively
 | Low delay B Main 10 |  |  |  | 
 | BD-rate Over ECM-9.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.04% | 0.05% | 97.6% | 100.1
Class C | -0.01% | -0.03% | 0.00% | 99.1% | 99.9%
Class E | -0.02% | -0.11% | 0.01% | 99.6% | 100.3%
Overall | -0.01% | -0.02% | 0.02% | 98.6% | 100.1%
Class D | -0.01% | 0.12% | -0.06% | 99.6% | 100.2%
Table 2: ECM-LDB
*For BQTerrace QP22 anchor data is copied for the Test data
Overall EncT & DecT for QP22 are 95.5% , 100.4% respectively

## Slide 6
RA worst-case encoding runtime
Over ECM 9.0 Random Access, QP=22 |  |  |  |  |  |  |  |  |  |  |  |  | 
ClassA2 | ECM Enc Time |  | Chunks | ECM Enc time/chunk |  |  | Enc time reduction |  |  |  | Enc time reduction/chunk |  | 
Sequence | [h] | [days] |  | [h] | [days] | [h] |  | [days] | [%] | [h] |  | [days] | [%]
CatRobot1 | 652.03 | 27.17 | 5 | 158.79 | 6.62 | -32.19 |  | -1.34 | -5% | -10.77 |  | -0.45 | -7%
DaylightRoad2 | 949.34 | 39.56 | 5 | 235.32 | 9.81 | -80.9 |  | -3.37 | -9% | -27.36 |  | -1.14 | -12%
ParkRunning3 | 1117.29 | 46.55 | 5 | 251.06 | 10.46 | -43.61 |  | -1.81 | -4% | -8.48 |  | -0.35 | -3%
Table 1: ECM-RA
Over ECM-9.0, Low delay B, QP=22t |  |  | 
ClassA2 | ECM Enc Time | Enc time reduction | 
Sequence | [h] | [h] | %
MarketPlace | 308.09 | -60.18 | -19%
RitualDance | 202.78 | -29.84 | -15%
Cactus | 217.49 | -17.3 | -8%
BasketballDrive | 304.23 | -6.83 | -2%
BQTerrace* (based on 267 frames) | 335 | -16 | -5%
Table 2: ECM-LDB

## Slide 7: Summary
This contribution proposes to adds a criterion based on no-split cost of 64x64 luma CU to early terminate MTT splitting.
Test2 shows on average encoding time reduction for RA and LDB by 4% for QP22 without degrading the overall coding gain.
The worst-case RA & LDB encoding runtime is reduced by 3% and 5% when compared against ECM-9.0.
Thanks to InterDigital for cross-checking.

## Slide 8
Thanks