## Slide 1: AHG12: DIMD Merge JVET-AE0071
Saverio Blasi, Ivan Zupancic, Jani Lainema

## Slide 2
Introduction
When using DIMD, a Histogram of Gradients is computed to predict directionality of template samples.
Up to 5 predictors are blended with Planar mode using weights depending on the HoG amplitudes.
DIMD HoG

## Slide 3
Proposed method - DIMD Merge
When using DIMD Merge, the DIMD modes of neighbouring blocks are used to determine intra-prediction modes for the current block.
In particular, the HoGs extracted from neighbouring blocks are averaged to determine a new merged HoG for the current block.
Current CU
DIMD Merge HoG

## Slide 4
ECM modifications
DIMD Merge is only allowed if there is at least one neighbouring DIMD (or DIMD Merge) block.
In that case, a flag is signalled to determine whether to do normal DIMD or DIMD Merge.
Encoder complexity is minimally changed as the method is tested in a small minority of blocks.
In DIMD Merge blocks, the decoder does not need to do any template-based operations.

## Slide 5
Results
 | All Intra Main10 |  |  |  | 
 | Over ECM-9.0 Full |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | 0.07% | -0.02% | 100% | 102%
Class A2 | -0.11% | -0.06% | -0.04% | 97% | 100%
Class B | -0.07% | 0.05% | 0.05% | 99% | 101%
Class C | -0.06% | -0.01% | 0.10% | 100% | 100%
Class E | -0.06% | -0.01% | 0.24% | 99% | 98%
Overall | -0.08% | 0.01% | 0.07% | 99% | 100%
Class D | -0.03% | -0.08% | 0.21% | 100% | 103%
Class F | -0.08% | 0.02% | 0.12% | 98% | 100%
TGM | -0.01% | -0.03% | 0.04% | 97% | 98%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 Full |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.14% | 0.03% | 101% | #NUM!
Class A2* | -0.05% | -0.02% | -0.07% | 102% | #NUM!
Class B | -0.04% | 0.02% | -0.02% | 100% | #NUM!
Class C | 0.00% | -0.28% | -0.03% | 99% | #NUM!
Class E |  |  |  |  | 
Overall | -0.03% | -0.10% | -0.02% | 100% | #NUM!
Class D | -0.03% | -0.22% | -0.01% | 99% | #NUM!
Class F | -0.02% | 0.06% | -0.03% | 101% | #NUM!
TGM | -0.02% | 0.01% | 0.02% | 98% | 99%
*Two test points in A2 copied from anchor

## Slide 6
Summary
Consistent coding efficiency gains (average -0.08% luma AI gains).
Higher gains in high-res classes A1 (-0.10%) and A2 (-0.11%).
No ET increase.
Proposed to study the technique in the next round of EEs.