## Slide 1: Non-EE2: IBC-LIC Model Merge mode JVET-AE0073
Lai Zhang, Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Introduction
IBC-LIC is an adopted tool in the current ECM. It compensates the local illumination variation within a picture between the CU coded with IBC and its prediction block with a linear equation, that is α*p[x]+β. The parameters of the linear equation are derived by template.
Current block
template
IBC-LIC can be applied to IBC AMVP mode and IBC merge mode. For IBC AMVP mode, an IBC-LIC flag is signaled to indicate the use of IBC-LIC. For IBC merge mode, the IBC-LIC flag is inferred from the merge candidate.
Reference block
template
(α, β)

## Slide 3: Proposed
In addition to derive linear model by template, it is proposed to inherit IBC-LIC model parameters from previously coded blocks. A linear model can be obtained as follows:
Construct a model candidate list, consisting of model parameters from:
  spatial adjacent and non-adjacent neighbors
  history candidates
  default models
Calculate the offset of each model candidate
Select a model from the candidate list and signal its index in the bitstream.
Signaling
  In the IBC-AMVP mode, the flag is signaled when the IBC-LIC flag is true.
  In the IBC-Merge mode, the flag is only signaled when the current block isn’t coded as IBC-CIIP, IBC-GPM, TM-Merge, or skip mode.
  If the flag is true, an index is further signaled.
Current block
B1
B0
A1
A0
B2
Cur
Fig.1 adjacent neighbors
Fig.2 partial of non-adjacent neighbors

## Slide 4: Simulation results
The proposed method is implemented on top of ECM-9.0.
 | All Intra Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.56% | -0.50% | -0.45% | 101.9% | 100.9%
Class TGM | -0.17% | -0.16% | -0.15% | 101.9% | 101.3%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.39% | -0.37% | -0.35% | 100.6% | 102.3%
Class TGM | -0.04% | -0.08% | -0.09% | 101.1% | 102.4%

## Slide 5: Conclusions
The proposed IBC-LIC model merge mode can improve the coding efficiency of ECM with minor complexity increases. It is recommended to further study this method in EE2.
Thanks to Bytedance for cross-checking!