## Slide 1: JVET-AE0075 Non-EE2: On IntraTMP block vector
Yue Yu
Lai Zhang , Luhang Xu, Haoping Yu, Jonathan Gan, Fan Wang, Zhihuang Xie, Dong Wang

## Slide 2: Introduction
Similar to IBC BV, intraTMP BV was adopted for coding future blocks at JVET-AB0061;
Fractional-pel (quarter-pel) intraTMP BV was adopted at JVET-AD0086 which allows reference block indicated by a quarter-pel resolution BV;
Fractional-pel IBC BV was stored in ECM-9.0;
However, full-pel instead of fractional-pel intraTMP BV was stored in ECM-9.0;
IntraTMP BV is not stored at HMVP while IBC BV is stored at HMVP.

## Slide 3: Proposal
To align intraTMP storing with a consistent design;
Fractional-pel instead of full-pel intraTMP BV will be stored;
Fractional-pel intraTMP BV will also be stored at HMVP.

## Slide 4: Simulation results
The proposed method is implemented on top of ECM-9.0.
 | All Intra Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.07% | -0.04% | -0.08% | 98.1% | 99.9%
Class TGM | -0.10% | -0.11% | -0.14% | 99.0% | 99.1%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.07% | -0.05% | -0.11% | xx% | xx%
Class TGM | -0.03% | 0.00% | -0.07% | xx% | xx%

## Slide 5: Conclusion
It is proposed to align intraTMP BV storing with fractional-pel resolution.
On top of ECM-9.0, the proposed method can provide with negligible complexity impact
  AI: -0.07%(Y) for class F and -0.10%(Y) for class TGM.
  RA: -0.07%(Y) for class F and -0.03%(Y) for class TGM.
Thank ETRI and Alibaba for crosschecking!

## Slide 7: Supplement (JVET-AB0061 results)
 | All Intra Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.04% | -0.15% | -0.02% | 101% | 100%
Class TGM | -0.11% | -0.10% | -0.10% | 100% | 98%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.05% | 0.12% | 0.14% | 100% | 99%
Class TGM | -0.01% | 0.02% | 0.04% | 100% | 99%