## Slide 1: JVET-AE0081: [AHG8] De-noising filter as pre-processing for machine task
Chulkeun Kim, Dong-Gyu Gwak, Jaehyun Lim
LG Electronics

## Slide 2
In this contribution, de-noising filter is proposed as a pre-processing technology for optimization of encoders and receiving systems for machine analysis of coded video content
When capturing video, noise may be captured as well.
If a de-noising filter is applied before encoding on the video transmission side
  The machine analysis performance can be improved by reducing unnecessary noise
  The burden of video transmission can be reduced by enhancing the coding efficiency
Motivation
Video Encoder
noise
+
Video Decoder
Network
Machine
analysis
Coding
efficiency
Machine
analysis
Transmission
burden

## Slide 3
Proposed method
Input YUV
Compress with VTM
Decompress with VTM
Convert to PNG
Determine task
performance
Ground truth
De-noising
filtering
Gaussian filters are used as examples of de-noising filters.
  The characteristics of the noise may depend on the purpose and environment of the application.
  De-noising filters can be defined according to the application.
  In the experiment, de-noised sequences are generated using Gaussian filters, and then run VTM-12 without any changes and the performance of the machine analysis was measured.
*Generate a filtered
version of the sequences
VTM enc/dec
without any changes

## Slide 4
Experimental results
Noise is observed in the original picture and the noise is reduced in the pre-processed picture with blurring the boundary of the object.
Original picture
pre-processed picture

## Slide 5
Experimental results
It is observed that the encoding of the preprocessed picture retains the shape of the object compared to the encoding of the original picture.
  Result of BQTerrace ( QP40, All intra)
encoding result of the original picture
encoding result of the pre-processed picture
12597.27 kbps, mAP 41.79
8768.737 kbps, mAP 43.04

## Slide 6
Experimental results
Noise is observed in the original image and the noise is reduced in the pre-processed image with blurring the boundary of the object.
  Result of Cactus (QP49, Random access)
Original picture
pre-processed picture

## Slide 7
Experimental results
It is observed that the encoding of the preprocessed picture retains the shape of the object compared to the encoding of the original picture
  Result of Cactus (QP49, Random access)
encoding result of the original picture
encoding result of the pre-processed picture
180.14 kbps, mAP 66.39
184.49 kbps, mAP 71

## Slide 8
Experimental results
Experimental results of the proposed de-noising filtering
  SFU-HW: -14.07%, -17.39%, -18.63% for RA, LD and AI respectively (Pareto-mAP)
  TVD: -18.75%, -16.22%, -22.30% for RA, LD and AI respectively (Pareto-MOTA)
[ Performance on SFU-HW dataset for object detection ]
[ Performance on TVD video dataset for object tracking ]
(The ‘/’ means non-monotonic performance.)
The low delay results on the TVD dataset were provided by the cross-checker.

## Slide 9
Experimental results
Joint-test results of combined with JVET-AD0122
  SFU-HW: -19.25, -25.84% for RA, LD respectively (Pareto-mAP)
  TVD: -22.48%, -30.98% for RA , LD respectively (Pareto-mAP)
  Additive performance improvements are observed
    JVET-AD0122 standalone: -7.34%/-6.96%(SFU-HW/TVD) for RA, -9.57%,-13.3%(SFU-HW/TVD)
[ Performance on SFU-HW dataset for object detection ]
*5.18%, 3.73%(SFU-HW/TVD) for RA, 8.45%. 14.76%(SFU-HW/TVD )for LD
[ Performance on TVD video dataset for object tracking ]
The low delay results on the TVD dataset were provided by the cross-checker.

## Slide 10
Conclusion
De-noising filter is proposed as a pre-processing technology for optimizations for encoders and receiving systems for machine analysis of coded video content.
de-noising filters can give gains without any normative changes.
The combined experimental results with JVET-AD0122 show additional performance improvements.
It is proposed to include the de-noising filter in the draft for the technical report regarding the pre-processing techniques in section 6.
Thank you to Ericsson for crosschecking
The low delay results on the TVD dataset were provided by the cross-checker.

## Slide 11
Appendix
Proposed description