## Slide 1: Non-EE2: Direct block vector(DBV) mode extension (JVET-AE0085)
Myungoh Hong, Jangwon Choi, Naeri Park, Jaehyun Lim, Seung-Hwan Kim
LG Electronics

## Slide 2
In DBV mode, when dual tree is activated in intra slices, if one of the luma blocks is coded with IBC mode or IntraTMP mode, luma block vector is used and scaled to derive chroma block vector using template matching
Chroma block copy is performed using derived chroma block vector
Introduction
5 locations in reconstructed luma samples
Prediction process of DBV mode

## Slide 3
Proposed methods
The number of locations to find block vector that is coded with IBC mode or IntraTMP mode are extended from 5 to 17
* Please note that the existing search locations (C, TL, TR, BL, and BR) is not changed
DBV candidate list is composed of block vector candidates and sorted in ascending order of SAD cost using template matching
* A template of at least one block vector in DBV candidate list is not available, DBV candidate list is not sorted
* If collocated luma block center position that is coded with IBC mode or IntraTMP mode is the same to chroma block
center position, DBV candidate list is also not sorted
A block vector with the first index in the DBV candidate list is scaled to derive chroma block vector without template matching and chroma block copy is performed

## Slide 4
Experimental results
Anchor : ECM-9.0 under CTC
 | All Intra Main10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.07% | 0.00% | 99.6% | 99.6%
Class A2 | -0.03% | -0.07% | 0.03% | 99.7% | 99.2%
Class B | 0.00% | 0.00% | 0.08% | 99.9% | 99.4%
Class C | -0.01% | -0.04% | 0.08% | 99.8% | 99.5%
Class E | -0.01% | -0.07% | 0.17% | 99.7% | 99.0%
Overall | -0.01% | -0.04% | 0.07% | 99.8% | 99.4%
Class D | 0.01% | -0.04% | -0.04% | 99.9% | 97.9%
Class F | -0.08% | -0.19% | -0.09% | 100.1% | 100.1%
Class TGM | -0.10% | -0.15% | -0.24% | 99.3% | 99.4%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.30% | -0.02% | 100.7% | 100.2%
Class A2 | -0.04% | -0.02% | 0.11% | 100.9% | 100.4%
Class B | 0.01% | -0.05% | 0.06% | 99.9% | 100.0%
Class C | 0.02% | -0.14% | -0.11% | 100.8% | 100.1%
Class E |  |  |  |  | 
Overall | 0.00% | -0.12% | 0.01% | 100.5% | 100.1%
Class D | -0.02% | -0.19% | 0.07% | 101.3% | 100.8%
Class F | -0.10% | 0.06% | -0.49% | 100.4% | 100.0%
Class TGM | -0.03% | -0.05% | -0.02% | 99.7% | 99.6%
* ParkRunning3 qp22 result is copied from anchor

## Slide 5
Conclusion
This contribution extend the number of locations from 5 to 17, and sorting block vector candidate list. Also, chroma block vector is derived without template matching
It provides coding gains with no almost impact of coding time
- For AI configuration:
  Natural contents : -0.01%/-0.04%/0.07%, 99.8%(EncT), 99.4%(DecT)
  Class F : -0.08%/-0.19%/-0.09%, 100.1%(EncT), 100.1%(DecT)
  Class TGM : -0.10%/-0.15%/-0.24%, 99.3%(EncT), 99.4%(DecT)
- For RA configuration:
  Natural contents : 0.00%/-0.12%/0.01%, 100.5%(EncT), 100.1%(DecT)
  Class F : -0.10%/0.06%/-0.49%, 100.4%(EncT), 100.0%(DecT)
  Class TGM : -0.03%/-0.05%/-0.02%, 99.7%(EncT), 99.6%(DecT).
It is suggested to study this proposal in next round EE
Thanks Qualcomm for crosschecking.