## Slide 1: JVET-AE0093 AHG11: Content-adaptive neural network loop-filter
R. Yang, M. Santamaria, F. Cricri, H. Zhang, J. Lainema, R. G. Youvalari, M. M. Hannuksela

## Slide 2
Highlights
Content adaptation of NN LOP filter, via overfitting to input test sequence
The weight-update is coded with MPEG-NNR and considered in the bitrates
Results with anchor NNVC-5.0 (NN intra and base NN LOP filters):
    -1.21% (Y), -6.43% (Cb), -5.52% (Cr).
Results with anchor NNVC-5.0 with NN tools OFF:
  -7.74% (Y), -13.73% (Cb), -12.49% (Cr).

## Slide 3
Proposed approach
Over-fitting of LOP filter
Content-adaptation is achieved by means of neural-network over-fitting on each test video and configuration
The model to be over-fitted is selected as the base model (one out of four) with the highest PSNR gain
Only a subset of parameters (multipliers) are over-fitted
Technique is applied to the LOP filter (JVET-AD0156)

## Slide 4
Proposed approach (ii)
Weight-update compression
The over-fitting result is a weight-update
Weight-updates are coded with the MPEG Neural Network Compression and representation (NNC) standard
  Previously known as NNR*

## Slide 5
Training and inference details
Training (over-fitting)
200 epochs for classes C & D; 100 epochs for classes A, B and F
Overfitting time is sequence dependent. Range [1, 11] hours
Inference
SADL int 16
Naïve quantisation as in JVET-AD0156
  Normalisation of weights and bias by scaling factors to reduce weights with large values
Complexity: 16.5 kMAC/pixel
Parameters: 53724

## Slide 6
Results
RA configuration
Anchor: NNVC 5.0 (NN intra tool + NN LOP filter). Test: 4 models (3 base + 1 over-fitted)
Anchor: NNVC 5.0 (NN tools OFF). Test: 4 models (3 base + 1 over-fitted)

## Slide 7
Results (extras) (ii)
RA configuration
Anchor: NNVC 5.0 (NN intra tool + LC NN filter). Test: 5 models (4 base + 1 over-fitted)

## Slide 8
Results (extras) (iii)
RA configuration
Anchor: NNVC 5.0 (intra NN tool OFF). Test: 4 models (3 base + 1 over-fitted)
The training data was regenerated by disabling the intra NN tool
Anchor: NNVC 5.0 (NN tools OFF). Test: 4 models (3 base + 1 over-fitted) & NN intra off

## Slide 9
Results (iv)
Comparison with other tools

## Slide 10
Conclusions
Overfitting the NN LOP filter has the following benefits:
  Increase in coding gains
  Negligible delay at decoder end
Recommendation
  Propose cross-check of training and inference in the next EE1 round

## Slide 11
Summary
Content adaptation of NN LOP filter, via overfitting to input test sequence.
The weight-update is coded with MPEG-NNR and considered in the bitrates.
Test: NNVC 5.0 with NN intra tool, base LC NN filters and overfitted LC NN filter.
Anchor: NNVC 5.0 (NN intra tool + base LC NN filters).
Test: NNVC 5.0 with NN intra tool, base LC NN filters and overfitted LC NN filter.
Anchor: NNVC 5.0 with NN tools OFF.