## Slide 1: JVET-AE0115
Non-EE2: Unified intra CC-models parameters precision
P. Bordes, F. Galpin, K. Naser, F. Le Léannec
InterDigital

## Slide 2: Introduction JVET-AE0115
The intra CC-models allow predicting chroma samples from reconstructed luma samples.
In ECM, the storage precision of the CC-model parameters differs depending on the type of CC-model:
• CCLM: integer 32-bits params
• GLM: integer 32-bits params
• CCCM: integer 64-bits params (CCCM, GLCCCM, NSCCCM, MDFCCCM)
In cross-component prediction (CCP) merge mode, the CC-models are transformed into 64-bits and next inherited.

## Slide 3: Proposal JVET-AE0115
It is proposed to unify the CC-model parameters using reduced 32-bits representation for storage and convolution:
The derived 64-bits parameters are transformed into 32-bits.
Next, when applying the CC-model, the convolution is made with 32-bits parameters and the accumulation uses 32-bits sum only.
Using fewer number of bits decreases memory bandwidth and allows effective SIMD implementation.
A software patch on top of ECM-9.0 is provided.

## Slide 4: Results JVET-AE0115
Thank you MediaTek for cross-check
Table 1: Performance results of proposal in AI (32-bits)
Table 2: Performance results of proposal in RA (32-bits)

## Slide 5: Results JVET-AE0115
Table 3: Performance results of proposal in AI (16-bits)