## Slide 1: AHG12 : Template-based CIIP weight derivation
Menghu Jia,
Yali Hu,
Ying Gao,
Shaowei Xie,
Cheng Huang
(ZTE Corporation)
JVET-AE0129

## Slide 2: Intruduction
Ciip pdpc | Intra mode | Condition | Weight
1 | dirMode=planar | Location:(x,y) | Weight depends on sample position
0 | dirMode is derived by TIMD | dirMode=planar or dirMode = DC or width<4 or height<4 | Weight depends on the code mode of neighboring blocks(Top block\Left block)
 |  | dirMode < DIA_IDX | Horizontal partitioning of coding blocks and applying fixed weights
 |  | others | Vertical partitioning of coding blocks and applying fixed weights
In CIIP, the predicted samples are obtained by weighting intra prediction and inter prediction
In ECM9.0, the weights of CIIP are derived as follows
TIMD : (intra + intra) prediction with TM-based Weights
BCW : (inter + inter) prediction with TM-based Weights
CIIP : (intra + inter) prediction with ?

## Slide 3: Proposed Method
Obtain the intra prediction and inter prediction of the template
Fuse the intra prediction and inter prediction of the template (weights (wIntra,wInter) ={(1,3),(2,2),(3,1)})
Calculate the SAD values of the predicted samples and reconstructed samples
Select the weights corresponding to the template with the smallest SAD as the weights for CIIP
The template cost is calculated based on the Y component and applies to all components
When PDPC is not enabled, the method introduced in this contribution will be enabled by default

## Slide 4: Results
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | 0.00% | -0.07% | 0.08% |  | 
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0.06% | -0.07% | -0.08% |  | 
Class F |  |  |  |  | 
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | 0.12% | -0.64% | -0.10% |  | 
Class E | 0.02% | 0.47% | 1.49% |  | 
Overall |  |  |  |  | 
Class D | 0.07% | 0.70% | -0.89% |  | 
Class F |  |  |  |  | 
It is recommoned to further study

## Slide 5: THANK YOU！