## Slide 1
Donghyun Kim
JVET-AE0136
Non-EE2: Fix on TM-based reordering for affine MMVD mode

## Slide 2: Problem statement
TM-based reordering for affine MMVD in ECM-9.0
  For a bi-predictive MMVD base, the MMVD offset can be added to CPMVs of list 0, while the MMVD offset can be added to or subtracted from CPMVs of list 1.
    Depending on the POCs of the reference pictures from list 0 and list 1.
    Problem: the reference picture index of list 0 is incorrectly used instead of the reference picture index of list 1 when calculating the POC of the reference picture from list 1.
      Consequently, the MMVD offset may be incorrectly applied to CPMVs of list 1.
void InterPrediction::sortAffineMergeCandidates(...)
{
...
else
{
const int poc0 = pu.cu->slice->getRefPOC(REF_PIC_LIST_0, mvfMmvd[0][0].refIdx);
const int poc1 = pu.cu->slice->getRefPOC(REF_PIC_LIST_1, mvfMmvd[0][0].refIdx);
const int currPoc = pu.cu->slice->getPOC();
if ((poc1 - currPoc)*(poc0 - currPoc) > 0)
{
posList0 = fPosPosition1 + 1;
posList1 = fPosPosition1 + 1;
load0 = true;
load1 = true;
}
else
{
posList0 = fPosPosition1 + 1;
posList1 = (fPosPosition1 ^ 1) + 1;
load0 = true;
load1 = true;
}
}
...
}
* mvfMmvd[LX][cpIdx]
  - LX : L0/L1
  - cpIdx: CPMV Index
JVET-AE0136

## Slide 3: Proposed fix
Replaces the reference picture index of list 0 with the reference picture index of list 1 to calculate the POC of the reference picture from list 1.
  Only one digit change in “sortAffineMergeCandidates” function.
Current Picture
Reference Picture from List 0
CPMV[1][0]
MMVD offset
: Bug
: Bug Fix
CPMV[0][0]
MMVD offset
– (MMVD offset)
Reference Picture from List 1
JVET-AE0136
void InterPrediction::sortAffineMergeCandidates(...)
{
...
else
{
const int poc0 = pu.cu->slice->getRefPOC(REF_PIC_LIST_0, mvfMmvd[0][0].refIdx);
#if FIX
const int poc1 = pu.cu->slice->getRefPOC(REF_PIC_LIST_1, mvfMmvd[1][0].refIdx);
#else
const int poc1 = pu.cu->slice->getRefPOC(REF_PIC_LIST_1, mvfMmvd[0][0].refIdx);
#endif
const int currPoc = pu.cu->slice->getPOC();
if ((poc1 - currPoc)*(poc0 - currPoc) > 0)
{
posList0 = fPosPosition1 + 1;
posList1 = fPosPosition1 + 1;
load0 = true;
load1 = true;
}
else
{
posList0 = fPosPosition1 + 1;
posList1 = (fPosPosition1 ^ 1) + 1;
load0 = true;
load1 = true;
}
}
...
}
* mvfMmvd[LX][cpIdx]
  - LX : L0/L1
  - cpIdx: CPMV Index

## Slide 4: Experimental results
Anchor: ECM-9.0 under CTC
Results
  RA: 0.00%, -0.07%, -0.01%
  LDB: same as ECM-9.0
    Since both reference pictures from list 0 and list 1 are always from the past.
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | 0.00% | 0.00% | 0.00% | 96.7% | 100.4%
Class E | 0.00% | 0.00% | 0.00% | 97.2% | 103.9%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.00% | 0.00% | 0.00% | 99.7% | 101.0%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.05% | 0.11% | 100.1% | 100.3%
Class A2 | -0.03% | -0.01% | -0.03% | 99.9% | #NUM!
Class B | 0.01% | -0.09% | -0.03% | 99.3% | 100.1%
Class C | 0.00% | -0.11% | -0.04% | 99.7% | 99.8%
Class E |  |  |  |  | 
Overall | 0.00% | -0.07% | -0.01% | 99.7% | #NUM!
Class D | 0.00% | -0.06% | -0.03% | 100.1% | 99.8%
* Encoding/Decoding time not reliable (Runtime should not be changed)
JVET-AE0136

## Slide 5: Conclusion
Proposed fix
  Resolves a bug in the implementation of TM-based reordering for affine MMVD.
    Simple S/W bug fix (one digit change) for ECM-9.0.
Experimental results
  RA: 0.00%, -0.07%, -0.01%
  LDB: same as ECM-9.0
Recommendation
  Incorporate the proposed fix in the next version of ECM.
Thanks to Bytedance for cross-checking (JVET-AE0213).
JVET-AE0136