## Slide 1: JVET-AE0140 LIC extensions
Alexey Filippov
Vasily Rufitskiy
Kirill Suverov

## Slide 2: Background
LIC parameter derivation in ECM-9.0:
2-parametric linear model is derived using the adjacent line of a block
Some samples are decimated
Parameters of the linear model used in LIC:
Scale
Shift (set to 5 in ECM-9.0)
Offset
Pred = ((Scale * Ref) >> Shift) + Offset,
      Scale
  Shift (set to 5 in ECM-9.0)
where Ref and Pred stand for reference and predicted samples

## Slide 3: Proposal
Extend the set of models applicable to inter-predicted blocks:
In addition to the current 2-parametric LIC model, higher-order models can be used to filter reference blocks to get prediction blocks
Switching between models using
  a flag
  TM cost value obtained for a probe (adjacent) line

## Slide 4: Multiparametric Reference Filtering
Reference samples template
Probe samples template
Reference samples corresponding to the current block
Reference frame
Current frame
Current block
Reference samples of the current block
Coefficients calculation
Set of coefficients

## Slide 5: Experimental results
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.17%* | -0.15% | -0.18% | 102.1% | 100.7%
Class A2 | -0.14%* | -0.09% | -0.11% | 101.2% | 100.4%
Class B | -0.15% | -0.39% | -0.22% | 102.3% | 100.9%
Class C | -0.17% | -0.24% | -0.19% | 102.9% | 100.2%
Class E |  |  |  |  | 
Overall | -0.16% | -0.24% | -0.18% | 102.2% | 100.6%
Class D | -0.06% | -0.07% | -0.08% | 102.2% | 100.7%
Class F | -0.06% | 0.05% | 0.28% | 101.5% | 100.1%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.23%* | -0.35% | -0.24% | 102.6% | 100.0%
Class E | -0.18% | -0.27% | -0.32% | 103.0% | 100.6%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.17% | -0.22% | -0.24% | 104.0% | 100.8%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
* - Missing rate points are taken from the ECM-9.0 anchor

## Slide 6: Conclusions
We recommend this proposal for studying in the next round of EE2

## Slide 7
THANK YOU