## Slide 1: JVET-AE0148 Non-EE2: Affine subblock BDOF refinement
Zhi Zhang, Han Huang, Jian-Liang Lin,
Vadim Seregin, Marta Karczewicz (Qualcomm)

## Slide 2: Introduction and Proposal
        In ECM9, BDOF is applied to non-affine blocks when meets BDOF condition, e.g., equal weighted Bi-pred and equal POC distance.
        In ECM9, AMVP-merge mode is applied to non-affine blocks
        AMVP predictor is signalled, e.g., refList index, refPic index, mvp index,
        Merge predictor is derived without signaling
        It is proposed to apply those modes to affine blocks as follows:
        BDOF is applied to affine subblock MC mode:
        Subblock MVs derived from affine model are used as initial MV
        Apply to affine merge mode, affine BM merge mode and SbTMVP mode
        AMVP-merge is applied to affine blocks, a flag is signalled to indicate the mode

## Slide 3: Simulation Results
 | Random access Main10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.19% | -0.04% | 103.2% | 102.4%
Class A2 | -0.30% | -0.23% | -0.20% | 103.7% | 106.6%
Class B | -0.10% | -0.08% | -0.03% | 102.9% | 104.5%
Class C | -0.18% | -0.22% | -0.05% | 102.5% | 104.2%
Class E |  |  |  |  | 
Overall | -0.14% | -0.17% | -0.07% | 103.0% | 104.4%
Class D | -0.18% | -0.35% | -0.22% | 102.4% | 105.3%
Class F | -0.07% | -0.11% | 0.01% | 102.6% | 103.1%
TGM | 0.02% | 0.00% | -0.04% | 101.7% | 100.6%
Affine subblock BDOF refinement
Affine subblock BDOF refinement
+ AMVP-merge mode for affine
 | Random access Main10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.06% | -0.14% | -0.11% | 107.8% | 102.7%
Class A2 | -0.34% | -0.29% | -0.28% | 107.3% | 106.9%
Class B | -0.16% | -0.17% | -0.04% | 107.5% | 104.6%
Class C | -0.21% | -0.25% | -0.15% | 107.0% | 103.1%
Class E |  |  |  |  | 
Overall | -0.19% | -0.21% | -0.13% | 107.4% | 104.3%
Class D | -0.26% | -0.18% | -0.32% | 106.5% | 104.7%
Class F | -0.13% | -0.13% | -0.09% | 106.1% | 103.5%
TGM | 0.00% | -0.06% | -0.08% | 104.3% | 100.8%
If iterative BDOF from EE2-3.5 is applied to refine affine subblocks
-0.22% (Y), -0.26% (U), -0.22% (V)