## Slide 1: Non-EE2:enabling template-based inter tools for scaled reference pictures in the RPR
Xiaoyu Xiu, Hong-Jheng Jhu, Che-Wei Kuo, Changyue Ma, Ning Yan, Wei Chen, Xianglin Wang

## Slide 2: Introduction
Template-based reordering methods
  ARMC, MMVD, affine MMVD, template-based BCW derivation, refIdx list reordering, MVD sign and magnitude-suffix prediction
  Template-based reordering methods are not applied to the scaled reference pictures
    Template prediction is bypassed with the corresponding cost being set to maximum
    Candidates associated with scaled reference pictures are located at the end of the list
  LIC
  LIC is always skipped in case any of the reference pictures is scaled
  LIC flag is not signaled and inferred to be 0

## Slide 3: Proposal
  Enabling template-based reordering and LIC for scaled reference pictures in the RPR
  The main aspects of all the related tools are kept exactly the same as the existing designs
  MC filters are replaced with the corresponding RPR down-sampling/up-sampling filters to generate template prediction samples
  One fix is provided to fix the encoder crash for the RA configuration in ECM-9.0 RPR
  The crash is caused by encoder assertion due to unfilled AMVP lists for the SMVD at encoder for scaled pictures
  The fix is submitted as MR447

## Slide 4: Performance evaluation
RPR-1.5x |  | RPR-2.0x | 
RA | LDB | RA | LDB
ScalingRatioHor: 1.5 | ScalingRatioHor: 1.5 | ScalingRatioHor: 2.0 | ScalingRatioHor: 2.0
ScalingRatioVer: 1.5 | ScalingRatioVer: 1.5 | ScalingRatioVer: 2.0 | ScalingRatioVer: 2.0
FractionNumFrames: 1.0 | FractionNumFrames: 1.0 | FractionNumFrames: 1.0 | FractionNumFrames: 1.0
RPR: 1 | RPR: 1 | RPR: 1 | RPR: 1
UpscaledOutput: 1 | UpscaledOutput: 1 | UpscaledOutput: 1 | UpscaledOutput: 1
SwitchPocPeriod: 16 | SwitchPocPeriod: 0 | SwitchPocPeriod: 16 | SwitchPocPeriod: 0
  Anchor: ECM-9.0 + MR437 + MR447
  Test: anchor + the proposed change

## Slide 5: Performance evaluation
RPR-1.5x
 | Low-delay B PSNR1 |  |  |  |  | Low-delay B PSNR2 |  |  |  | 
 | Over ECM-9.0 |  |  |  |  | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -0.84% | -0.74% | -0.66% | 104.7% | 102.7% | -0.83%* | -0.77%* | -0.66%* | 104.7% | 102.8%
Class C | -0.99% | -1.12% | -0.37% | 105.3% | 105.5% | -0.91% | -1.13% | -0.37% | 105.3% | 105.5%
Class E | -0.86% | -1.42% | -1.09% | 104.5% | 104.5% | -0.84% | -1.50% | -1.11% | 104.5% | 104.5%
Overall | -0.89% | -1.04% | -0.67% | 104.9% | 104.1% | -0.86% | -1.07% | -0.68% | 104.9% | 104.1%
Class D | -0.64% | -0.41% | -0.78% | 103.8% | 101.2% | -0.57% | -0.39% | -0.86% | 103.8% | 101.2%
Class F | -1.26% | -1.32% | -0.92% | 103.7% | 104.2% | -1.06% | -1.13% | -0.77% | 103.7% | 104.2%
 | Random Access |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -1.80% | -1.25% | -1.45% | 104.0% | 101.9%
Class C | -1.13% | -1.06% | -1.13% | 104.0% | 103.5%
Class E |  |  |  |  | 
Overall | -1.50% | -1.17% | -1.31% | 104.0% | 102.6%
Class D | -1.07% | -1.03% | -0.96% | 103.3% | 102.5%
Class F | -1.70% | -1.48% | -1.41% | 103.0% | 104.5%
  * represents the data including unavailable test points which are pasted from the anchors

## Slide 6: Performance evaluation
RPR-2.0x
 | Low-delay B PSNR1 |  |  |  |  | Low-delay B PSNR2 |  |  |  | 
 | Over ECM-9.0 |  |  |  |  | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -0.78% | -0.70% | -0.62% | 105.0% | 102.9% | -0.68%* | -0.69%* | -0.67%* | 105.0% | 102.9%
Class C | -0.83% | -0.83% | -0.35% | 104.7% | 104.2% | -0.68% | -0.88% | -0.40% | 104.7% | 104.2%
Class E | -0.69% | -0.40% | -0.68% | 104.5% | 104.8% | -0.59% | -0.55% | -0.73% | 104.5% | 104.8%
Overall | -0.77% | -0.67% | -0.54% | 104.8% | 103.8% | -0.65% | -0.72% | -0.59% | 104.8% | 103.8%
Class D | -0.58% | -0.63% | -0.41% | 103.9% | 101.3% | -0.33% | -0.84% | -0.60% | 103.9% | 101.3%
Class F | -1.30% | -0.79% | -0.68% | 104.6% | 104.8% | -0.87% | -0.91% | -0.52% | 104.6% | 104.8%
 | Random Access |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -1.76% | -1.24% | -1.29% | 103.6% | 102.5%
Class C | -1.08% | -0.99% | -0.92% | 103.5% | 103.0%
Class E |  |  |  |  | 
Overall | -1.46% | -1.13% | -1.13% | 103.6% | 102.7%
Class D | -0.86% | -0.72% | -0.81% | 102.6% | 102.3%
Class F | -1.54% | -1.18% | -1.28% | 102.5% | 103.8%
  * represents the data including unavailable test points which are pasted from the anchors

## Slide 7: Closing
Proposal
  Enabling template-based reordering tools and LIC for the RPR
  RA: -1.50%, LDB: -0.89% for RPR-1.5x
  RA: -1.46%, LDB: -0.77% for RPR-2.0x
  Recommendation
  Study the proposed method in the context of EE2