## Slide 1
JVET-AE0161
AHG11: Input and output rotation of model for NNVC in-loop filter
Renjie Chang, Liqiang Wang, Xiaozhong Xu, Shan Liu (Tencent)

## Slide 2
In this contribution, the rotation operations are applied to the inputs and outputs of NNVC HOP network to further improve the coding performance.
In the rotation process, all the input samples including image information and side information are rotated and then fed into network to perform the inference.
Introduction
1

## Slide 3
Proposed method
1
A slice-level flag is signaled to indicate the rotation type including no rotation, rotation to the left and rotation to the right. The operations of rotating left and right are shown as follows.
Fig. 2 Rotation to the left
Fig. 3 Rotation to the right
Besides, to reduce the encoding time, only partial CTUs are used in the RDO process of selecting the best rotation type.

## Slide 4
Results
1
Table 1. Proposed vs NNVC-5.0 (only HOP)
 | Random access Main10 |  |  |  | 
 | BD-rate Over NNVC-5.0 (only HOP) |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT CPU
Class A1 | -0.18% | -0.27% | -0.74% | 144% | 123%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -0.08% | -0.37% | -0.55% | 141% | 122%
Class C | -0.14% | -0.82% | -0.74% | 134% | 121%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.21% | -1.10% | -1.42% | 133% | 115%
Class F | -0.09% | -0.58% | -0.49% | 156% | 125%
 | Random access Main10 |  |  |  | 
 | BD-rate Over NNVC-5.0 (NNIntra+HOP) |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT CPU
Class A1 | #VALUE! | #VALUE! | #VALUE! |  | 
Class A2 | #VALUE! | #VALUE! | #VALUE! |  | 
Class B | #VALUE! | #VALUE! | #VALUE! |  | 
Class C | -0.13% | -0.78% | -0.95% |  | 
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! |  | 
Class D | -0.17% | -1.37% | -1.33% |  | 
Class F | #VALUE! | #VALUE! | #VALUE! |  | 
Table 2. Proposed vs NNVC-5.0 (NNIntra + HOP)

## Slide 5
In this contribution, the rotation operations are proposed to be applied to both input and output of HOP network to further improve the coding performance.
Experimental results demonstrate the proposed method can achieve about -0.2%/-0.4%/-0.6% gain for RA.
Conclusions
1
Thanks OPPO for crosschecking.

## Slide 6
Notes: That is all. Thanks.