## Slide 1: JVET-AE0165
EE1 -4.4: Low complexity NN filter with design elements of Unified Filter Architecture and EE-1.2 and EE-1.3
11-19 July 2023
Y. Li , D. Rusanovskyy, M. Karczewicz (Qualcomm)

## Slide 2: Overview
Unified High Operation Point (HOP) filter
  477 kMAC/pixel
  AI {-7.9%, -19.1%, -20.2%}
  Training ongoing
Low-performance Operation Point (LOP)
  16.2 kMAC/pixel
  4 models; parameters: 0.2M in total
  AI {-4.58%, -5.67%, -5.74%}
  RA {-5.20%, -7.53%, -6.60%}
Proposed HOP architecture at LOP complexity:
  14.8 to 18.7 kMAC/pixel
  1 model; parameters: 0.05M
  AI (int16): {-4.42%, -10.52%, -11.18%} (Stage I)
  RA (Stage II under running)

## Slide 3: Proposed method
Head blocks
  Reducing extracted feature set
  Removing the activation
Backbone blocks
  CP decomposition
  Feature reduction
  Simplification of the network
Tail blocks
  Decomposition of the convolution
In the blocks marked with “Separable”, depth-wise convolution is performed.

## Slide 4: Network Information
Training
  Unified HOP dataset
  Unified HOP training process
  End-to-End training
Inference: HOP aligned input/output

## Slide 5: Test Results (with SADL and 16-bit integer)
Compared to NNVC-4.0 (NNIntra and LOP enabled)
Complexity in kMAC/pixel: 14.8 (frame-wise), 16.7 (block-wise of block 256x256), and18.7 (block-wise of block 128x128)
BD-Rate (AI only)
Compared to NNVC-4.0 (All tools off)
The proposed (with NNIntra enabled) compared to NNVC-4.0 (All tools off)
(For the joint YCbCr metric, the BD-rate gain is -1.1%)

## Slide 6: Conclusion
Adjustment to the HOP architecture to meet LOP complexity constraints.
  HOP database and End-to-End training process
  HOP input/output interface
  HOP based filter architecture
The proposed method outperforms the LOP anchor for the AI configuration:
  AI (int16) {0.08%, -5.41%, -5.83%}, For the joint YCbCr metric, the BD-rate gain is -1.1%.
  Complexity in kMAC/pixel: 14.8 (frame-wise); 16.7 (block-wise of block 256x256); 18.7 (block-wise of block 128x128).
  Memory: 1 model of 0.05M, instead of 4 models in LOP anchor
It is proposed to study the proposed method in the next round of EE.

## Slide 7: Thank you