## Slide 1: AI-based video Coding
JVET Neural Network-based Video Coding (NNVC)
Elena Alshina

## Slide 2: JVET NNVC activities
Neural network-based video coding (AHG11)
(jvet@lists.rwth-aachen.de)
Evaluate and quantify the performance improvement potential of NN-based video coding technologies compared to existing video coding standards such as VVC, including both individual coding tools and novel architectures.
Discuss potential refinements of the test conditions for NN-based video coding in JVET-AD2016. Generate and distribute anchor encoding, and develop supporting software as needed.
Study the impact of training (including the impact of loss functions) on the performance of candidate technologies, and identify suitable material for testing and training.
Analyse complexity characteristics, perform complexity analysis, and develop complexity reductions of candidate technology.
Finalize and discuss the EE on neural network-based video coding.
Coordinate with other relevant groups, including SC29/AG5 on the evaluation and assessment of visual quality, and AHG12 on the interaction with ECM coding tools. If possible, prepare encodings with combinations of tools included in the NNVC software for visual quality assessment at the next meeting.
Coordinate with AHG14 on items related to NNVC software development.
NNVC software development (AHG14)
(jvet@lists.rwth-aachen.de)
Coordinate development of the NNVC software and associated configuration files.
Prepare and deliver NNVC-5.0 software version and the reference configuration encodings according to the NNVC common test conditions as described in JVET-AD2016.
Investigate combinations of tools included in the NNVC software, prepare and release anchor data for all configurations of the software, including anchor for High Operation Point configuration.
Study and maintain the SADL (Small Adhoc Deep-Learning Library). Identify gaps in functionality and develop improvements as needed.
Coordinate with NNVC algorithm and software description (JVET-AD2019) editors to identify any mismatches between software and description document, suggest further updates to the description document as appropriate.
Develop the software basis for High Operation Point in NNVC-5.1 as described in JVET-AD0380.
Coordinate with AHG11 on items related to NNVC activities.
Documents:
JVET-AD2016 Common test conditions and evaluation procedures for neural network-based video coding technology [E. Alshina, R.-L. Liao, S. Liu, A. Segall]
JVET-AD2023 Exploration experiment on neural network-based video coding (EE1) [E. Alshina, F. Galpin, Y. Li, D. Rusanovskyy, M. Santamaria, J. Ström, L. Wang, Z. Xie]
JVET-AD2019 Description of algorithms and software in neural network-based video coding (NNVC) version 3 [F. Galpin, Y. Li, D. Rusanovskyy, J. Ström, L. Wang]
SW location:
https://vcgit.hhi.fraunhofer.de/jvet-ahg-nnvc/

## Slide 3: Complexity & Performance aspects to be reported
Training
  Epoch: Number of complete passes through the training data (e.g. 100)
  Batch size: Number of samples processed before the model is updated. (e.g. 4Kx16frames)
  Training time: CPU and/or GPU (e.g. 48h)
  Learning curve: Plot of the training loss and validation loss (or similar) versus the number of epochs
  Loss function: Function used to calculate the model error during training and optimization (e.g. L1, L2, etc.)
  Training sequences: Sequences used for training
  Training configuration per rate-distortion point: Any changes in the requested information used to generate different rate-distortion points
  Patch size: Size of input to the neural networks (patchW×patchH×patchT, e.g. 64x64x3)
  Learning rate: Amount that the weights are updated during training (e.g. 5e-4)
  Learning rate update strategy: Description of any learning rate adaptation during training
  Mini-batch selection procedure: Description of mini-batch selection procedure
  Optimizer: Algorithm used to change the attributes of proposed neural networks (e.g. ADAM)
  Preprocessing: (e.g. preprocessing procedure, normalization, cropping method, rotation, zoom etc.)
  Training data update strategy: Description of any change in training data during training
Inference
  Network visualization: Graphical representation of the neural network
  Param. number (each): Number of parameters for each model in the neural network.
  Param. number (all): Total numbers of parameters for all models in the neural network.
  Param. precision: Bits for storing one parameter. Besides, using “I” for indicating the integer, and using “F” for indicating the floating number. For example, if the proposed method uses 16-bit integer to represent a parameter, you can report this information as “16 (I)”.
  kMAC: Number of multiply–accumulate (MAC) operations per 1,000 samples in the worst-case for the inference stage.
  Total Conv. layers: Total numbers of convolutional layers in the network structure. If there is no convolutional layer, just fill in 0.
  Total FC layers: Total number of fully-connected layers in the network structure. If there is no fully-connected layer, just fill in 0.
  Mem.T (MB): the temporary memory shall be reported as (i) the total memory size required for inference and (ii) the maximum memory size per model.
  Batch size: The number of samples processed in parallel during inference. (e.g. 4Kx16frames)
  Patch size: Size of input to the neural networks during inference (patchW×patchH×patchT, e.g. 64x64x3)
  Border handling: Description on boundary handing, if inference operates on a block (or CTU) basis.
Metrics
  PSNR Y, U, V
  MS-SSIM
Encoder and Decoder Run Time (CPU)
Video sequences
4K  6 videos (A1, A2)
1080p  5 videos (class B)
832x480 4 videos (class C)
720p 3 videos (class E)
416x240 4 videos (class D)
Screen Content  4 videos (class F)
HDR  4 videos (class H2)
Configurations
Random Access
All Intra
Low Delay - B (rarely reported)

## Slide 4: Cross-check of training
Training sets
  BVI-DVC https://fan-aaron-zhang.github.io/BVI-DVC/
    191 video scenes s in 4 resolution (480  272 ... 38402176)
  Tencent Video Dataset (TVD) https://multimedia.tencent.com/resources/tvd
    86 video scenes
    3840  2160
  DIV2K https://data.vision.ee.ethz.ch/cvl/DIV2K/
    900 high resolution images (converted to YUV)
Training cross-check methods
  Training from Random Initialization (multiple stages)
  “Fine tuning” (training of final stage from proponent’s check-point)
When training is considered to be verified?
  “Model trained by proponent” “Model trained by cross-checker”
  BD-rate difference: 0.1% (All Intra , Random Access cfg) ... 0.5% (Low Delay B cfg)
Is it enough?
it is desirable to extend
Training from scratch
~60 days

## Slide 5: NNVC algorithm study steps
1
Proposal to JVET
any NN framework implementation
test results vs VVC anchor (NNVC SW)
2
Study in Exploration Experiment EE1
any NN framework implementation
inference cross-check
3
Study in Exploration Experiment EE1
SADL 16 bits quantized implementation
training cross-check
4
Adoption to NNVC common SW base
Interaction with other NN tools
ON or OFF by default
BD-rate gain in RA cfg
kMAC/pxl
total memory size for NN parameters
Complexity (kMAC/pxl, memory)
BD-rate vs VVC
-10%
0%
Device
Capability
Why SADL (Small Adhoc Deep-Learning Library)?
Necessary (but not sufficient) for device interoperability
Transparent (mathematical convolution)
Quantized NN (necessary, but not sufficient for device interoperability)

## Slide 6: JVET Neural Network-based Video Coding tools
Chart: Random Access
| 615 | 615 | 615 | 615 | 615 | 615 | 615 | 615 | 615 | 664 | 677 | 677 | 673 | 673 | 664 | 664 | 664 | 664 | 605.45000000000005 | 605.45000000000005 | 16.2 | 16.2 | 16.2 | 17.7 | 17.7 | 17.7
Loop Filter | -0.089129 | -0.0918 | -0.0975 | -0.0998 | -0.091709 | -0.10243 | -0.089201 | -0.089372 | -0.0893 | -0.094865 | -0.096026 | -0.095991 | -0.095908 | -0.095998 | -0.094969 | -0.10089 | -0.10007 | -0.095903 | -0.1003 | 0 | -0.0505 | -0.0502 | -0.0501 | -0.0543 | -0.0537 | -0.0534
Post Filter | -0.047795
Super Resolution | -0.0123 | -0.021342
Devices | 0
NN Intra | -0.01575
NN-inter | -0.0432
64 kMAC/pxl, Nvidia RTX 3080, 4K
----- NNVC 3.0 SW; Oct. 2022---------
High complexity in-loop filters
----- NNVC 4.0 SW; Jan. 2023 ---------
Post-filter SEI (in VSEI spec)
Reduced Resolution Coding & NN-based super resolution
Block-level NN-intra
-----NNVC 5.0 SW; April 2023---------
Low complexity in-loop filter
Unified high complexity in-loop filter
-----not yet in NNVC (but in EE1)---------
Synthesized Inter frame

## Slide 7: JVET NNVC for picture coding
Chart: All Intra
| 615 | 615 | 615 | 615 | 615 | 615 | 615 | 615 | 615 | 664 | 677 | 677 | 673 | 673 | 664 | 664 | 664 | 664 | 605.45000000000005 | 605.45000000000005 | 16.2 | 16.2 | 16.2 | 17.7 | 17.7 | 17.7
Loop Filter | -0.065149 | -0.0663 | -0.0751 | -0.0761 | -0.069636 | -0.080319 | 0 | 0 | 0 | -0.075231 | -0.073864 | -0.073855 | -0.073868 | -0.073861 | -0.075228 | -0.075227 | -0.075227 | -0.075231 | -0.0788 | -0.0724 | -0.0464 | -0.0464 | -0.0462 | -0.0494 | -0.0491 | -0.0488
Post Filter | 0 | 0
Super Resolution | -0.0056559 | -0.0034691 | -0.008 | -0.0081 | -0.0083852 | -0.011276
Device | 0
NN Intra | -0.033513 | -0.096432 | -0.10488
64 kMAC/pxl, Nvidia RTX 3080, 4K
----- NNVC 3.0 SW; Oct. 2022---------
High complexity in-loop filters
----- NNVC 4.0 SW; Jan. 2023 ---------
Post-filter SEI (in VSEI spec)
Reduced Resolution Coding & NN-based super resolution
Block-level NN-intra
-----NNVC 5.0 SW; April 2023---------
Low complexity in-loop filter
Unified high complexity in-loop filter
-----not yet in NNVC (but in EE1)---------
Synthesized Inter frame

## Slide 8: NNVC-4.0 (Jan. 2023) vs VVC anchor
 | All Intra Main 10 |  |  |  | 
 | Over VTM-11.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -9.6% | -18.8% | -19.6% | 284% | 23039%
Class A2 | -8.6% | -19.8% | -16.4% | 265% | 18285%
Class B | -8.8% | -19.2% | -22.6% | 264% | 17165%
Class C | -9.7% | -18.3% | -21.1% | 239% | 11684%
Class E | -13.4% | -22.2% | -22.5% | 257% | 19624%
Overall | -9.9% | -19.5% | -20.7% | 260% | 17104%
Class D | -9.5% | -18.2% | -21.7% | 226% | 10674%
Class F | -6.6% | -15.3% | -14.4% | 177% | 14663%
Class TGM |  |  |  |  | 
 | Random Access Main 10 |  |  |  | 
 | Over VTM-11.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -10.8% | -17.2% | -21.6% | 187% | 31683%
Class A2 | -12.3% | -19.8% | -16.2% | 186% | 30213%
Class B | -11.1% | -21.6% | -22.7% | 191% | 31365%
Class C | -12.7% | -22.8% | -24.3% | 172% | 27411%
Class E |  |  |  |  | 
Overall | -11.7% | -20.7% | -21.6% | 184% | 30093%
Class D | -14.9% | -23.8% | -27.6% | 166% | 24723%
Class F | -6.3% | -13.8% | -12.2% | 237% | 12250%
Class TGM |  |  |  |  | 
 | Low delay B Main 10 |  |  |  | 
 | Over VTM-11.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -8.1% | -18.9% | -19.8% | 184% | 29612%
Class C | -10.0% | -19.9% | -20.8% | 164% | 26646%
Class E | -9.8% | -16.6% | -18.8% | 276% | 26585%
Overall | -9.2% | -18.7% | -19.9% | 196% | 27828%
Class D | -11.9% | -24.3% | -27.1% | 159% | 23860%
Class F | -5.5% | -12.5% | -10.1% | 232% | 14878%
Class TGM |  |  |  |  | 
 | Low delay P Main 10 |  |  |  | 
 | Over VTM-11.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C |  |  |  |  | 
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D |  |  |  |  | 
Class F |  |  |  |  | 
Class TGM |  |  |  |  | 
NNVC-4.0: NNinta + NNLF (~600 kMAC/pxl) + enc NNLF opt + temp. filter (w/o Super Res , w/o Post Filter)
JVET-AD0014

## Slide 9: ECM-8.0 (Jan. 2023) vs VVC anchor
 | All Intra Main 10 |  |  |  | 
 | Over VTM-11.0ecm8 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -9.0% | -18.8% | -25.2% | 703% | 380%
Class A2 | -13.5% | -22.8% | -25.9% | 695% | 382%
Class B | -8.3% | -21.8% | -20.1% | 692% | 421%
Class C | -9.2% | -14.0% | -14.3% | 677% | 419%
Class E | -10.5% | -18.9% | -17.7% | 648% | 423%
Overall | -9.9% | -19.2% | -20.2% | 684% | 407%
Class D | -7.5% | -11.5% | -11.5% | 672% | 418%
Class F | -22.2% | -30.6% | -30.2% | 460% | 365%
Class TGM | -35.6% | -42.9% | -42.3% | 387% | 329%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-11.0ecm8 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -19.9% | -22.8% | -29.8% | 687% | 742%
Class A2 | -22.4% | -29.6% | -32.9% | 632% | 887%
Class B | -18.3% | -29.1% | -27.1% | 558% | 758%
Class C | -20.0% | -23.6% | -23.5% | 574% | 757%
Class E |  |  |  |  | 
Overall | -19.9% | -26.5% | -27.8% | 601% | 779%
Class D | -20.8% | -25.0% | -25.2% | 594% | 876%
Class F | -24.9% | -32.4% | -32.7% | 438% | 465%
Class TGM | -33.3% | -38.7% | -38.9% | 489% | 417%
 | Low delay B Main 10 |  |  |  | 
 | Over VTM-11.0ecm8 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -16.4% | -30.9% | -29.4% | 543% | 665%
Class C | -17.7% | -26.2% | -26.2% | 559% | 671%
Class E | -14.7% | -24.7% | -23.7% | 545% | 419%
Overall | -16.4% | -27.8% | -26.9% | 549% | 594%
Class D | -19.8% | -26.9% | -27.3% | 545% | 768%
Class F | -22.1% | -31.3% | -30.6% | 448% | 474%
Class TGM | -30.4% | -37.0% | -36.7% | 458% | 388%
 | Low delay P Main 10 |  |  |  | 
 | Over VTM-11.0ecm8 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -15.5% | -30.7% | -28.6% | 501% | 648%
Class C | -17.2% | -25.5% | -24.9% | 481% | 736%
Class E | -14.2% | -22.9% | -23.1% | 514% | 481%
Overall | -15.7% | -27.0% | -26.0% | 497% | 627%
Class D | -19.9% | -27.0% | -27.5% | 462% | 750%
Class F | -21.2% | -31.3% | -30.0% | 436% | 436%
Class TGM | -27.6% | -35.1% | -35.0% | 490% | 361%
JVET-AD0006
(classical tools)

## Slide 10: NNVC 5.0
Tools overview

## Slide 11: NN-based Intra
Default ON in NNVC-5.0
neural networks:
for different block sizes
NN- input:
NN- outputs:
and denotes the index characterizing the LFNST),
of the VVC intra prediction mode (PLANAR or DC or directional intra prediction mode)
“Pre-processing”
subtract mean value,
replace unavailable by 0,
Normalize, re-shape
“Post-processing”
re-shape
return to 0....2b-1 range
cfg | Y | U | V | Y | U | V | Enc | Dec
RA | -1.8% | -0.5% | -0.9% | -1.7% | 0.1% | -0.1% | 1.2 | 1.8
LD-B | -0.4% | -0.0% | -0.2 | -0.4% | 0.2% | 0.6% | 1.1 | 1.3
AI | -3.6% | -3.2% | -3.3% | -3.6% | -2.8% | -2.6% | 1.8 | 6.9
 | BD-rate PSNR | BD-rate MS-SSIM | Run time
More improvements under study in EE1
JVET-AD0212
kMAC/pxl 8
Total Parameters Number 1.5 M
InterDigital

## Slide 12: NNLF for low OP
Number of hidden layers: n = 11
Feature maps and rank: K = 24, R = 24, M = 72
Default ON in NNVC-5.0
Dolby & Ittiam, Qualcomm
cfg | Y | U | V | Y | U | V | Enc | Dec
RA | -5.2% | -7.5% | -6.6% |  |  |  | 1.5 | 107
LD-B |  |  |  |  |  |  |  | 
AI | -4.7% | -5.9% | -5.9% |  |  |  | 1.3 | 61
 | BD-rate PSNR | BD-rate MS-SSIM | Run time
kMAC/pxl 16
Total Parameters Number 0.1 M

## Slide 13: Reduced Resolution Coding & NN-based super resolution
= PSNR {Orig, ((Orig2)2)} (complexity of image)
= 37,
=3
= 47 (RA cfg), 44 (all intra cfg)
QP_offset = 6 (SF=2.0); 4 (SF=1.5), 2(SF=1.25); 0 (SF=1.0)
– QP for full resolution coding (defines target quality)
QPi(SF) = + QP_offset
GOP1 GOP2 .....
Selection of GOPi(SF, QP_offset) w/o multi-pass coding
Scale Factor | Re-sampler | Y | U | V
1.0; 2.0 | RPR | -0.7% | -0.7% | -0.7%
1.0; 2.0; 1.5; 1.25 | RPR | -1.2% | 3.2% | 2.7%
1.0; 2.0 | NN-based | -1.8% | -1.9% | -1.6%
Implemented
but OFF NNVC-5.0
LGE,
Tencent..
cfg | Y | U | V | Y | U | V | Enc | Dec
RA | -1.8% | -1.9% | -1.6% | -16.1% | -14.5% | -12.8% | 1.1 | 4.6
LD-B |  |  |  |  |  |  |  | 
AI | -2.5% | -2.7% | -2.4% | -15.9% | -12.7% | -12.0% | 1.0 | 4.3
 | BD-rate PSNR | BD-rate MS-SSIM | Run time
kMAC/pxl 469
Total Parameters Number 4.5 M
results from
JVET-AB0098

## Slide 14: NN post-filter (in VSEI spec)
Basic NN structure: single model, no resBlocks, long activation
Input: Y  4 , U , V, QP, BS, Output: enhanced Y, U, V
RA BD-rate Y: ~2.5%,
VSEI text
JVET-AD2006
Nokia,
Qualcomm
cfg | Y | U | V | Y | U | V | Enc | Dec
RA | -5.0% | -18.7% | -17.1% | -4.5% | -19.1% | -16.9% | 1.5(*) | 288
LD-B |  |  |  |  |  |  |  | 
AI |  |  |  |  |  |  |  | 
 | BD-rate PSNR | BD-rate MS-SSIM | Run time
kMAC/pxl 34
Total Parameters Number 0.4 M
Implemented
but OFF NNVC-5.0
Feature: Biases are over fitted and signaled once per second
on-line training ~ encoding)RA BD-rate Y: ~5.0%

## Slide 15: NN- synthesis for Inter frame
 | is DRF | is DRF | Use TMVP | The calculation of
1 | × | × | √ | 
2 | × | √ | × | -
3 | √ | × | × | -
4 | √ | √ | √ | 
 |  |  | Use TMVP | 
1 | × | × | √ | 
2 | × | √ | × | -
3 | √ | × | × | -
4 | √ | √ | √ | 
  Modification of TMVP
Optical flow: L. Kong, B. Jiang, D. Luo, W. Chu, X. Huang, Y. Tai, C. Wang, and J. Yang. IFRNet: Intermediate feature refine network for efficient frame interpolation. IEEE/CVF Conference on Computer Vision and Pattern Recognition, 2022, pp. 1959-1968.
not yet in NNVC-5.0
Tencent
cfg | Y | U | V | Y | U | V | Enc | Dec
RA | -4.3% | -10.7% | -10.1% | -5.2 | -11.8% | -11.3% | 1.5 | 653
LD-B | -3.2% | -10.4% | -7.6% | -4.1% | -10.1% | -7.3% | 1.5 | 948
AI |  |  |  |  |  |  |  | 
 | BD-rate PSNR | BD-rate MS-SSIM | Run time
kMAC/pxl 329
Total Parameters Number 19.3 M
More improvements under study in EE1
JVET-AD0162

## Slide 16: High performance NN loop filters
kMAC/pxl 673
Total Parameters Number 3.1 M
cfg | Y | U | V | Y | U | V | Enc | Dec
RA | -9.8% | -21.1% | -20.5% | -9.7% | -20.9% | -19.3% | 1.5 | 489
LD-B | -8.9% | -17.8% | -19.2% | -8.6% | -16.5% | -19.0% | 1.6 | 448
AI | -7.5% | -16.8% | -17.4% | -7.8% | -17.9% | -18.15% | 1.4 | 274
 | BD-rate PSNR | BD-rate MS-SSIM | Run time
kMAC/pxl 615
Total Parameters Number 1.9 M
Tencent+
Bytedance+
Pixel
Shuffle
Att. Residual block 0...7
cfg | Y | U | V | Y | U | V | Enc | Dec
RA | -9.6% | -20.9% | -21.5% | -9.2% | -21.8% | -21.6% | 1.7 | 325
LD-B | -8.3% | -19.8% | -20.7% | -8.0% | -20.9% | -22.8% | 1.9 | 287
AI | -7.4% | -18.3% | -19.9% | -7.5% | -20.4% | -21.7% | 1.4 | 181
 | BD-rate PSNR | BD-rate MS-SSIM | Run time
not any mode in NNVC-5.0
Known hints: RDO with NN filter consideration (+0.3%), temporal filtration (+0.5%)
filter set#0
filter set#1

## Slide 17
Rec [3]
Pred [3]
BS [3]
QPbase
[1]
QPslice[1]
CONV 33,d1
CONV 33,d2
CONV 11,d3
CONV 11,d4
CONV 11,d4
PReLU
PReLU
PReLU
PReLU
PReLU
CONV
1  1, d6
PReLU
CONV2 3  3, C
PReLU
Back Bone Block, C
Back Bone Block, C
...
CONV
3  3
PReLU
CONV
3  3, 6
Pixel Shuffle
Rec Y
Rec UV [2]
RecEXT UV [2]
RecEXTY
2
Crop
N
CONV 3  1 CC21
[C,h,w]
CONV 1  1 (C1+C22)C
CONV 1  1 CC1
CONV 1  3 C21C22
CONV 1  3 CC31
CONV 3  1 C31C
PReLU
Back Bone Block C
[C,h,w]
Parameters selection:
d1 =192 C = 64 N = 24
d2 = 32 C1 =160 d6 = 48
d3 = 16 C21= 32
d4 = 16 C22= 32
d5 = 16 C31= 64
Crop
IPB [1]
CONV 33,d5
PReLU
Unified NNLF for High OP
~500 kMAC/pxl
~10% RA cfg gain vs VVC
Bytedance, Ericson, Qualcomm, Tencent, ...
in NNVC-5.0

## Slide 18: Unified training methodology
Training Model stage I (Intra artifacts)
Data extraction for intra from vanilla VTM
  encoder turns on md5sum, just NNVC-4.0 all NNVC tools disabled, encoder_intra_vtm.cfg, just first frame
  QPs = 22,27,32,37,42 + 19,24,29,34,39
  DIV2K (4:4:4 RGB  YUV420 10 bits, version ffmpeg to be specified, script is part of NNVC SW)
  Rotation, flipping, down-sampling (script to be provided by ByteDance + list of output + md5sum)
  Reconstruction is extracted before de-block
  All CTUs are extracted (except those on the border)  list of md5sums (NNVC SW coordinators to provide)  10 days
  Status check via e-mail
Model stage I training from scratch for Intra data:
  Random initialization (NNVC SW decide)
  Use all CTUs
  Learning Rate scheduler to be provided by Qualcomm
  Resume of training (track of learning rate, store check-points…, must be added to the training scripts) functionality is in training scripts to be adjusted for unified model
Status check via e-mail (learning curve)  10 days
 RA and all intra cfg results under AhG11 test condition (model uses only for Intra slice)
Training Model stage II (Inter artifacts)
Data extraction with model stage I:
  encoder turns on md5sum, NNVC-4.0 + Model stage I for I-frames only, encoder_ra_model1.cfg, 65 frames (last is duplicated), Intra Period 64, GOP=32.
  QPs = 22,27,32,37,42
  List of sequences
    TVD: 65 frames, 20 sequences (Tencent provides list of sequences with md5sum)
    BVI (YUV420), 620 sequences (Bytedance provides list of sequences with md5sum + script for duplication last frame duplicated)
    All reconstructed CTU are extracted before de-block , list of frames to be provided by Tencent and Bytedance (after check) + DVI2K training data as in training stage I
  Status check via e-mail  10 days
Model stage II training with extracted data:
  Random initialization (NNVC SW decide)
  Use all CTUs
  Rotation and flipping is part of training already
  Learning Rate scheduler to be provided by Qualcomm
  Resume of training (track of learning rate, store check-points…, must be added to the training scripts) functionality is in training scripts to be adjusted for unified model
 RA and all intra cfg results under AhG11 test condition
Status check via e-mail (learning curve) (likely telco will be needed) decide next stage  10 days
Training Model stage III (coding with NN enhanced ref. pic.)
Data extraction with Model stage II:
  encoder turns on md5sum, NNVC-4.0 + Model stage II (both Intra and Inter frames), encoder_ra_model1.cfg, 65 frames (last is duplicated), Intra Period 64, GOP=32.
  QPs = 22,27,32,37,42
  List of sequences
    TVD: 65 frames, 20 sequences (Tencent provides list of sequences with md5sum)
    BVI (YUV420), 620 sequences (Bytedance provides list of sequences with md5sum + script for duplication last frame duplicated)
    ALL reconstructed CTU are extracted before de-block , list of frames to be provided by Tencent and Bytedance (after check) + DVI2K training data as in training stage I
  Status check via e-mail  10 days
Model Stage III training with extracted data:
  Random initialization (NNVC SW decide)
  Use all CTUs
  Rotation and flipping is part of training already (on the fly augmentation)
  Learning Rate scheduler to be provided by Qualcomm
  Resume of training (track of learning rate, store check-points…, must be added to the training scripts) functionality is in training scripts to be adjusted for unified model
 RA and all intra cfg results under AhG11 test condition
Status check via e-mail (learning curve) + telco  10 days
SW prepared by JVET - AhG 14, announced, training to performed by at least 5 companies in parallel (== cross-check)

## Slide 19: New EE1 tests

## Slide 20: NN-based video coding visually
JVET-Z0053
In total 24 cases (videos/rate points) were viewed:
14 – NNLF#0 looks better than anchor
10 – NNLF#0 ~ anchor
0 – NNLF#0 looks worse than anchor
9 – NNLF#1 looks better than anchor
14 – NNLFF#1 ~ anchor
1 – NNLFF#1 looks worse than anchor (resolved later)
In total 8 cases (4K videos/rate points) were viewed:
3 – NNSR looks better than anchor
5 – NNSR ~ anchor
0 – NNSR looks worse than anchor
1 – RPR looks better than anchor
6 – RPR ~ anchor
1 – RPR looks worse than anchor
NNLF #0
NNLF #1
Reduced resolution Coding
Viewing conducted by AG5
in April, 2022

## Slide 21: VVC full size coding VVC scale factor 2 + NNSR

## Slide 22: VVC VVC + NNLF

## Slide 23: Any E2E AI video technology?
cfg | Y | U | V | Y | U | V | Enc | Dec
RA | -4.4% | 6.1% | 4.8% |  |  |  |  | 1.5
 | BD-rate PSNR | BD-rate MS-SSIM | Run time
Huawei
JVET-AA0063
OPPO, Xidian Uni
JVET-AA0059
cfg | Y | U | V | Y | U | V | Enc | Dec
RA | -3.6% | -4.5% | -3.4% |  |  |  | 0.3 | 1.5
 | BD-rate PSNR | BD-rate MS-SSIM | Run time
not yet mature enough for EE1
Intra-frame – E2E AI, Inter-frames – VVC Intra-frame – VVC, Inter-frames – E2E AI

## Slide 24: JVET NNVC summary
Common SW base
  NNVC 5.0
AI-based video coding development methodology keeps refining
  cross-checks, training, agreed complexity and performance metrics
Some visual benefits provided by NNVC were confirmed by viewing
  Both NNLF and NNSR
SADL - framework for NN tools
  100% controlled, operates in int16
Tools under study
  NN-loop filter (LOP ~16 kMAC/pxl, 5% gain, HOP ~500kMAC/pxl, 10% gain)
  NN-Super-resolution
  NN-Intra
  NN-post filter (VSEI)
  NN-based synthesized Inter