## Slide 1: JVET-AH0063: AHG12: On Shifting Quantization Center
Yue Yu
Haoping Yu, Luhang Xu, Jonathan Gan, Fan Wang, Zhihuang Xie, Dong Wang
JVET-AH0063

## Slide 2: Background
Dependent quantization (DQ) uses two quantizers.
Quantization index of DQ is calculated aswhere is the quantization level of Q0 or Q1 and actually coded in the bitstream, denotes signum function.
ECM-12.0 used to predict the rate and derive a dequantization shifting amount.
where is the dequantized coefficient, is the size of the lookup table, is the dequantized value,. .
JVET-AH0063

## Slide 3: Proposal
Applying the quantization center shifting in the transform skip mode.
The quantization level from Q0 and Q1 instead of quantization index of DQ is proposed to derive the shifting amount;
Because the dequantization value of Q1 is smaller than that of Q0 for the same quantization level due to DQ, this contribution proposes to use different sizes of tables for Q1 and Q0 to compensate this.
where indicates Q0 or Q1, is the dequantized coefficient, is the size of table, is the dequantized value of the quantization level from quantizer Qi,

## Slide 4: Simulation results
JVET-AH0063
Top: Transform skip only result, Bottom: Combination results. (The encoding and decoding time are not accurate)
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.01% | -0.01% | 0.04% | 101.0% | 102.0% | 100.3% | 100.0%
Class A2 | -0.01% | -0.03% | -0.01% | 100.5% | 101.1% | 100.0% | 100.0%
Class B | -0.01% | 0.03% | 0.03% | 100.7% | 100.5% | 99.3% | 100.0%
Class C | 0.00% | 0.01% | -0.02% | 101.7% | 101.8% | 100.3% | 100.0%
Class E | 0.01% | -0.10% | -0.07% | 100.9% | 101.3% | 100.0% | 100.0%
Overall | 0.00% | -0.01% | 0.00% | 101.0% | 101.3% | 99.9% | 100.0%
Class D | -0.03% | 0.19% | 0.04% | 101.5% | 105.5% | 100.0% | 100.0%
Class F | -0.05% | 0.11% | -0.04% | 101.2% | 102.5% | 100.0% | 100.0%
Class TGM | -0.14% | -0.04% | -0.19% | 100.7% | 102.2% | 100.0% | 100.1%
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.03% | -0.11% | -0.10% | 100.1% | 100.1% | 99.4% | 100.0%
Class A2 | -0.03% | 0.02% | -0.07% | 100.2% | 100.2% | 99.7% | 100.1%
Class B | -0.04% | -0.04% | -0.01% | 100.6% | 100.0% | 100.0% | 100.0%
Class C | -0.01% | -0.07% | -0.03% | 100.5% | 101.1% | 100.4% | 100.0%
Class E | -0.02% | 0.01% | -0.18% | 101.4% | 101.7% | 100.0% | 100.0%
Overall | -0.03% | -0.04% | -0.07% | 100.6% | 100.6% | 99.9% | 100.0%
Class D | -0.01% | 0.07% | -0.20% | 101.4% | 98.6% | 100.2% | 100.1%
Class F | -0.06% | 0.00% | -0.05% | 100.8% | 100.5% | 100.0% | 100.1%
Class TGM | -0.09% | -0.02% | -0.20% | 100.7% | 100.2% | 100.0% | 100.0%

## Slide 5: Conclusions
This contribution proposes to apply quantization center shifting in transform skip mode;
This contribution further proposes to use different size of tables to derive the shifting amount of Q0 and Q1
The simulation results show noticeable coding gain for all the classes of test content while no increase in complexity.
It is proposed to study this in the next round of EE
Thank Kwai and Interdigital for crosschecking this proposal.
JVET-AH0063