## Slide 1: JVET-AH AhG10: Distortion Propagation Factor for VVC Low-Delay Configuration
Hongwei Guo, Ce Zhu, Junjie Chen, Lei Luo (UESTC)
Yongkai Huo, Yutian Liu (Transsion)

## Slide 2: Proposed Method
JVET-AF0089 & JVET-AG0055
Pre-encode the frame with fixed QP and test mode
Calculate distortion propagation factor (DPF) for each block through its coding distortion and motion compensation predicted (MCP) error
Calculate the weight coefficient for each CTU through DPFs, and finally determine the CTU-level adaptive Lagrange multiplier and QP

## Slide 3: Updates to the method
Distortion propagation factor (DPF) of each coding block:
Distortion propagation length of key frames: 8
Distortion propagation length of non-key frames: 1 or 0 (pre-encoding is skipped)
: coding distortion
: MCP error
: configurable distortion propagation length

## Slide 4: Comparison with BIM
Block importance mapping (BIM): JVET-V0057 and JVET-Y0077.
Aspect | Block Importance Mapping (BIM) | Our Method
Function | CTU-level QP adaptation | 
Weights Determination | Based on motion compensation to calculate the weights of different CTUs | 
Estimation Avenue | MCP error → delta QP → Lagrange multiplier | MCP error & Coding distortion → Lagrange multiplier → QP
Motion Compensation Algorithm | Motion Compensation Temporal Filter (MCTF) | Pre-encoding
Modified Frames | Key frames (POC divisible by 8) I & B & P frames | Both key frames and non-key frames (configurable) B & P frames

## Slide 5: Results
DPFKeyLength = 8
DPFNonkeyLength = 1
DPFKeyLength = 8
DPFNonkeyLength = 0

## Slide 6: Results
DPFKeyLength = 12
DPFNonkeyLength = 1
DPFKeyLength = 12
DPFNonkeyLength = 0

## Slide 7: Results
BIM

## Slide 8: Subjective Results
BasketballDrill.Q22.jvet10.lb 220

## Slide 9: Conclusion
Over VTM-23.0, all frames pre-encoded:
  LDB: -4.09%, -4.13%, -3.40% {104%, 100%}
  LDP: -4.09%, -3.87%, -2.75% {104%, 100%}
Over VTM-23.0, only key frames pre-encoded:
  LDB: -3.78%, -3.09%, -2.21% {101%, 100%}
  LDP: -3.72%, -2.96%, -1.83% {102%, 100%}
This contribution proposes an updated version of the method in contribution JVET-AF0089 and JVET-AG0055.
Our method can provide coding performance benefits compared to the original scheme.
The encoding time of the proposed method is slightly increased. The pre-encoding of non-key frames can be skipped to reduce the time complexity.
A subjective video quality test was conducted and no compression artifact was observed.
It is recommended to adopt this proposed scheme into VTM under Low-Delay configuration.
Thanks to Xidian Univ. for the cross-check.

## Slide 10: Thanks
www.transsion.com