## Slide 1: JVET-AG0152 Ahg12: adaptive dual tree coding in B slices
F. Le Léannec, K. Naser, T. Dumas,
T. Poirier, F. Urban, E. François

## Slide 2: Partitioning in ECM
Similar design as in VVC with removed restrictions:
  Maximum CTU size increased to 256 for class A
  Latency constraint for small blocks in inter slices is removed
  VPDU constraint is removed
    BT/TT split modes
    CCLM latency restriction
    LMCS processing
Dual tree systematically used in intra slices
Single tree systematically used in inter slices

## Slide 3: JVET-AH0152 proposal
Adaptive dual tree coding of intra regions in inter slices
  Single tree coding down to block size 64x64
  For a non-split CU, skip flag and coding mode are signaled
  If intra, separate-tree CU-level flag is signaled
    If true: CU is root of a separate tree representation of luma and chroma
    IBC and Inter CUs excluded from local dual tree representation
  Dual tree inferred if CU luma size higher than a threshold
  Single tree inferred if CU luma size lower than a threshold
  No change in intra slices: dual tree only, regardless Intra/IBC coding mode

## Slide 4: Obtained typical behaviour

## Slide 5: Simulation results
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-12.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0,03% | -2,02% | -0,45% | 103,5% | 96,4% | 102,3% | 100,6%
Class A2 | 0,07% | -0,64% | -0,50% | 103,4% | 97,4% | 102,3% | 100,8%
Class B | -0,01% | -1,70% | -1,60% | 98,7% | 100,0% | 102,2% | 100,7%
Class C | -0,04% | -0,45% | -0,35% | 101,8% | 102,6% | 101,9% | 100,6%
Class E |  |  |  |  |  |  | 
Overall | 0,01% | -1,22% | -0,82% | 101,4% | 99,4% | 102,2% | 100,7%
Class D | 0,04% | -0,24% | -0,23% | 100,2% | 103,6% | 102,6% | 100,8%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!

## Slide 6: Conclusion
Adaptive dual tree choice at coding tree node level in inter slices
Coding gain in RA configuration
  RA: 0,01% / -1,22% / -0,82% (Y / Cb / Cr) 101,4% (EncT) 99,4% (DecT)
Propose to study in next EE2 round