## Slide 1: [AHG9]: Neural-network post-filter for tone mapping operations
AI0062, Claire-Hélène DEMARTY, Franck AUMONT, Laurent BLONDE, Erik REINHARD, Olivier LE MEUR

## Slide 2: Context (1/2)
At the 34th JVET meeting, it was proposed a new NNPF (Neural network post filter) purpose for Recovering Images from Energy-Aware Images (JVET-AH0126).
The Energy-Aware process (i.e., producing from an original image an image that will consume less when displayed) and its inverse process (i.e., recovering an image close to the original from an energy-reduced image) can be considered as Tone Mapping operations.
As it was suggested by the experts that NNPF should cover basic image processing operations, it is therefore proposed to add a new NNPF Tone Mapping purpose in the NNPF SEI message.

## Slide 3: Context (2/2)
To distinguish between tone mappers operating on the color, or on the brightness dimension, it is further proposed to add a sub-purpose to the Tone Mapping operation, related to brightness adaptation.
Some metadata related to brightness adaptation sub-purpose are also proposed, among which the amount of brightness adaptation and the appropriate display model, as suggested by the experts during the 34th JVET meeting.
Brightness adaptation can serve different goals from enhancing aesthetics to adapting the energy consumption of the content while displayed.

## Slide 4: Proposal (1/7)
The proposed modification and the associated semantics are detailed in Table 1.
The value of nnpfc_purpose shall be in the range of 0 to 511, inclusive, in bitstreams conforming to this edition of this document. Values of 512 to 65 535, inclusive, for nnpfc_purpose are reserved for future use by ITU-T | ISO/IEC and shall not be present in bitstreams conforming to this edition of this document.

## Slide 5: Proposal (2/7): Syntax

## Slide 6: Proposal (3/7): Syntax

## Slide 7: Proposal (4/7)

## Slide 8: Proposal (5/7)
The variables ChromaUpsamplingFlag, ResolutionResamplingFlag, PictureRateUpsamplingFlag, BitDepthUpsamplingFlag, ColourizationFlag, TemporalExtrapolationFlag, SpatialExtrapolationFlag, and ToneMappingFlag, specifying whether nnpfc_purpose indicates the purpose of the NNPF to include chroma upsampling, resolution resampling, picture rate upsampling, bit depth upsampling, colourization, temporal extrapolation, and tone mapping respectively, are derived as follows:
ChromaUpsamplingFlag = ( ( nnpfc_purpose & 0x02 ) > 0 ) ? 1 : 0 ResolutionResamplingFlag = ( ( nnpfc_purpose & 0x04 ) > 0 ) ? 1 : 0 PictureRateUpsamplingFlag = ( ( nnpfc_purpose & 0x08 ) > 0 ) ? 1 : 0 BitDepthUpsamplingFlag = ( ( nnpfc_purpose & 0x10 ) > 0 ) ? 1 : 0 ColourizationFlag = ( ( nnpfc_purpose & 0x20 ) > 0 ) ? 1 : 0 TemporalExtrapolationFlag = ( ( nnpfc_purpose & 0x40 ) > 0 ) ? 1 : 0 SpatialExtrapolationFlag = ( ( nnpfc_purpose & 0x80 ) > 0 ) ? 1 : 0
ToneMappingFlag = ( ( nnpfc_purpose & 0x100 ) > 0 ) ? 1 : 0

## Slide 9: Proposal (6/7)
nnpfc_tone_mapping_subpurpose indicates the sub-purpose of the tone mapping operation as specified in Table 2, where (nnpfc_tone_mapping_subpurpose & bitMask) not equal to 0 indicates the NNPF of purpose Tone Mapping has the sub-purpose associated with the bitMask value in Table 2.
The value of the nnpfc_tone_mapping_subpurpose shall be 1, in bitstreams conforming to this version of this Specification. Values of 2 to 255, inclusive, for nnpfc_tone_mapping_subpurpose are reserved for future use.
The variable TM_BrightnessAdaptationFlag specifying whether nnpfc_tone_mapping_subpurpose indicates the sub-purpose of the Tone Mapping NNPF to include brightness adaptation, is derived as follows:
TM_BrightnessAdaptationFlag = ( ( nnpfc_tone_mapping_subpurpose & 0x01 ) > 0 ) ? 1 : 0

## Slide 10: Proposal (7/7)
nnpfc_ratio_value, when ToneMappingFlag is equal to 1 and TM_BrightnessAdaptationFlag is equal to 1, specifies the expected percentage of brightness adaptation, through brightness decrease or increase (accordingly with the value of the nnpfc_ratio_sign_flag field), that the Tone Mapping post-filter should achieve. The percentage of brightness adaptation is to be considered relatively to the average brightness of the content before applying the NNPF Tone Mapping. The percentage ratio is computed using the following equation:
The expected brightness after application of the NNPF Tone Mapping may be derived as follows:
If == 1:
If nnpfc_ratio_sign_flag == 0:
nnpfc_ratio_sign_flag specifies if the value of nnpfc_ratio_value should be considered as negative or positive. If nnpfc_ratio_sign_flag equals 0, the use of the NNPF results in an increase of content brightness. If nnpfc_ratio_sign_flag equals 1, the use of the NNPF results in a decrease in terms of content brightness.
nnpfc_display_model is a bit field mask which indicates the recommended display models on which the tone mapping neural network post filter for brightness adaptation may be used.
For example, nnpfc_display_type_field= means that the NNPF can be used for both “Transmissive pixel” and “Emissive pixel” display models.

## Slide 11: Use case #1: Decrease energy consumption at display
With the hypothesis that energy consumption of display devices is correlated to the amount of emitted light, a NNPF Tone Mapping is used to decrease the brightness of the decoded content, thus decreasing its energy consumption when displayed onscreen.

## Slide 12: Use case #1: Decrease energy consumption at display
Neural network proposed in Le Meur, Olivier, Claire-Hélène Demarty, and Laurent Blondé. "Deep-learning-based energy aware images." ICIP 2023.
nnpfc_ratio_value, meaning that the brightness is adjusted by 10%, 20%, 40% and 60%, respectively.
nnpfc_ratio_sign_flag=1, indicating that the brightness should be decreased
Three sequences , 30 fps, 420, 8 bits:
  Mitsubishi_Traffic (299 frames)
  RedKayak_8bit (570 frames)
  RushFieldCuts_8bit (570 frames)
Quality metrics Y-PSNR, MS-SSIM, VMAF
Power consumption measurements were made on a LG42C2 screen

## Slide 13: Evolution of quality metrics for nnpfc_ratio_value in {10, 20, 40, 60}: Mitsubishi_Traffic
-10%
-20%
-40%
-60%
PSNR
MS SSIM
VMAF

## Slide 14: Evolution of quality metrics for nnpfc_ratio_value in {10, 20, 40, 60}: RedKayak_8bit
PSNR
MS SSIM
VMAF

## Slide 15: Evolution of quality metrics for nnpfc_ratio_value in {10, 20, 40, 60}: RushFieldCuts_8bit
PSNR
MS SSIM
VMAF

## Slide 16: Quality vs. measured Power: Mitsubishi_Traffic
-10%
-40%
-60%
-20%
PSNR
MS SSIM
VMAF

## Slide 17: Quality vs. measured Power: RedKayak_8bit
PSNR
MS SSIM
VMAF

## Slide 18: Quality vs. measured Power: RushFieldCuts_8bit
PSNR
MS SSIM
VMAF

## Slide 19: Use case #2: Increase energy consumption at display
Hypothesis: preprocessing prior to encoding through some adaptation (decrease) of its brightness. The energy-aware video content, i.e., with reduced brightness, is encoded, transmitted, and decoded.
At the decoder, two options:
Display decoded video content with a reduced brightness: the energy consumption of the display is lower;
When the energy constraint at the user side is relaxed (e.g., some extra energy is available), the NNPF Tone Mapping can be used to increase the value of the brightness, to recover a video content close to the original.
1
2

## Slide 20: Use case #2: Increase energy consumption at display
Neural network proposed in Le Meur, Olivier, and Claire-Hélène Demarty. "Invertible Energy-Aware Images. " IEEE Signal Processing Letters (2023).
nnpfc_ratio_value, meaning that the brightness is adjusted by 10%, 20%, 40% and 60%, respectively.
nnpfc_ratio_sign_flag=0, indicating that the brightness should be increased
Three sequences , 30 fps, 420, 8 bits:
  Mitsubishi_Traffic (299 frames)
  RedKayak_8bit (570 frames)
  RushFieldCuts_8bit (570 frames)
Quality metrics Y-PSNR, MS-SSIM, VMAF
Power consumption measurements were made on a LG42C2 screen

## Slide 21: Evolution of quality metrics for nnpfc_ratio_value in {10, 20, 40, 60}: Mitsubishi_Traffic
PSNR
MS SSIM
VMAF

## Slide 22: Evolution of quality metrics for nnpfc_ratio_value in {10, 20, 40, 60}: RedKayak_8bit
PSNR
MS SSIM
VMAF

## Slide 23: Evolution of quality metrics for nnpfc_ratio_value in {10, 20, 40, 60}: RushFieldCuts_8bit
PSNR
MS SSIM
VMAF

## Slide 24: Conclusion
This contribution offers new service opportunities and is timely, as the EU Energy Efficiency Directive [1] identifies the Information & Communication Technology (ICT) sector as an energy hungry sector (responsible for 5 to 9 % of the world’s total electricity use and more than 2 % of global emissions).
It is suggested to include this new purpose in the VSEI specification.
[1] https://energy.ec.europa.eu/topics/energy-efficiency/energy-efficiency-targets-directive-and-rules/energy-efficiency-directive_en