## Slide 1: JVET-AI0226: Longer motion compensation interpolation filter
Ruoyang Yu, Han Huang, Vadim Seregin, Marta Karczewicz

## Slide 2: Introduction
ECM uses 12-tap interpolation filter for luma motion compensation
In EE2 (3.10) of the previous meeting, sharp 12-tap interpolation filter for bi-prediction was proposed and has been adopted in this meeting

## Slide 3: Proposal
Following the same spirit of the EE and with attempt to preserve more high frequencies for bi-prediction, it is proposed to use longer (16-tap) interpolation filter for luma motion compensation.
Two sets of 16-tap interpolation filter are proposed, set0 and set1.
  Both sets are used for bi-prediction, uni-prediction uses existing ECM 12-tap interpolation filter
  set0 ”boosts” less high frequency than set1, and is activated for blocks that have both side greater than 32, or has one side equals to 4 (i.e., 4xN or Nx4 blocks)
  Filters are designed based on cosine-windowed sinc function

## Slide 4: Results
CTC RA and LDB
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | #VALUE! | #VALUE! | #VALUE! |  |  | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! |  |  | #NUM! | #NUM!
Class B | -0.01% | -0.01% | 0.03% |  |  | 100.1% | 100.0%
Class C | -0.31% | -0.16% | 0.09% | 103.8% | 104.7% | 99.9% | 100.0%
Class E |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! |  |  | #NUM! | #NUM!
Class D | -0.71% | -0.38% | -0.33% | 104.2% | 106.6% | 100.1% | 100.0%
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! |  |  | #NUM! | #NUM!
Class C | -0.28% | -0.19% | -0.59% |  |  | 100.1% | 100.1%
Class E | -0.05% | 0.27% | -0.38% |  |  | 100.0% | 100.2%
Overall | #VALUE! | #VALUE! | #VALUE! |  |  | #NUM! | #NUM!
Class D | -0.47% | -0.75% | 0.21% | 105.4% | 105.7% | 100.2% | 100.0%

## Slide 5: Conclusion
16-tap interpolation filters are proposed for luma bi-predictive motion compensation
Results indicate some good improvement for lower resolution classes, some more tests with different alternatives are still running to see if results for higher resolution classes can be improved
It is proposed to study using 16-tap interpolation filters in the next round of EE

## Slide 7: Appendix (Coefficients for filter set0 and set1)
Fractional sample position | Interpolation filter coefficients (set0) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0/16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 256 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1/16 | 0 | 0 | -1 | 2 | -3 | 6 | -14 | 254 | 16 | -7 | 4 | -2 | 1 | 0 | 0 | 0
2/16 | 0 | 1 | -2 | 4 | -7 | 12 | -26 | 249 | 35 | -15 | 8 | -5 | 3 | -2 | 1 | 0
3/16 | -1 | 2 | -4 | 7 | -11 | 19 | -38 | 242 | 54 | -22 | 13 | -8 | 5 | -3 | 2 | -1
4/16 | -1 | 3 | -5 | 8 | -13 | 22 | -44 | 230 | 76 | -31 | 18 | -11 | 7 | -4 | 2 | -1
5/16 | -1 | 3 | -5 | 9 | -15 | 25 | -49 | 216 | 98 | -38 | 21 | -13 | 8 | -5 | 3 | -1
6/16 | -2 | 4 | -7 | 11 | -17 | 28 | -53 | 201 | 119 | -43 | 24 | -15 | 9 | -5 | 3 | -1
7/16 | -1 | 3 | -6 | 11 | -17 | 28 | -53 | 182 | 141 | -48 | 26 | -16 | 10 | -6 | 3 | -1
8/16 | -1 | 3 | -6 | 10 | -17 | 28 | -51 | 162 | 162 | -51 | 28 | -17 | 10 | -6 | 3 | -1
9/16 | -1 | 3 | -6 | 10 | -16 | 26 | -48 | 141 | 182 | -53 | 28 | -17 | 11 | -6 | 3 | -1
10/16 | -1 | 3 | -5 | 9 | -15 | 24 | -43 | 119 | 201 | -53 | 28 | -17 | 11 | -7 | 4 | -2
11/16 | -1 | 3 | -5 | 8 | -13 | 21 | -38 | 98 | 216 | -49 | 25 | -15 | 9 | -5 | 3 | -1
12/16 | -1 | 2 | -4 | 7 | -11 | 18 | -31 | 76 | 230 | -44 | 22 | -13 | 8 | -5 | 3 | -1
13/16 | -1 | 2 | -3 | 5 | -8 | 13 | -22 | 54 | 242 | -38 | 19 | -11 | 7 | -4 | 2 | -1
14/16 | 0 | 1 | -2 | 3 | -5 | 8 | -15 | 35 | 249 | -26 | 12 | -7 | 4 | -2 | 1 | 0
15/16 | 0 | 0 | 0 | 1 | -2 | 4 | -7 | 16 | 254 | -14 | 6 | -3 | 2 | -1 | 0 | 0
Fractional sample position | Interpolation filter coefficients (set1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0/16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 256 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1/16 | -1 | 2 | -4 | 5 | -7 | 11 | -19 | 259 | 12 | -3 | 0 | 1 | -1 | 1 | -1 | 1
2/16 | -2 | 3 | -5 | 7 | -11 | 17 | -31 | 254 | 31 | -11 | 5 | -2 | 1 | 0 | 0 | 0
3/16 | -2 | 4 | -6 | 9 | -14 | 22 | -41 | 245 | 51 | -19 | 10 | -5 | 3 | -1 | 0 | 0
4/16 | -2 | 4 | -7 | 11 | -16 | 26 | -48 | 234 | 72 | -27 | 14 | -8 | 4 | -2 | 1 | 0
5/16 | -2 | 4 | -7 | 11 | -17 | 28 | -52 | 219 | 95 | -35 | 19 | -11 | 7 | -4 | 2 | -1
6/16 | -2 | 4 | -7 | 12 | -18 | 29 | -54 | 202 | 117 | -41 | 22 | -13 | 8 | -4 | 2 | -1
7/16 | -2 | 4 | -7 | 11 | -18 | 29 | -53 | 183 | 140 | -47 | 25 | -15 | 9 | -5 | 3 | -1
8/16 | -1 | 3 | -6 | 10 | -17 | 28 | -51 | 162 | 162 | -51 | 28 | -17 | 10 | -6 | 3 | -1
9/16 | -1 | 3 | -5 | 9 | -15 | 25 | -47 | 140 | 183 | -53 | 29 | -18 | 11 | -7 | 4 | -2
10/16 | -1 | 2 | -4 | 8 | -13 | 22 | -41 | 117 | 202 | -54 | 29 | -18 | 12 | -7 | 4 | -2
11/16 | -1 | 2 | -4 | 7 | -11 | 19 | -35 | 95 | 219 | -52 | 28 | -17 | 11 | -7 | 4 | -2
12/16 | 0 | 1 | -2 | 4 | -8 | 14 | -27 | 72 | 234 | -48 | 26 | -16 | 11 | -7 | 4 | -2
13/16 | 0 | 0 | -1 | 3 | -5 | 10 | -19 | 51 | 245 | -41 | 22 | -14 | 9 | -6 | 4 | -2
14/16 | 0 | 0 | 0 | 1 | -2 | 5 | -11 | 31 | 254 | -31 | 17 | -11 | 7 | -5 | 3 | -2
15/16 | 1 | -1 | 1 | -1 | 1 | 0 | -3 | 12 | 259 | -19 | 11 | -7 | 5 | -4 | 2 | -1

## Slide 8: Appendix (example of magnitude response)

## Slide 9: Appendix (phase delay of set0 and set1)