## Slide 1: JVET-AI0261 AHG 12: Rectangular Partitioning Restrictions
ALEXANDRE TISSIER
Mohsen Abdoli
Ramin G. Youvalari

## Slide 2: Introduction
The partitioning process supports QT plus the MTT partitioning structure which contains BT and TT that can be both applied horizontally and vertically.
Restrictions are applied to limit the complexity such as the maximum BT and TT sizes which defines the maximum blocks sizes where MTT is available.
Another restriction is the maximum MTT depth that does not allow MTT split when the current MTT depth of the block is higher.

## Slide 3: Rectangular partitioning restrictions
Enabling MTT for MTT restricted blocks in I-Slices
  Luma :
    Maximum BT size : 32 to 64
    Maximum TT size : 32 to 64
  Chroma :
    Maximum BT size : 64 to 128
    Maximum TT size : 32 to 128
No split available after MTT split applied on MTT restricted blocks

## Slide 4: Results
Test 1: Luma only :
  Maximum BT size : 32 to 64
  Maximum TT size : 32 to 64
Test 2: Chroma only :
  Maximum BT size : 64 to 128
  Maximum TT size : 32 to 128
Test 3: Luma and chroma only
  Maximum BT size luma / chroma : 32 to 64 / 64 to 128
  Maximum TT size luma / chroma : 32 to 64 / 32 to 128

## Slide 5: Conclusion
    Rectangular partitioning restrictions is proposed
    Enabling MTT for MTT restricted blocks in I-Slices
    No split is allowed after one MTT split is applied on MTT restricted blocks
    The proposed method obtains promising coding gains over ECM-13.0:
      Test 1 : AI configuration: -0.08%, -0.06%, -0.06% for Y, U, V
      Test 2 : AI configuration: -0.06%, -0.94%, -0.90% for Y, U, V
      Test 3 : AI configuration: -0.14%, -1.00%, -0.96% for Y, U, V
      RA configuration: -0.xx%, 0.xx%, 0.xx% for Y, U, V
    It is suggested to study the proposed method in next EE2 round