## Slide 1
JVET-AJ0093
A Neural Network Downscaling Filter for RPR
Y.-Q. Zhu, W.-X. He,
X. Li, J. Ye,
Q. Liu, Z. Lv

## Slide 2: Introduction
Motivation: to design a downscaling network to enhance RPR framework.
Key points:
Generate a low-resolution frame to replace the RPR down-sampled frame.
Use Original frame and RPR down-sampled frame as input.

## Slide 3: Network
Key points:
Two branch for Y and UV components.
Training scripts:
  Dataset: DIV2K, BVI-DVC, TVD
  Input: use a HR frame from 2× up-sampled original frame and a LR frame 2× down-sampled from the HR frame.
Complexity: 5.26kMAC/pxl, 0.022M

## Slide 4: Result
 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -1.63% | 3.06% | 4.03% | -3.14% | 0.87% | 2.56%
Class A2 | -1.41% | 8.57% | 10.19% | 0.08% | 10.11% | 9.69%
Avg. A1 & A2 | -1.52% | 5.82% | 7.11% | -1.57% | 5.49% | 6.12%
Coding performance over NNVC8.0 anchor
Coding performance over NNVC8.0 anchor with default RPR
 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -0.14% | -0.30% | -0.30% | -0.07% | -0.43% | -0.18%
Class A2 | -0.21% | -0.43% | -0.31% | -0.01% | -0.22% | -0.16%
Avg. A1 & A2 | -0.18% | -0.36% | -0.31% | -0.04% | -0.32% | -0.17%

## Slide 5: Conclusion
Proposed to introduce an NN-downscaling method to enhance RPR framework.
It is suggested to be adopted into NNVC.