## Slide 1: [AHG9]: On NNPF for brightness adaptation
AJ0147, Claire-Hélène DEMARTY, Edouard FRANCOIS, Olivier LE MEUR, Franck AUMONT

## Slide 2: Context (1/2)
At the 34th JVET meeting, a new NNPF (Neural network post filter) purpose for Recovering Images from Energy-Aware Images was proposed (JVET-AH0126).
At the 35th JVET meeting, a new NNPF purpose for Tone Mapping was proposed (JVET-AI0062)
During and since the 35th JVET meeting, some concerns were raised:
  How to handle the application of the proposed SEI in the case of the existence in the bitstream of other metadata related to Tone Mapping operations?
  What do TV makers think about the proposal?
  How the application of the proposed SEI interacts with the processes implemented in the TV and rendering devices?

## Slide 3: Context (2/2)
At this point, it is important to note that conflicts already exist between different types of metadata related to Tone Mapping operations, or between some existing NNPFs e.g., for Bit Depth upsampling and these metadata, independently of the proposal on the new NNPF purpose for Brightness Adaptation.
To answer these concerns:
  Some experiments were conducted that show that the proposed new NNPF brings additional energy gains and is complementary with already built-in TV modules for energy savings.
  To solve potential conflict issues, it is proposed to add usage guidance in the form of recommendation in the specification

## Slide 4: Experiments (1/7): comparison with TV built-in energy-saving modules
Usage workflow: the proposed NNPF will operate before any built-in energy-saving TV module.
As a consequence, TV modules will always be capable of adapting their processing to the content delivered by the NNPF.
Usage workflow

## Slide 5: Experiments (2/7): Protocol
On an LG42C3 TV screen, with a built-in energy-saving mode, adapting the screen brightness to the ambient light. This module is either OFF or in AUTO mode.
In a dark room (no window); light can be turned ON/OFF.
3 sequences: RushFieldCuts_8bit, Mitsubishi_Traffic and RedKayak_8bit.
5 different targets of brightness adaptation in the range [0%,60%] per sequence:
  [None, Low, Middle-Low, Middle-High, High]
Real power measures using a ZES Zimmer 661 power meter
6 different scenarios - Scenario #0 == BASE (no post processing by NNPF, nor by built-in TV module)
 | TV ambient light module | Light in the room | NNPF processing
Scenario #0 (Base) | OFF | Does not matter | No
Scenario #1 | AUTO | ON | No
Scenario #2 | AUTO | OFF | No
Scenario #3 | OFF | Does not matter | Yes
Scenario #4 | AUTO | ON | Yes
Scenario #5 | AUTO | OFF | Yes

## Slide 6: Results (3/7): Power gain compared to Scenario #0
Brightness reduction ratio | None (original) | Low | Middle-low | Middle-high | High
Scenario #0 | 0% | - | - | - | -
Scenario #1 | 6.9% | - | - | - | -
Scenario #2 | 15.2% | - | - | - | -
Scenario #3 | 0% | 3.1% | 4.8% | 9% | 12.9%
Scenario #4 | 6.9% | 9.3% | 10.8% | 13.5% | 16.1%
Scenario #5 | 15.2% | 16.3% | 17% | 18.4% | 19.9%
RushFieldCuts_8bit
Brightness reduction ratio | None (original) | Low | Middle-low | Middle-high | High
Scenario #0 | 0% | - | - | - | -
Scenario #1 | 6.1% | - | - | - | -
Scenario #2 | 13.6% | - | - | - | -
Scenario #3 | 0% | 5.8% | 7.7% | 11% | 14%
Scenario #4 | 6.1% | 11% | 12.1% | 14.4% | 16.3%
Scenario #5 | 13.6% | 16.3% | 16.8% | 18% | 19.1%
Mitsubishi_Traffic
Brightness reduction ratio | None (original) | Low | Middle-low | Middle-high | High
Scenario #0 | 0% | - | - | - | -
Scenario #1 | 9.4% | - | - | - | -
Scenario #2 | 19.6% | - | - | - | -
Scenario #3 | 0% | 3.4% | 6% | 11.7% | 17.2%
Scenario #4 | 9.4% | 11.5% | 13.5% | 17.6% | 21.5%
Scenario #5 | 19.6% | 21.1% | 22.1% | 24.1% | 26%
RedKayak_8bit

## Slide 7: Results (4/7): Power gain compared to Scenario #0
Brightness reduction ratio | None (original) | Low | Middle-low | Middle-high | High
Scenario #0 | 0% | - | - | - | -
Scenario #1 | 6.9% | - | - | - | -
Scenario #2 | 15.2% | - | - | - | -
Scenario #3 | 0% | 3.1% | 4.8% | 9% | 12.9%
Scenario #4 | 6.9% | 9.3% | 10.8% | 13.5% | 16.1%
Scenario #5 | 15.2% | 16.3% | 17% | 18.4% | 19.9%
Brightness reduction ratio | None (original) | Low | Middle-low | Middle-high | High
Scenario #0 | 0% | - | - | - | -
Scenario #1 | 6.1% | - | - | - | -
Scenario #2 | 13.6% | - | - | - | -
Scenario #3 | 0% | 5.8% | 7.7% | 11% | 14%
Scenario #4 | 6.1% | 11% | 12.1% | 14.4% | 16.3%
Scenario #5 | 13.6% | 16.3% | 16.8% | 18% | 19.1%
Brightness reduction ratio | None (original) | Low | Middle-low | Middle-high | High
Scenario #0 | 0% | - | - | - | -
Scenario #1 | 9.4% | - | - | - | -
Scenario #2 | 19.6% | - | - | - | -
Scenario #3 | 0% | 3.4% | 6% | 11.7% | 17.2%
Scenario #4 | 9.4% | 11.5% | 13.5% | 17.6% | 21.5%
Scenario #5 | 19.6% | 21.1% | 22.1% | 24.1% | 26%
Same range of energy savings from built-in module and NNPF post processing

## Slide 8: Results (5/7): Power gain compared to Scenario #0
Brightness reduction ratio | None (original) | Low | Middle-low | Middle-high | High
Scenario #0 | 0% | - | - | - | -
Scenario #1 | 6.9% | - | - | - | -
Scenario #2 | 15.2% | - | - | - | -
Scenario #3 | 0% | 3.1% | 4.8% | 9% | 12.9%
Scenario #4 | 6.9% | 9.3% | 10.8% | 13.5% | 16.1%
Scenario #5 | 15.2% | 16.3% | 17% | 18.4% | 19.9%
Brightness reduction ratio | None (original) | Low | Middle-low | Middle-high | High
Scenario #0 | 0% | - | - | - | -
Scenario #1 | 6.1% | - | - | - | -
Scenario #2 | 13.6% | - | - | - | -
Scenario #3 | 0% | 5.8% | 7.7% | 11% | 14%
Scenario #4 | 6.1% | 11% | 12.1% | 14.4% | 16.3%
Scenario #5 | 13.6% | 16.3% | 16.8% | 18% | 19.1%
Brightness reduction ratio | None (original) | Low | Middle-low | Middle-high | High
Scenario #0 | 0% | - | - | - | -
Scenario #1 | 9.4% | - | - | - | -
Scenario #2 | 19.6% | - | - | - | -
Scenario #3 | 0% | 3.4% | 6% | 11.7% | 17.2%
Scenario #4 | 9.4% | 11.5% | 13.5% | 17.6% | 21.5%
Scenario #5 | 19.6% | 21.1% | 22.1% | 24.1% | 26%
NNPF followed by TV built-in modules: increased energy savings
Both processings are complementary

## Slide 9: Results (6/7):
None
Low
Middle - Low

## Slide 10: Results (7/7):
High
Middle - High

## Slide 11: Proposal Option #1 (1/6): JVET-AI0062
The proposed modification and the associated semantics are detailed in Table 1.
The value of nnpfc_purpose shall be in the range of 0 to 511, inclusive, in bitstreams conforming to this edition of this document. Values of 512 to 65 535, inclusive, for nnpfc_purpose are reserved for future use by ITU-T | ISO/IEC and shall not be present in bitstreams conforming to this edition of this document.

## Slide 12: Proposal Option #1 (2/6): Syntax

## Slide 13: Proposal Option #1 (3/6)
The variables ChromaUpsamplingFlag, ResolutionResamplingFlag, PictureRateUpsamplingFlag, BitDepthUpsamplingFlag, ColourizationFlag, TemporalExtrapolationFlag, SpatialExtrapolationFlag, and ToneMappingFlag, specifying whether nnpfc_purpose indicates the purpose of the NNPF to include chroma upsampling, resolution resampling, picture rate upsampling, bit depth upsampling, colourization, temporal extrapolation, and tone mapping respectively, are derived as follows:
ChromaUpsamplingFlag = ( ( nnpfc_purpose & 0x02 ) > 0 ) ? 1 : 0 ResolutionResamplingFlag = ( ( nnpfc_purpose & 0x04 ) > 0 ) ? 1 : 0 PictureRateUpsamplingFlag = ( ( nnpfc_purpose & 0x08 ) > 0 ) ? 1 : 0 BitDepthUpsamplingFlag = ( ( nnpfc_purpose & 0x10 ) > 0 ) ? 1 : 0 ColourizationFlag = ( ( nnpfc_purpose & 0x20 ) > 0 ) ? 1 : 0 TemporalExtrapolationFlag = ( ( nnpfc_purpose & 0x40 ) > 0 ) ? 1 : 0 SpatialExtrapolationFlag = ( ( nnpfc_purpose & 0x80 ) > 0 ) ? 1 : 0
ToneMappingFlag = ( ( nnpfc_purpose & 0x100 ) > 0 ) ? 1 : 0

## Slide 14: Proposal Option #1 (4/6)
nnpfc_tone_mapping_subpurpose indicates the sub-purpose of the tone mapping operation as specified in Table 2, where (nnpfc_tone_mapping_subpurpose & bitMask) not equal to 0 indicates the NNPF of purpose Tone Mapping has the sub-purpose associated with the bitMask value in Table 2.
The value of the nnpfc_tone_mapping_subpurpose shall be 1, in bitstreams conforming to this version of this Specification. Values of 2 to 255, inclusive, for nnpfc_tone_mapping_subpurpose are reserved for future use.
The variable TM_BrightnessAdaptationFlag specifying whether nnpfc_tone_mapping_subpurpose indicates the sub-purpose of the Tone Mapping NNPF to include brightness adaptation, is derived as follows:
TM_BrightnessAdaptationFlag = ( ( nnpfc_tone_mapping_subpurpose & 0x01 ) > 0 ) ? 1 : 0

## Slide 15: Proposal Option #1 (5/6)
nnpfc_ratio_value, when ToneMappingFlag is equal to 1 and TM_BrightnessAdaptationFlag is equal to 1, specifies the expected percentage of brightness adaptation, through brightness decrease or increase (accordingly with the value of the nnpfc_ratio_sign_flag field), that the Tone Mapping post-filter should achieve. The percentage of brightness adaptation is to be considered relatively to the average brightness of the content before applying the NNPF Tone Mapping. The percentage ratio is computed using the following equation:
The expected brightness after application of the NNPF Tone Mapping may be derived as follows:
If nnpfc_ratio_sign_flag == 1
If nnpfc_ratio_sign_flag == 0
nnpfc_ratio_sign_flag specifies if the value of nnpfc_ratio_value should be considered as negative or positive. If nnpfc_ratio_sign_flag equals 0, the use of the NNPF results in an increase of content brightness. If nnpfc_ratio_sign_flag equals 1, the use of the NNPF results in a decrease in terms of content brightness.
nnpfc_display_model is a bit field mask which indicates the recommended display models on which the tone mapping neural network post filter for brightness adaptation may be used.
For example, nnpfc_display_type_field= means that the NNPF can be used for both “Transmissive pixel” and “Emissive pixel” display models.

## Slide 16: Proposal Option #1 (6/6)
When other metadata related to Tone Mapping operations or any operation modifying the brightness, contrast, luminance, colours or bit depth of an image are present in the bitstream together with the NNPFC SEI message with purpose corresponding to Tone Mapping, it is recommended that only one of these operations is considered.

## Slide 17: Proposal Option #2 (1/5)
A new NNPF purpose solely dedicated to Brightness Adaptation is proposed
The proposed modification and the associated semantics are detailed in Table 1.
The value of nnpfc_purpose shall be in the range of 0 to 511, inclusive, in bitstreams conforming to this edition of this document. Values of 512 to 65 535, inclusive, for nnpfc_purpose are reserved for future use by ITU-T | ISO/IEC and shall not be present in bitstreams conforming to this edition of this document.
Table 1: Modified list of purposes

## Slide 18: Proposal Option #2 (2/5) Syntax

## Slide 19: Proposal Option #2 (3/5)
The variables ChromaUpsamplingFlag, ResolutionResamplingFlag, PictureRateUpsamplingFlag, BitDepthUpsamplingFlag, ColourizationFlag, TemporalExtrapolationFlag, SpatialExtrapolationFlag, and BrightnessAdaptationFlag, specifying whether nnpfc_purpose indicates the purpose of the NNPF to include chroma upsampling, resolution resampling, picture rate upsampling, bit depth upsampling, colourization, temporal extrapolation, and tone mapping respectively, are derived as follows:
ChromaUpsamplingFlag = ( ( nnpfc_purpose & 0x02 ) > 0 ) ? 1 : 0 ResolutionResamplingFlag = ( ( nnpfc_purpose & 0x04 ) > 0 ) ? 1 : 0 PictureRateUpsamplingFlag = ( ( nnpfc_purpose & 0x08 ) > 0 ) ? 1 : 0 BitDepthUpsamplingFlag = ( ( nnpfc_purpose & 0x10 ) > 0 ) ? 1 : 0 ColourizationFlag = ( ( nnpfc_purpose & 0x20 ) > 0 ) ? 1 : 0 TemporalExtrapolationFlag = ( ( nnpfc_purpose & 0x40 ) > 0 ) ? 1 : 0 SpatialExtrapolationFlag = ( ( nnpfc_purpose & 0x80 ) > 0 ) ? 1 : 0
BrightnessAdaptationFlag = ( ( nnpfc_purpose & 0x100 ) > 0 ) ? 1 : 0

## Slide 20: Proposal Option #2 (4/5)
nnpfc_ratio_value, when BrightnessAdaptationFlag is equal to 1, specifies the expected percentage of brightness adaptation, through brightness decrease or increase (accordingly with the value of the nnpfc_ratio_sign_flag field), that the Brightness Adaptation post-filter should achieve. The percentage of brightness adaptation is to be considered relatively to the average brightness of the content before applying the NNPF Brightness Adaptation. The percentage ratio is computed using the following equation:
The expected brightness after application of the NNPF Brightness Adaptation may be derived as follows:
If nnpfc_ratio_sign_flag == 1
If nnpfc_ratio_sign_flag == 0
nnpfc_ratio_sign_flag specifies if the value of nnpfc_ratio_value should be considered as negative or positive. If nnpfc_ratio_sign_flag equals 0, the use of the NNPF results in an increase of content brightness. If nnpfc_ratio_sign_flag equals 1, the use of the NNPF results in a decrease in terms of content brightness.
nnpfc_display_model is a bit field mask which indicates the recommended display models on which the brightness adaptation neural network post filter may be used.
For example, nnpfc_display_type_field= means that the NNPF can be used for both “Transmissive pixel” and “Emissive pixel” display models.

## Slide 21: Proposal Option #2 (5/5)
When other metadata related to Tone Mapping operations or any operation modifying the brightness, contrast, luminance, colours or bit depth of an image are present in the bitstream together with the NNPFC SEI message with purpose corresponding to Brightness Adaptation, it is recommended that only one of these operations is considered.

## Slide 22: Conclusion
It is suggested to include this new purpose in the VSEI specification.