## Slide 1: Comments on the requirements for the next generation video coding standard
Jingxin Li (CESI), Yin Zhao (Huawei), Yuan Zhang (China Telecom), Siwei Ma (Peking Univ.), Hui Yuan (Shangdong Univ.), Qian Zhang (BOE)
m69713 / JVET-AJ0167

## Slide 2: Use case and requirement study is very important at this stage
Use cases and requirements impact the scope, target applications and technical goals of a standard
Reasonable, realistic and comprehensive work of standardization community on use cases and requirements would shorten the time between standard finalization and wide deployment.
Three related contributions (JVET-AH0199, JVET-AI0216, JVET-AI0247) were discussed in the last two meetings.
The proponents suggest discussing the requirements and use cases for the next generation video standard, by considering
  1) the feedback from industry on VVC deployment,
  2) the industrial needs that have not been fully fulfilled by VVC,
  3) the emerging industrial needs according to the development of new technologies and applications by year 2030 and beyond.
Existing markets and the needs for further technical improvement
Challenges and new opportunities
Future applications

## Slide 3: Suggestions from this contribution
A broad scope of requirements were collected and summarized in JVET-AI0247.
  A lot of video related applications (even include video editing that typically uses lightweight codecs like ProRes)
However, it may not be enough to just ambiguously define a lot of applications to be supported by a new video coding standard.
  For targeting applications, it is better to be more specific on how the new standard will be more attractive than the existing standards (e.g., VVC and HEVC), so that industry will embrace the new standard.
  Besides, it’s better to figure out, for major targeting applications, the required coding efficiency improvement as well as affordable complexity/cost/power consumption increase.
In this contribution, some comments are made to further clarify some requirements. Further steps related to the requirements and to the test conditions are also suggested.

## Slide 4: Comment 1: On encoder and decoder complexity for mobile applications
Mobile devices (e.g., smartphone) already support 4K 60/120fps video recording and playback.
  Software based encoding and decoding is not possible to meet the encoding & decoding speed and power consumption constraint. Hardware codec is a better choice.
VVC encoder (vs. HEVC encoder) is possible to reach 25% coding efficiency gain with 3x chip area size.
Power consumption of a 4K@60 HEVC encoder (5nm process) on a smartphone is approximately 100mA.
Process: N5 -> N3E -> N2P -> A16
Power: 100% ~66% ~46% ~40%
Year: 2020 2026
4K@60 recording | HEVC | VVC | New Gen
Bitrate | 100% | 75% | 56%
Chip size | 1x | 3x | 9x
Power consumption (5nm) | 100mA | 300mA | 900mA
Power consumption (1.6nm) | 40mA | 120mA | 360mA
What if New Gen continues with this trade-off?
Assuming by year 2030 and beyond, A16 process is widely used for smartphones, to ensure the encoder power consumption under more advanced A16 process will not be much larger than that of HEVC encoder with N5 nowadays (e.g., < 200 mA), the encoder complexity should be less than 5x HEVC.

## Slide 5: Comment 1: On encoder and decoder complexity for mobile applications
Requirements on compression efficiency can be formulated as follows.
Decoding complexity increment compared to VVC is no more than 2.
Under traditional test conditions: 40% BD-rate gain with no more than 10 encoding complexity.
Significant part of this rate reduction must come from low-complexity encoder techniques. Under constrained encoder complexity: 25% BD-rate gain over VVC (with encoder constrained to reflect real-time encoder), with no more than 1.5 encoding complexity is desirable.
It is recommended to establish an AhG on the low-complexity real-time coding to develop test condition reflecting real-time encoding case, and to explore technologies that are more competent for real-time coding applications with constrained complexity and power consumption.
Such test conditions are not intended to replace traditionally used in WG5 test conditions (which reflect off-line encoding use case), but will be used as additional test configuration.
It is highly desirable to extend complexity assessment beyond CPU encoding/decoding run time which is traditionally used in JVET, considering at least power consumption on mobile devices.
Complexity increase can be compensated by advanced semiconductor process
Maybe still commercially beneficial for VOD business with offline encoding
Good trade-off for low-complexity encoding use cases.

## Slide 6: Comment 2: On ultra-low-delay communication
To achieve stable ultra low latency, it needs more than fast encoding and decoding
  With hardware codec + multi-slice coding, the delay from codec can be as low as ~6 ms.
Among all the modules, the most unstable processing time or delay is from transmission.
  The transmission delay is influenced by network condition.
  When a packet loss happens in the transmission process because of transmission congestion or bit error in the air interface, the decoder cannot start decoding a frame even if all other packets of the frame have been received successfully.
  Re-transmission of lost packet increases latency by a Round Trip Time (RTT) (usually > 20 ms), and thus increase considerable latency under such ultra-low-delay applications.
 | Low-delay broadcasting / Live streaming | Video call/video conference | Ultra low delay RTC (e.g., cloud gaming, tele-driving, screen casting)
Desirable e2e latency | 1~2 s | 200~500 ms | 50~100 ms
Capture / rendering
encoding
transmission
decoding
display
~4ms
~2ms
~16ms
~16ms
60fps
4 slices
15 ~ ? ms
User instruction transmission, 10ms
Cloud/edge
Cloud gaming, VDI
Device collaboration

## Slide 7: Comment 2: On ultra-low-delay communication
Wireless communication has large instantaneous bandwidth fluctuation due to signal fading and interference.
  It seems an inevitable problem for mobile devices since they are connected to Internet or with other devices via wireless network.
It is not only a problem for wireless communication. For the ethernet, the bandwidth fluctuation may also be significant, “approximately 5.6% of Ethernet users encounter at least five occurrences of dramatic bandwidth reduction (i.e. reduction by more than 50% within 100ms) per minute” [6].
Fig. 1 WiFi bandwidth fluctuation measured in an indoor environment.
Fig. 2 The bandwidth fluctuation when the car is running on the road (4G network)

## Slide 8: Comment 2: On ultra-low-delay communication
Such dramatic bandwidth change at millisecond-level granularity is challenging for rate control
  It is difficult for bandwidth estimation to be reliable in such a case.
  Converging to a new bitrate need some time. RPR helps much in quick bitrate adaptation in this case, but still it is relied on bandwidth estimation.
All in all, in the ultra-low-delay scenarios, the challenge to the video decoder is that it cannot always receive all packets in time.
  Some packets may be lost/discarded, while some may arrive later than expected.
It is recommended to establish an AhG on ultra-low-delay coding to collect requirements, use cases, evaluation criteria, test conditions, test materials for the ultra-low-delay application scenarios.

## Slide 9: Comment 3: on HDR video coding
HDR has been supported by more and more capturing devices and displays. HDR content is provided widely as premier services by OTT service providers.
Proponents welcome the Call for new HDR materials for future video coding development [8] issued by WG5.
It is recommended to include a wide set of modern HDR test materials into the CTC of the new generation video coding standard.
A quality metric well correlated with subjective quality should be verified and used in the common test conditions.

## Slide 10: Comment 4: on UGC and PUGC video coding
User Generated Video (UGC) and Professional User Generated Content (PUGC) are getting increased popularity. Like PGC (movie/episodes/news), UGC/PUGC content has become part of people’s life.
It is recommended to include some UGC and PUGC content in the CTC of the new generation video coding standard, e.g., some videos recorded by smartphones, some videos produced by post-production with compressed source materials, some videos with color grading to be more vivid.
CTC camera captured sequences:
(more on PGC video capture)
UGC content:
HEVC bitstream
Video editing
YUV420
HEVC bitstream
(lower bitrate)
Transcoding
encode
encode
PUGC content:
HEVC bitstream
Video editing &
Color grading
YUV420
encode
RGB-to-YUV
conversion
Livestreaming:
Server

## Slide 11: Comment 5: on other emerging types of video coding
Immersive VR applications. Some new format was noticed.
Video coding for machines is an emerging use case.
It is recommended to consider better support of machine analysis as a feature of the new standard.
RF5.2mm F2.8 L DUAL FISHEYE
+
=
EOS R5 – High Resolution and High Speed 8K Full-frame Mirrorless Camera
Rectified to stereoscopic video for 180-degree 3D VR streaming
Fisheye video
[9] https://www.youtube.com/watch?v=OJAr7SbVGBg
[9]

## Slide 12: Conclusion
It is recommended to study the requirements of a new generation video coding standard more thoroughly during the next several meeting cycles, to make the technology under development better aligned with the needs from the video industry.
  A clear vision of a standard helps identify its value and advantages over existing standards such as VVC and HEVC.
  The vision and goals of the new standard should be discussed in parallel with the exploration on new coding technologies.
To facilitate the development of technologies targeting at new use cases, additional test conditions simulating applications that have not been addressed well by the current common test conditions should be further studied and established.
It is recommended to establish one AhG on low-complexity real-time coding, and one AhG on ultra-low-delay coding.

## Slide 13
Thank you.

## Slide 14: References
[1] “On the requirements and use cases of new-generation video coding standard”, JVET-AH0199, Rennes, France, April 2024.
[2] “On Future Video Codec Design and Evaluation”, JVET-AI0216, Sapporo, Japan, July 2024.
[3] “Proposed timeline and requirements for the next generation video coding standard”, JVET-AI0247, Sapporo, Japan, July 2024.
[4] https://www.anandtech.com/show/21408/tsmc-roadmap-at-a-glance-n3x-n2p-a16-2025-2026
[5] J. van der Hooft et al., "HTTP/2-Based Adaptive Streaming of HEVC Video Over 4G/LTE Networks," in IEEE Communications Letters, vol. 20, no. 11, pp. 2177-2180, Nov. 2016.
[6] Wang, Shibo, et al. "Pudica: Toward {Near-Zero} Queuing Delay in Congestion Control for Cloud Gaming." 21st USENIX Symposium on Networked Systems Design and Implementation (NSDI 24). 2024.
[7] Meng, Zili, et al. "Hairpin: Rethinking packet loss recovery in edge-based interactive video streaming." 21st USENIX Symposium on Networked Systems Design and Implementation (NSDI 24). 2024.
[8] E. François, W. Husak, S. Iwamura, D. Rusanovskyy, A. Segall, M. Wien, Call for new HDR materials for future video coding development, JVET-AI2034.
[9] Shoot VR with Canon’s New RF5.2mm F2.8 L Dual Fisheye Lens, https://www.youtube.com/watch?v=OJAr7SbVGBg