## Slide 1: JVET-AJ0194 AHG12: Extended IntraTMP merge candidate list with an improved fusion mode
Damian Ruiz Coll, Jung-Kyung Lee
(Ofinno)

## Slide 2: AHG12: Extended IntraTMP merge candidate list with an improved fusion mode
Current IntraTMP merge and AR-BVP lists in ECM-14.0
  Only the first BV fusion candidate among the 5 fusion BVs is selected for the IntraTMP merge list and AR-BVP lists.
  For the BVs encoded with IntraTMP fusion mode, the fusion model is always signaled to the decoder.
  For the non-fusion candidates, the BV candidate indicated by the IntraTMP index is selected for the IntraTMP merge list, and the first BV in the IntraTMP list if such TMP index is not 0.
PROPOSAL
  Check the full set of fusion BV candidates (up to 5) for neighboring blocks coded in TMP fusion mode.
  Improved IntraTMP fusion mode with derivation of fusion model for fusion groups 1 and 2.
  Check up to 3 non-fusion BV candidates (candidates with lower template cost) beyond the first index for neighboring blocks coded in TMP mode.

## Slide 3: AHG12: Extended IntraTMP merge candidate list with an improved fusion mode
PROPOSAL
  Check the full set of fusion BV candidates (up to 5) for neighboring blocks coded in TMP fusion mode.
    SAD-based model: Skip candidates if fusion weight Wi< ThSAD
    Gaussian solver model: Skip candidates if fusion parameter Pi < ThGAUSS
  Improved IntraTMP fusion mode with derivation of fusion model for fusion groups 1 and 2.
The SAD fusion group 0 (most likely ) is signaled just with one bin.
Fusion groups 1 and 2 for both models are signaled with the same code, and the fusion model is determined based on the fused template’s cost.
TMP Fusion Model | Fusion Group | Ecm-14.0 | Proposed
SAD | 0 | 00 | 0
 | 1 | 010 | 110
 | 2 | 011 | 111
Gaussian solver | 0 | 10 | 10
 | 1 | 110 | 110
 | 2 | 111 | 111
Updated fusion group and model bins

## Slide 4: Results
  Simulation results on top of ECM-14.0 for AI/RA

## Slide 5: Conclusion
Extended the IntraTMP merge and AR-BVP lists by checking the whole set of fusion BVs.
Improved fusion model signaling based on fused template cost
Extended the IntraTMP merge and AR-BVP lists by checking up to 3 non-fusion BVs.
Provides Luma gain of -0.04% in AI with a slight enc/dec runtime increase.
Propose for study in the next round of EE2.
Thank you to ETRI for the crosschecking.