## Slide 1: JVET-AJ0216 Non-EE2: On interpolation filter for intra template prediction C. Zhou, Z. Lv, G. Wang

## Slide 2: JVET-AJ0216
In ECM, the single 4-tap DCTIF is used for the template prediction, and the related tools include TIMD, MPM reorder, etc.
The interpolation filter type is determined as follows, using a unified strategy as in intra block prediction:
If all of following conditions are true, [1 2 1]/4 filter is is applied for reference samples:
The current block size is greater than 32
The directional mode is integer angles
If minDistVerHor is greater than intraHorVerDistThres[ nTbS ]
If all of following conditions are true, 4-tap/6-tap SIF is used for the interpolation:
The current block size is greater than 32
The directional mode is non-fractional angles
If minDistVerHor is greater than intraHorVerDistThres[ nTbS ]
Otherwise, 6-tap DCTIF is used for the interpolation.
The 6-tap DCTIF is always apply for TMRL mode.
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.04% | 0.00% | -0.04% | 100.2% | 98.8% | 99.8% | 100.1%
Class A2 | -0.01% | -0.12% | -0.01% | 100.5% | 98.2% | 100.0% | 100.2%
Class B | -0.01% | 0.00% | 0.14% | 99.8% | 99.6% | 102.3% | 100.0%
Class C | -0.03% | 0.00% | -0.08% | 99.6% | 99.3% | 100.5% | 100.0%
Class E | -0.04% | 0.14% | 0.09% | 99.6% | 99.3% | 101.1% | 100.0%
Overall | -0.02% | 0.01% | 0.03% | 99.9% | 99.1% | 100.9% | 100.0%

## Slide 3: Conclusion
It is proposed to a unified interpolation filter selection strategy as in intra block prediction for template prediction.
On top of ECM-14.0, it achieves 0.02% coding gain for luma component
It is suggested to investigate in the next round of EE2.
Thanks Alibaba for cross-checking!

## Slide 4
THANK
YOU