## Slide 1: JVET-AJ0128 Non-EE2: Multiple filter taps for EIP C. Zhou, Z. Lv, G. Wang

## Slide 2
In ECM, the EIP mode uses a 15-tap filter for prediction as below:
It is proposed to support two filter taps: 15-tap and 9-tap. An index is signaled to indicate which filter tap is used. The 9-tap filter is shown as below:

## Slide 3
Results
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.02% | -0.14% | -0.02% | 101.4% | 99.5% | 100.0% | 100.1%
Class A2 | -0.01% | -0.03% | -0.01% | 101.2% | 98.9% | 100.5% | 100.3%
Class B | -0.01% | -0.01% | 0.01% | 101.1% | 99.8% | 103.3% | 99.9%
Class C | -0.04% | -0.02% | 0.00% | 100.4% | 99.6% | 100.0% | 100.0%
Class E | -0.06% | 0.12% | 0.18% | 100.6% | 99.8% | 101.1% | 100.0%
Overall | -0.03% | -0.02% | 0.03% | 100.9% | 99.6% | 101.2% | 100.0%
Class D | -0.01% | 0.01% | -0.03% | 100.6% | 100.0% | 99.7% | 100.0%
Class F | -0.05% | -0.03% | -0.17% | 100.0% | 99.3% | 96.2% | 99.9%

## Slide 4: Conclusion
It is proposed to a multiple filter taps method, which can reduce the complexity of EIP.
On top of ECM-14.0, it achieves 0.03% coding gain for luma component.
It is suggested to investigate in the next round of EE2.
Thanks OPPO for cross-checking!

## Slide 5
THANK
YOU