## Slide 1: JVET-AJ0238: OBMC modifications
Ruoyang Yu

## Slide 2: Introduction
For a GPM block with its two partitions coded with non-affine inter, blending operation (which blends two motion compensated partitions) is performed first, and then MVs are stored into 4x4 units according to the blending weights, and finally OBMC is carried out
For an inter block with subblock motion, the current OBMC is performed on CU boundary first, and then on inner subblock boundary

## Slide 3: Proposal
The main idea of the proposal is to adjust OBMC operation order
  Modification 1: For a GPM block with its two partition coded with non-affine inter, OBMC is carried out first for the two partitions separatly, and followed by blending operation
    If the corresponding parition contains subblock motion, OBMC is then also applied on those subblock boundaries
  Modification 2: For an inter block with subblock motion, OBMC is performed on inner subblock boundary first, and then on CU boundary

## Slide 4: Result
RA and LDB under ECM CTC
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.03% | -0.18% | -0.22% | 100.5% | 100.5% | 100.1% | 100.0%
Class A2 | -0.06%* | 0.00% | -0.11% | 100.5% | 100.3% | 99.7% | 99.7%
Class B | -0.07% | 0.02% | -0.05% | 101.3% | 99.6% | 99.8% | 99.7%
Class C | -0.07% | -0.14% | 0.04% | 101.2% | 100.7% | 99.4% | 99.2%
Class E |  |  |  |  |  |  | 
Overall | -0.06%* | -0.07% | -0.07% | 100.9% | 100.2% | 99.7% | 99.6%
Class D | -0.05% | -0.21% | -0.29% | 100.7% | 100.2% | 99.2% | 98.9%
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-14.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class C | -0.06% | -0.09% | -0.16% | 100.1% | 100.2% | 98.9% | 98.5%
Class E | -0.02% | -0.16% | -0.94% | 100.2% | 99.3% | 100.3% | 100.2%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class D | 0.02% | 0.26% | 0.26% | 100.3% | 97.8% | 99.1% | 99.0%

## Slide 5: Conclusion
Two modifications regarding to OBMC operation order are proposed
The modifications are relatively straightforward, and demonstrate some BD-rate benefits
Suggest to study the modifications in the next round of EE2