## Slide 1
JVET-AJ0254
AHG8: Pre-analysis based adaptive temporal resampling algorithm for machine vision
Shurun Wang, Jie Chen, Yan Ye, Binzhe Li(Alibaba group)
Shiqi Wang (CityUHK)

## Slide 2
Outline
Algorithm description
Performance
Conclusion

## Slide 3
Temporal resampling framework
Pre-analysis : determine the resampling ratio
Temporal Down-sampling
Encoder
Decoder
Temporal Up-sampling
Machine Analysis

## Slide 4
Pre-analysis based adaptive algorithm
Video content is diverse: Pre-analysis based adaptive algorithm is necessary
Temporal complexity measurement:
  Mean intersection of union (MIOU) based
  Sequence level MIOU, .
  Frame level MIOU, .
  is derived based on .
  In different configurations (RA/LD/AI), the calculation methods of are different.

## Slide 5
Notations
Given a frame pair (), The detection results of each frame are:
  ,
  : the coordinates of the bounding box top-left center
  and : the width and height of bounding box
  and are the object class and the confidence score of bounding box, where , indicating the possibility of correct detection.
By comparing the intersection of union () for the bounding boxes in and ,
  Matched box pairs can be achieved, noted as:
  , where .
  Calculation between paired boxes, and
A
B
C
C
A
B
C
+
+

## Slide 6
Frame level MIOU,
Based on the definition in [1], paired bounding boxes are classified into 3 groups.
  Small : ; Medium :; Large:
  Noted as . Specifically,
    . is the class number in .
Calculate
  Calculate the IOU of class in group :
  Calculate MIOU of group :
  The frame-level MIOU is defined as
Based on the definition in [2]
[1] Lin, Tsung-Yi, et al. "Microsoft coco: Common objects in context." Computer Vision–ECCV 2014: 13th European Conference, Zurich, Switzerland, September 6-12, 2014, Proceedings, Part V 13. Springer International Publishing, 2014.
(1)
(2)
For object tracking task, only the meaningful and moving object classes would be considered, such as person, car and bus, etc.

## Slide 7
Sequence level MIOU,
is calculated based on .
For simplicity, only the first 33 frames of video sequence are calculated.
For resampling ratio2:
  For RA:
    Frame pairs are
    Frame-level MIOUs are {}
  For LD:
    Frame pairs are {, with interval 8
  For AI:
    Frame pairs are {, with interval 2
For resampling ratio 4, the intervals are equally scaled up with factor 2
Interval 8
Interval 16
Interval 32
(3)

## Slide 8
Adaptive temporal resampling ratio decision
For sequence-level MIOU
Decision metric
    Here, is the sum of confidence score, , .
Given a video sequence and coding configuration, the decision metric for resampling ratio 2 and 4 are and .
Decision rule:
  If and , resampling ratio is 4.
  If and , resampling ratio is 2.
  Otherwise, resampling ratio is 1. Temporal resampling is not performed.
(4)

## Slide 9
Performance-SFU-HW dataset
SFU-HW | Metric | BD-rate (%) |  | BD-mAP
Config | Class Name | Mono-mAP | mAP | 
RA | Class A | 0.00% | 0.00% | 0.00
 | Class B | -4.28% | / | 1.20
 | Class C | 1.61% | -0.06% | -0.31
 | Class D | -7.49% | -6.18% | 1.01
 | Average | -3.13% | / | 0.59
LD | Class A | -12.73% | -12.57% | 2.63
 | Class B | -17.14% | / | 5.38
 | Class C | -14.60% | -15.06% | 2.65
 | Class D | -25.03% | -23.15% | 4.19
 | Average | -18.45% | / | 3.96
AI | Class A | -72.56% | -72.43% | 32.02
 | Class B | -63.18% | / | 24.31
 | Class C | -68.33% | -68.24% | 18.02
 | Class D | -70.21% | -70.30% | 18.68
 | Average | -67.65% | / | 21.24

## Slide 10
Performance-TVD dataset
TVD | Metric | BD-rate (%) |  | BD-MOTA
Config | Sequence Name | Mono-MOTA | MOTA | 
RA | TVD-01-1 | 0.00% | / | 0.00
 | TVD-01-2 | 0.00% | 0.00% | 0.00
 | TVD-01-3 | -8.24% | / | 0.79
 | TVD-02-1 | -2.48% | / | -0.62
 | TVD-03-1 | -4.89% | -2.44% | 0.60
 | TVD-03-2 | -26.24% | / | 2.05
 | TVD-03-3 | 2.40% | -1.39% | -0.47
 | Average | -5.64% | / | 0.34
LD | TVD-01-1 | -13.44% | / | 1.46
 | TVD-01-2 | -33.47% | -33.99% | 3.09
 | TVD-01-3 | -42.49% | -46.17% | 4.16
 | TVD-02-1 | -38.06% | / | 1.57
 | TVD-03-1 | -23.12% | -24.69% | 3.99
 | TVD-03-2 | -41.75% | -40.53% | 3.92
 | TVD-03-3 | -26.38% | -27.33% | 2.07
 | Average | -31.25% | / | 2.89
AI | TVD-01-1 | -71.54% | -71.62% | 16.78
 | TVD-01-2 | -74.28% | -73.72% | 13.45
 | TVD-01-3 | -70.98% | -70.88% | 12.21
 | TVD-02-1 | -66.88% | -67.48% | 5.53
 | TVD-03-1 | -75.15% | -74.97% | 19.91
 | TVD-03-2 | -75.81% | -75.44% | 16.26
 | TVD-03-3 | -74.43% | -75.18% | 16.05
 | Average | -72.72% | -72.76% | 14.31

## Slide 11
Conclusion
The proposed algorithm effectively improves the compression performance of VVC under different configurations.
It is suggested:
  Include the implementation in AHG8 software branch.
  Add the following highlighted sentence to section 7.3 of the next draft of technical report (TR)
  Include the algorithm description (section 1 of proposal document) to the annex of TR
“In some use cases, for example when the frame rate is high, a way to reduce the bit rate without a strong negative impact on the machine consumption performance is to skip certain frames and encode the video at a lower frame rate. One example is to remove every other frame from the input video and encode the video at half frame rate. This can be done in a dynamic manner, for example by evaluating the motion between two or more frames (e.g., evaluating the mean intersection of union (MIOU) based on an object detection pre-analysis module) and if there is only little motion, a frame can be removed. Motivated by dynamic motion of various sequences, the frame resampling ratio can be adaptively determined and signaled in the bitstream via SEI messages. In some cases, if the receiving system requires a specific frame rate, a corresponding post-processing technology that up-samples to full frame rate needs to be applied.”
Thanks for the crosscheck of Ericsson

## Slide 12
实验室名称
Thanks！