## Slide 1: JVET-AJ0299 AHG12: Intra TMP improvements
M. Radosavljević, F. Le Léannec, K. Naser, T. Dumas

## Slide 2: Proposed improvements to Intra TMP
HMVP usage in Intra TMP merge mechanism
    Inspired from contribution JVET-AG0074
    History-based list of BVs is maintained similarly to HMVP
    HMVP candidates added after adjacent and non-adjacent spatial candidates and before ARBVP candidates

## Slide 3: Proposed improvements to Intra TMP
Increased Maximum Distance for Non-adjacent Intra TMP merge candidates
  Increased from 4 to 7
  7 rows/columns of spatial neighboring blocks (in terms of current CU width/height) can be used for non-adjacent Intra TMP merge

## Slide 4: Proposed improvements to Intra TMP
Improved CABAC context for Intra TMP-LIC flag signaling
2 contexts are used instead of 1
the context to signal LIC flag is chosen conditionally to Intra TMP fusion flag

## Slide 5: Simulation results

## Slide 6: Conclusion
3 aspects proposed to improve Intra TMP
  HMVP-like merge BV candidates
  Increased maximum non-adjacent distance
  Separate CABAC context for LIC flag signaling
Coding gain in AI configuration with 102.4% EncT and 103.4% DecT
  AI : -0,08% / -0,07% / -0,03% (Y / Cb / Cr)
Propose to study in EE2, targeting reduced runtime increase vs anchor