## Slide 1: Proposal of scalable hevc initial test model
Y. Ye (InterDigital), A. Fuldseth (Cisco), P. Yin (Dolby), Chunhui Cui (ASTRI)
11th JCT-VC meeting, Oct. 2012

## Slide 2: Proposed Initial Test Model for Scalable HEVC
HM6.1 based available now
  HM8.1 based available soon
Minimal change to enhancement layer codec
  Change limited within high level syntax
  No change to EL block level operations
  No change to EL prediction structure
Use only base layer texture prediction
  Only one coding tool: base layer reconstruction is upsampled by fixed upsampling filters and used as an additional reference picture for enhancement layer coding.
Picture by picture two layer encoding and decoding.
Provide tools for memory leak check and bitstream extractor.

## Slide 3: Benefits
Small changes on HM and easy to understand.
Clean to be used as a starting point for further development.
Base layer coding information is ready for implementing block level coding tools.
Easily extended to multiple standard scalability, such as HEVC, H.264/AVC, MPEG-2.
Convenient for future development and debugging, with tools of memory leak check and bitstream extractor

## Slide 4: Performance
 | All Intra HEVC 2x |  |  | All Intra HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | 2.8% | 13.4% | 13.7% |  |  | 
Class B | 1.5% | 12.2% | 12.6% | 0.3% | 8.9% | 9.8%
Overall | 2.2% | 12.8% | 13.2% | 0.3% | 8.9% | 9.8%
 | 2.2% | 12.9% | 13.5% | 0.3% | 7.8% | 7.2%
 | Random Access HEVC 2x |  |  | Random Access HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | 7.7% | 18.4% | 19.5% |  |  | 
Class B | 5.5% | 13.5% | 15.1% | 4.7% | 12.1% | 14.2%
Overall | 6.6% | 15.9% | 17.3% | 4.7% | 12.1% | 14.2%
 | 6.6% | 15.8% | 17.2% | 4.7% | 12.0% | 14.0%
 | Hybrid vs HEVC 2x |  |  | Hybrid vs HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | 7.5% | 16.7% | 17.8% |  |  | 
Class B | 4.6% | 12.2% | 13.7% | 3.9% | 9.7% | 11.3%
Overall | 6.0% | 14.5% | 15.7% | 3.9% | 9.7% | 11.3%
 | 6.0% | 14.4% | 15.7% | 3.9% | 9.6% | 11.2%
 | Hybrid vs AVC 2x |  |  | Hybrid vs AVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | 7.5% | 16.7% | 17.8% |  |  | 
Class B | 4.6% | 12.2% | 13.7% | 3.9% | 9.7% | 11.3%
Overall | 6.0% | 14.5% | 15.7% | 3.9% | 9.7% | 11.3%
 | 6.0% | 14.4% | 15.7% | 3.9% | 9.6% | 11.2%
 | Random Access HEVC SNR |  |  |  |  | 
 | Y | U | V |  |  | 
Class A+ | 4.7% | 15.1% | 16.8% |  |  | 
Class B | 5.0% | 13.8% | 17.7% |  |  | 
Overall | 4.9% | 14.4% | 17.2% |  |  | 
 | 4.9% | 14.3% | 17.0% |  |  | 
JCTVC-K0045 (benchmark) vs. JCTVC-K0034
Luma BD-rate gap
AI: 0.3-2.2%
RA: 4.7-6.6%
Hybrid: 3.9-6.0%
SNR: 4.9%