## Slide 1: Functional Block diagram of legacy HEVC decoder
Bitstream
CABAC
MV recon
MC
Spatial Pred
Pixel Recon
Inverse scan
IQ/IT
Loop filter
(De-blocking /SAO)
Decoded Picture Buffer
inter
Residues
intra
Rec Pic
Bitstream
Header parser (FW)

## Slide 2: Example HEVC implementation using one legacy decoder core for decoding multiple pictures in a single Layer bitstream
AU0
AU1
Decode AU0
Pipeline parameter configurations based on spatial resolution
Pipeline ramp-up/ramp-down
AU2
Single layer bitstream
Header parser (FW)
Legacy
Decoder core
time
Memory
LCU bins
Decode AU1
Decode AU2

## Slide 3: Example SHVC implementation using one legacy decoder core for decoding multiple pictures in a multi-layer bitstream
L0
L1
Decode L0
Decode L1
Decode L2
Pipeline parameter configurations based on spatial resolution
Pipeline ramp-up/ramp-down
L2
3-layer bitstream
Rec
Rec
IL-Ref
IL-Ref
Single legacy
Decoder core
External capability
time
Header parser (FW)
Memory
Re-sampler

## Slide 4: Repurposing legacy core for multi-layer extensibility
Header parser firmware capability to decode syntax extensions of multiple layers
Resampling capability
Legacy decoder core should be capable of decoding multiple layers
Firmware capability to support multiple spatial resolution changes across layers.
It is viable and easy to re-purpose one legacy HEVC decoder to decode Multiple layers