## Slide 1: Simplification of AMVP (JCT2-A0014)
Yoshiya Yamamoto Tomohiro Ikai
Tadashi Uchiumi
SHARP Corporation
JCT2 1st Meeting: Stockholm, SE, 16–20 July 2012

## Slide 2: Background
Conventional motion vector candidate construction for AMVP in HTM3.1
Inter-view motion prediction
Spatial (Left and Top) candidate vectors
Temporal candidate vector
Pruning between the first predictor and the second predictor
Remove MV candidates whose index is larger than 2
Final motion vector candidates
The construction process, especially Inter-view motion prediction, is complex.
However, no candidate motion vector derivation process could be avoided
in order to check the correspondence between idx and predictor.
Non-base view?
Y
N

## Slide 3: Proposal
We propose changes of Inter-view motion prediction and pruning.
Inter-view motion prediction
or Zero candidate vector
Spatial (Left and Top) candidate vectors
Temporal candidate vector
Pruning between the spatial candidate vectors
Remove MV candidates whose index is larger than 2
Final motion vector candidates
Zero vector is added to candidate list, when the first predictor is not available.
→ Always the first predictor is available and it corresponds to idx=0.
Pruning between the spatial candidate vectors (not first and second predictor).
→ The first predictor is independent from other predictor.
⇒Unnecessary candidate vector derivation process could be avoided.
e.g. if idx > 0, Inter-view motion prediction could be skipped.
⇒Candidate motion vector derivation process except Inter-view motion prediction is same as HM6.1
Non-base view?
Y
N
Same as HM6.1

## Slide 4: Experimental Result
BD-rate:
About 0.0 % loss
Runtime:
no significant difference
.
Results are cross checked by Sony (JCT2-Axxxx)
Sequences | video 0 | video 1 | video 2 | video only | synthesized only | Encoding time | Decoding time
Balloons | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 99.9% | 100.2%
Kendo | 0.0% | -0.1% | 0.0% | 0.0% | 0.1% | 100.4% | 99.6%
Newspapercc | 0.0% | -0.1% | -0.1% | 0.0% | 0.1% | 100.9% | 100.5%
GhostTownFly | 0.0% | -0.1% | 0.2% | 0.0% | 0.0% | 99.9% | 100.3%
PoznanHall2 | 0.0% | -0.2% | -0.5% | -0.1% | 0.0% | 100.0% | 99.4%
PoznanStreet | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 100.8% | 99.5%
UndoDancer | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 99.5% | 99.4%
1024x768 | 0.0% | -0.1% | 0.0% | 0.0% | 0.1% | 100.4% | 100.1%
1920x1088 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 100.0% | 99.7%
average | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 100.2% | 99.9%

## Slide 5: Conclusion
Motivation
  To avoid unnecessary candidate vector derivation process in AMVP
Proposal : Simplification candidate list construction
  Zero vector is added to candidate list, when the first predictor (Inter-view motion prediction) is not available
  Pruning between the spatial candidate vectors
Recommend
  - Propose to adopt in HTM and WD